## Slide 1: CCT Superconducting Magnets
17 Feb 2022
Kévin Pepitone

## Slide 2: Outline
Channel 5.65 x 2.31 mm2 – First prototype
Channel 6.15 x 2.31 mm2 – Future…

## Slide 3: Important values
Pitch of 5.8 mm
Walls are minimum 0.3 mm
148 turns min to magnetic length of 857 mm
Total coil length of 1064 mm (to be confirmed with the model)

## Slide 4: Channels explanation 5.65 x 2.31 mm2
Channel 5.65 x 2.31 mm2
0.05 mm gap cable-cable ; cable-former
Tolerance 0.05 mm
Cable 1.08 mm diameter

## Slide 5: Jungle of numbers 5.65 x 2.31 mm2 – at cold
Inner former inner radius = 35 mm
Channel 5.65 x 2.31 mm2 cable is 1.08 mm
Rcoil 1 inner = Inner former inner radius + 2.85 mm = 37.85 mm
Rcoil 1 outer = Rcoil 1 inner + Tcoil (= 5.65) = 43.5 mm
Outer former inner radius = Rcoil 1 outer + T former gap (= 0.7) = 44.2 mm
Rcoil 2 inner = Outer former inner radius + 2.85 mm = 47.05 mm
Rcoil 2 outer = Rcoil 2 inner + Tcoil (= 5.65)= 52.7 mm
Rsupport inner = Rcoil 2 outer + T former gap (= 0.7) = 53.4 mm
Rsupport outer = Rsupport inner + Tsupport (= 18.15 mm) = 71.55 mm
Ryoke inner = Rsupport outer + Tyoke gap (= 1.6 mm) = 73.15 mm
Ryoke outer = 237.0 mm
Tilt = 30 deg

## Slide 6: Jungle of numbers 5.65 x 2.31 mm2 - CATIA
Aluminum shrinks 4 mm/m
Iron shrinks 2mm/m
Inner former inner radius = 35.15 mm
Channel 5.65 x 2.31 mm2 cable is 1.08 mm
Rcoil 1 inner = Inner former inner radius + 2.85 mm = 38.00 mm
Rcoil 1 outer = Rcoil 1 inner + Tcoil (= 5.65) = 43.65 mm
Outer former inner radius = Rcoil 1 outer + T former gap (= 0.7) = 44.35 mm
Rcoil 2 inner = Outer former inner radius + 2.85 mm = 47.25 mm
Rcoil 2 outer = Rcoil 2 inner + Tcoil (= 5.65)= 52.9 mm
Rsupport inner = Rcoil 2 outer + T former gap (= 0.7) = 53.6 mm
Rsupport outer = Rsupport inner + Tsupport (= 18.25 mm) = 71.85 mm
Ryoke inner = Rsupport outer + Tyoke gap (= 1.6 mm) = 73.45 mm
Ryoke outer = 237.5 mm
Tilt = 30 deg

## Slide 7: View 5.65 x 2.31 mm2

## Slide 8: Channels explanation 6.15 x 2.31 mm2
Channel 6.15 x 2.31 mm2
0.05 mm gap cable-cable ; cable-former
0.5 mm on the top of the channel for more cable
Tolerance 0.05 mm
Cable 1.08 mm diameter

## Slide 9: Jungle of numbers 6.15 x 2.31 mm2 – at cold
Inner former inner radius = 35 mm
Channel 6.15 x 2.31 mm2 cable is 1.08 mm
Rcoil 1 inner = Inner former inner radius + 2.35 mm = 37.35 mm
Rcoil 1 outer = Rcoil 1 inner + Tcoil (= 6.15) = 43.5 mm
Outer former inner radius = Rcoil 1 outer + T former gap (= 0.7) = 44.2 mm
Rcoil 2 inner = Outer former inner radius + 2.35 mm = 46.55 mm
Rcoil 2 outer = Rcoil 2 inner + Tcoil (= 6.15)= 52.7 mm
Rsupport inner = Rcoil 2 outer + T former gap (= 0.7) = 53.4 mm
Rsupport outer = Rsupport inner + Tsupport (= 18.15 mm) = 71.55 mm
Ryoke inner = Rsupport outer + Tyoke gap (= 1.6 mm) = 73.15 mm
Ryoke outer = 237.0 mm
Tilt = 30 deg

## Slide 10: Jungle of numbers 6.15 x 2.31 mm2 - CATIA
Aluminum shrinks 4 mm/m
Iron shrinks 2mm/m
Inner former inner radius = 35.15 mm
Channel 6.15 x 2.31 mm2 cable is 1.08 mm
Rcoil 1 inner = Inner former inner radius + 2.35 mm = 37.50 mm
Rcoil 1 outer = Rcoil 1 inner + Tcoil (= 6.15) = 43.65 mm
Outer former inner radius = Rcoil 1 outer + T former gap (= 0.7) = 44.35 mm
Rcoil 2 inner = Outer former inner radius + 2.40 mm = 46.75 mm
Rcoil 2 outer = Rcoil 2 inner + Tcoil (= 6.15)= 52.90 mm
Rsupport inner = Rcoil 2 outer + T former gap (= 0.7) = 53.6 mm
Rsupport outer = Rsupport inner + Tsupport (= 18.15 mm) = 71.85 mm
Ryoke inner = Rsupport outer + Tyoke gap (= 1.6 mm) = 73.45 mm
Ryoke outer = 237.5 mm
Tilt = 30 deg

## Slide 11: View 6.15 x 2.31 mm2
70.4 mm at warm

## Slide 12: Jungle of numbers 5.65 x 2.31 mm2 – at cold
1 - Inner former inner radius = 35 mm
Channel 5.65 x 2.31 mm2 cable is 1.08 mm
2 - Rcoil 1 inner = Inner former inner radius + 2.85 mm = 37.85 mm
3 - Rcoil 1 outer = Rcoil 1 inner + Tcoil (= 5.65) = 43.5 mm
4 - Outer former inner radius = Rcoil 1 outer + T former gap (= 0.7) = 44.2 mm
5 - Rcoil 2 inner = Outer former inner radius + 2.85 mm = 47.05 mm
6 - Rcoil 2 outer = Rcoil 2 inner + Tcoil (= 5.65)= 52.7 mm
7 - Rsupport inner = Rcoil 2 outer + T former gap (= 0.7) = 53.4 mm
Rsupport outer = Rsupport inner + Tsupport (= 18.15 mm) = 71.55 mm
Ryoke inner = Rsupport outer + Tyoke gap (= 1.6 mm) = 73.15 mm
Ryoke outer = 237.0 mm
Tilt = 30 deg
1
2
3
4
5
6
7