## Slide 1: High Power RF Solid State Amplifiers at FREIA
Dragos Dancila, Long Hoang Duc, Magnus Jobs, Vitaliy Goryashko, Anders Rydberg, Jörgen Olsson, Roger Ruber and Tord Ekelöf
Oct. 4 – meeting with Scandinova
FREIA Laboratory, Uppsala University

## Slide 2: RF Source Development - FREIA
Testing prototype superconducting accelerating cavities (26 SC in final LINAC), cryomodules and high power RF stations
  High power RF stations at ESS specifications 352.21 MHz, 400 kW, 14 Hz, 3.5 ms, 200 kHz bandwidth
Uppsala University
ESS - Lund

## Slide 3
FREIA Uppsala
Cryogenics
RF Power Stations
Horizontal Cryostat
400 kW 3.5 ms pulses at 14Hz
Dual TH595 tetrodes
Load pull
Liquid Nitrogen
Helium liquefaction (150 l/h)
2000 l storage dewar
Operating at 1.8 to 4.5 K
16 mbar pressure
Operating at 352.21 MHz
Q > 109
Operating gradient 9 MV/m
Spoke Cavity
Closed-loop LLRF system
Cryogenics control
Control System

## Slide 4
400kW RF Stations
Tetrode based (Dual TH595)
400 kW 3.5 ms pulses at 14Hz
20 kV 40 A anode power supplies
Class AB
Cost Efficient/Reliability
Efficiency a key-parameter

## Slide 5
RF Power Station – SSA
400kW
200kW
No presurization and ferrite dummy loads
Power Distribution at 3 levels
  Half height WR2300: 400kW
  6-1/8 inch, 50  coax: 200 kW
  7/8 inch, 50  coax: 10 kW
Pre amp. Efficiency: 50 - 55 % (class AB)
Amp. Efficiency > 67 % (class AB)
TH 595

## Slide 6
AN10967 is a demo board designed and manufactured by NXP for the BLF578 LDMOS transistor.
push-pull configuration, class AB
delivering 1000 W in CW
  Max efficiency: 70%
  Gain: 20 dB
  Highest temp spot: 145C (15l/min water)
SSA research: collaboration with NXP(now Ampleon) and ESRF

## Slide 7: 1kW level Hot S-parameters measurements (pulsed)

## Slide 8: 1kW level Hot S-parameters measurements (pulsed)
R1
R2
A
B
S1
S2
S3
reference planes,
calibration planes
bidirectional coupler
27 dB
bidirectional coupler
50 dB
dummy load
150 W
circulator
100 W
pre-amp.
50 dB
att.
25 dB
att.
25 dB
att.
0 dB
att.
30 dB
-10 dBm
40 dBm
60 dBm
10 dBm
-20 dBm
60 dBm
40 dBm
60 dBm
40 dBm
13 dBm
-12 dBm
20 dBm
-40 dBm
-40 dBm
<40 dBm
att.
10 dB
<20 dBm
<10 dBm
10 dBm
10 dBm
<-10 dBm
<-35 dBm
SSA module
20 dB
<-40 dBm
-70 dBm

## Slide 9: 1kW level Hot S-parameters measurements (pulsed)
Using Hot S-parameters measurements we can characterize the output impedance at different output power levels.
The impedance is changing quite dramatically with the output power and this needs to be taken in to account for power combination.
(BLF578 measurements realized in pulsed mode with ESS parameters)
@ 352 MHZ

## Slide 10
Tested in pulsed mode with ESS characteristics (14 Hz, 3.5 ms) delivering up to 1300 W.
  BLF188XR - excellent ruggedness
  Max efficiency: 71%
  Gain: 19 dB (at 1.5 dB comprsession )
  Highest temp spot: 30 ⁰C (15l/min water)
  Excellent nonlinear behavior: second harmonic at -34dBc - no balun
SSA development at UU: single ended RF power amplifier – 1250 W and 70% efficiency

## Slide 11
Single ended RF power amplifier – 1250 W and 70% efficiency – 8 amplifiers for 10 kW demonstrator
quiescent drain current, IDq=0.1 A and drain voltage, VDS=50 V.
temperature rises for only few degrees, to about 30⁰C
Hot S-parameters measured at different output power at 352MHz

## Slide 12: 10 kW – SSA demonstrator
8 x 1.25 kW
capacitor bank
Combiners
Planar and WG
Monitoring circuits:
drain voltage
drain current
temperature

## Slide 13: 10 kW amplifier under construction

## Slide 14: Drain efficiency and phase of the 8 modules of the 10 kW amplifier demo
A small variation in both gain (< 0.5 dB) and phase (< 5⁰) is measured for the 8 modules of the 10 kW demonstrator.
Efficiency is around 70% at 1250 W (pulsed conditions 14 Hz, 3.5 ms)
Phase measurements performed using the hot S-parameters set-up.

## Slide 15: 10 kW 352 MHz amplifier
quarter wave type splitter/combiner
amplifier
8 modules
pre-amplifier #2
1 module
pre-amplifier #1
Gysel type splitter/combiner
* splitting & combination losses : 0,72 dB

## Slide 16: Spread among the 8 amplifiers
Power combination losses are reduced at high power levels due to the good balance among the 8 amplifiers.

## Slide 17: 8:1 λ/4 splitter/combiner
RL is at -41 dB level
we can deduce the RL of the combiner at -32 dB
1:8 splitter connected to 8 loads.
Circulator is used to measure RL

## Slide 18: 8:1 λ/4 splitter/combiner
RL is at -28 dB level
considering 1:8 splitting/combination
we can deduce the RL of the combiner at -17 dB
higher RL due to slightly phase and amplitude imbalances
1:8 splitter connected with circulators
to the 8:1 combiner
Measured IL 0.93 dB
(with cables 0.3 dB and circulator 0.2 dB)
we deduce the
splitter/combiner
IL = 0.2 dB

## Slide 19: Gysel Combiner
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | -21* | -24.7 | -23.7 | -24.2 | -24.1 | -23.7 | -23.4 | -22.7
2 |  | -24* | -27.5 | -26.8 | -26.3 | -24.8 | -24.9 | -23.6
3 |  |  | -21* | -26.4 | -27.3 | -25.2 | -24.9 | -23.3
4 |  |  |  | -23* | -30.6 | -27.1 | -26.1 | -24.1
5 |  |  |  |  | -25* | -26.2 | -26.5 | -24.2
6 |  |  |  |  |  | -25* | -27.1 | -23.7
7 |  |  |  |  |  |  | -26* | -24.9
8 |  |  |  |  |  |  |  | -26*
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Phase [deg] | 121 | 117 | 117 | 120 | 120 | 117 | 117 | 121
Mag [dB] | -9.24 | -9.32 | -9.24 | -9.16 | -9.19 | -9.27 | -9.29 | -9.15
Measured Performance
Aluminum Casing
High Integration Factor
Integrated Loads
Easily Reproducible
Average Insertion Loss (IL): 0.2dB
Peak Power (Tested): 10 kW

## Slide 20: Gysel Combiner
line coupling compensates parasitic coupling
Phase Balancing

## Slide 21: FREIA development: 100 kW non-resonant power combiner with door-knob couplers
3-1/8 inch
output connector
at 352.2 MHz
RL is 24 dB
i.e. 0.5% reflection
at 352.2 MHz
IL is 0.3 dB
i.e. 6% losses
7/16 inch input connector
h = 3 cm
D = 50 cm
can handle
1 MW pulsed
V.A. Goryashko, D. Dancila, A. Rydberg, R. Yogi & R. Ruber (2014): A megawatt
class compact power combiner for solid-state amplifiers, Journal of Electromagnetic Waves and Applications, DOI: 10.1080/09205071.2014.962187
Notes: Measured parameters agree very well with the design values.
The combiner is broadband.

## Slide 22: Collaboration
Power splitting +
Power combiner
LLRF and control system
RF modules
(new transistors
new packaging
intelligent modules)
Connectors
RF + DC + water
(Capacitor tank)
ACDC convertors +
power supply
Water cooling system
(thermal aspects)
Business perspective:
commercialisation
distribution

## Slide 23
Strategy for power combining – v1
4 x 12
1.2 meter
120 kW
480 kW
10 kW tile
8 SSA modules
Gysel combiner
& splitter 8:1
400 kW station
with major components developed at FREIA
300 W pre-amplifier
1 SSA module
1 SSA 25 W amplifier
Standard WR 2300 for high power combining; broadband design, ultra high power handling capability;
high isolation to avoid the need for circulators at each input port

## Slide 24
10 kW tile
8 SSA modules
Gysel combiner
& splitter 8:1
300 W pre-amplifier
1 SSA module
1 SSA 25 W amplifier
40 kW
Quarter wave combiner 4:1
(see Legnaro 4-ways)
480 kW
Coaxial combiner 12:1
12 x
12 x 4
Strategy for power combining – v2
0,6 meter
400 kW station
with major components developed at FREIA

## Slide 25
10 kW tile
8 SSA modules
Gysel combiner
& splitter 8:1
300 W pre-amplifier
1 SSA module
1 SSA 25 W amplifier
400 kW
Coaxial combiner 40:1
40 x
Strategy for power combining – v3
0,6 meter
400 kW station
with major components developed at FREIA

## Slide 26: Conclusions
A single ended high RF power Solid-State Amplifier was successfully designed and manufactured producing 1.25 kW with an efficiency of 70% at 352 MHz, in ESS operational mode (14 Hz, 3.5 ms). This is a simple and robust design minimizing manufacturing cost towards mass fabrication and industrialization. Joint UU - Ampleon application note.
Measurement methods have been developed and implemented allowing hot S-parameters measurements.
A small variation in both gain (< 0.5 dB) and phase (< 5⁰) is measured for the 8 modules of the 10 kW demonstrator under construction at FREIA.
A 10 kW demonstrator, using 8 modules is finalized at FREIA. Monitoring circuits and power combiners are under development.
Strategy for the near future: highly efficient class E amplifiers at 100 MHz for GE’s cyclotron nucleotides production – Eurostars application; possibly 400 MHz (for CERN crab cavity tests); development and amplifier design of Latch-Free LIGBT/IGBT high power transistors at UU – Comheat AB (compared with LDMOS, saturation current is presently 15-30 times higher).
Joint UU - Ampleon application note on BLF188XR’s site