## Slide 1: Gersemi Cryostat
Mechanical analysis
ACS – P. Duthil
2nd Follow-up meeting – 25th October 2016

## Slide 2: Vertical cryostat Geometry 1/2
CAD geometry
Ports
40
8
60
4

## Slide 3: Geometry 2/2
FEM geometry
  Mesh elements
    Coloured: shells elements (coloured by thicknesses expressed in mm)
    Grey: solid elements
Two thickness considered for the bottom dish end:
6 mm: min. measured thickness;
8 mm: nominal thickness

## Slide 4: Material 1/3
Model
AISI 304L (1.4306 / X2CrNi19-11)
E = 190 000 Mpa
= 0.305
ρ = 7 900 kg/m3

## Slide 5: Material 2/3
Pressure Equipment Directive 2014/68/EU
  EN 10028-7
    Proof strength: Rp1,0 = 240 Mpa @ room T° (= pressure test T°)
    Tensile strength: Rm  500 Mpa @ room T° (= pressure test T°)
    Elongation after fracture: A  45 %
  EN 13445-3 (p35)
 fd 304L = 166 MPa
 ftest 304L  250 MPa

## Slide 6: Material 1/3
Pressure Equipment Directive 2014/68/EU
  EN13445-3
p565
for the membrane stresses
(=neutral fibre of the shell elements):
  - for areas away from the shape discontinuities:
  f = fd (cf. §2.2 for fd)  smax membrane < 166 MPa
  - for areas near shape discontinuities:
  f = fd x 1.5  smax membrane < 249 MPa
for the bending stresses: f = fd x 1.5
 smax bending < 249 MPa
 for normal pressure operation (i.e. for MAWP = Ps):

## Slide 7: Internal pressure
Pressure test of the dewar
  EN13458:
    Ptest = 1.43 x (Ps + 0.1) = 1.43 x (0.4 + 0.1) = 0,715 Mpa with Ps = MAWP
    For the pressure test: no vacuum inside the vacuum vessel but atmospheric pressure around the dewar  pressure of 0.615 Mpa applied on the inner surfaces of the dewar
  Calculated stresses in solid elements:

## Slide 8: Internal pressure
Pressure test of the dewar
  Calculated stresses in shell elements:
6 mm thick bottom dish end:
Membrane stress
Membrane
+ bending stress
8 mm thick bottom dish end:
Membrane stress
Membrane
+ bending stress

## Slide 9: Internal pressure
Nominal operation of the dewar
  Pressure only
    Ps = MAWP = 4 barg
    Vacuum inside the vacuum vessel
     pressure of 0.5 Mpa applied on the inner surfaces of the dewar
  Stresses
  in solid elements:
Membrane stress
Membrane + bending stress
  Stresses in shell elements:
6 mm thick
bottom dish end:

## Slide 10: Internal pressure
Nominal operation of the dewar
  Stresses
  in solid elements:
Membrane stress
Membrane + bending stress
  Stresses in shell elements:
8 mm thick
bottom dish end:

## Slide 11: Internal pressure
Nominal operation of the dewar
  Pressure + Mass of the magnet
    Ps = MAWP = 4 barg
    60 000 N applied on the lambda set
  Stresses in all elements:
6 mm thick
bottom dish end:
8 mm thick
bottom dish end:

## Slide 12: Valve Box Geometry 1/1
FEM geometry
  Mesh elements
    Coloured: shells elements (coloured by thicknesses expressed in mm)
    Grey: solid elements
Thicknesses of some solid elements:
Top lid: 25 mm
Bottom lid: 25 mm
Flanges: 25 mm

## Slide 13: Material 1/3
Model
AISI 304L (1.4306 / X2CrNi19-11)
E = 190 000 Mpa
= 0.305
ρ = 7 900 kg/m3

## Slide 14: External pressure
Linear buckling due to pressure forces only
    gravity and masses are not taken into account here (nor the reaction of the support pods on the floor – see report 1)
 First linear buckling mode for a critical pressure of 0,82 MPa

## Slide 15: Thank you for your attention
CSP12
28 Novembre 2014