## Slide 1: Status of ESS neutrino Super Beam (ESSνSB)
Marcos Dracos
on behalf of the ESSνSB/EuroNuNet project

## Slide 2: Overview
The European Spallation Source
The neutrino beam using the ESS facility
The needed ESS linac modifications
Ongoing activities
Physics performance
EU support

## Slide 3: European Spallation Source

## Slide 4: European Spallation Source
under construction since 2014
(~1.85 B€ facility)

## Slide 5: ESS proton linac
The ESS will be a copious source of spallation neutrons.
5 MW average beam power.
125 MW peak power.
14 Hz repetition rate (2.86 ms pulse duration, 1015 protons).
Duty cycle 4%.
2.0 GeV protons
  up to 3.5 GeV with linac upgrades
>2.7x1023 p.o.t/year.
Linac ready by 2023 (full power)

## Slide 6: What kind of neutrino beam can we extract using this linac?
by doubling the linac pulsing rate…
p
π
ν
decay tunnel
proton beam
target
hadrons
hadronic collector
(focusing)
Detector
physics
⨂B
conventional neutrino (super) beam
production of a powerful neutrino beam

## Slide 7: ESSνSB ν energy distribution (without optimisation)
at 100 km from the target and per year (in absence of oscillations)
neutrinos
anti-neutrinos
almost pure νμ beam
small νe contamination which could be used to measure νe cross-sections in a near detector

## Slide 8: CP Violating Observables (νμ→νe)
matter effect
⇒ accessibility to mass hierarchy
⇒ very long baseline
(small in our case)
Non-CP terms
CP violating
≠0 ⇒ CP Violation
be careful, matter effects also create asymmetry
atmospheric
solar
interference

## Slide 9: Neutrino Oscillations with "large" θ13
more sensitivity at 2nd oscillation max.
for small θ13 1st oscillation maximum is better
for "large" θ13 1st oscillation maximum is dominated by atmospheric term
CP interference
CP interference
solar
solar
atmospheric
atmospheric
θ13=1º
θ13=8.8º
(arXiv:1110.4583)
L/E
L/E
1st oscillation max.: A=0.3sinδCP
2nd oscillation max.: A=0.75sinδCP
(see arXiv:1310.5992 and arXiv:0710.0554)
P(νμ→νe)
2nd oscillation maximum
θ13=8.8º
("large" θ13)
dCP=-90
dCP=0
dCP=+90
L/E

## Slide 10: Can we go to the 2nd oscillation maximum using our proton beam?
Yes, if we place our far detector at around 500 km from the neutrino source.
MEMPHYS like Cherenkov detector
(MEgaton Mass PHYSics studied by LAGUNA)
Neutrino Oscillations (Super Beam, Beta Beam)
Proton decay
Astroparticles
Understand the gravitational collapsing: galactic SN ν
  Supernovae "relics"
Solar Neutrinos
Atmospheric Neutrinos
500 kt fiducial volume (~20xSuperK)
Readout: ~240k 8” PMTs
30% optical coverage
(arXiv: hep-ex/0607026)

## Slide 11: Neutrino spectra
540 km (2 GeV), 10 years
below ντ production, almost only QE events
neutrinos
anti-neutrinos
2 years
8 years
δCP=0

## Slide 12: 2nd Oscillation max. coverage
2nd oscillation max.
well covered by the ESS neutrino spectrum
1st oscillation max.

## Slide 13: ESS Linac modifications to produce a neutrino Super Beam
European Spallation Source Linac

## Slide 14: How to add a neutrino facility?
The neutron program must not be affected and if possible synergetic modifications.
Linac modifications: double the rate (14 Hz → 28 Hz), from 4% duty cycle to 8%.
Accumulator (C~400 m) needed to compress to few μs the 2.86 ms proton pulses, affordable by the magnetic horn (350 kA, power consumption, Joule effect)
  H- source (instead of protons),
  space charge problems to be solved.
~300 MeV neutrinos.
Target station (studied in EUROν).
Underground detector (studied in LAGUNA).
Short pulses (~μs) will also allow DAR experiments (as those proposed for SNS) using the neutron target.

## Slide 15
Required modifications of the ESS accelerator architecture for ESSνSB

## Slide 16
Preparing the ESS linac for operation at 10 MW with a 8% duty cycle and 28 Hz pulsing
For the medium-beta elliptical-cavity part ESS is planning to use tetrodes. Thales has developed a new screen grid with graded wire thickness making operation at 10 % duty cycle possible.
The picture shows the cryostat and test bunker at the FREIA Lab in Uppsala where a first prototype of the ESS 352 MHz spoke accelerating cavity is currently under test at 14 Hz and later on will be tested at 28 Hz.
FREIA Lab, Uppsala

## Slide 17
Accumulation Ring
The accumulator is needed to compress to less than few μs the 2.86 ms proton pulses, affordable by the magnetic horn (350 kA, power consumption, Joule effect), but also keeping a reasonable size of the ring.
Baseline: single-ring accumulator
  Current studies give a 376 m circumference accumulator ring 1.32μs.
  1 ring leads to a very large space–charge tune–shift of about 0.75.
Option: 4 superposed rings located in the same tunnel,
  Each ring receives 1/4 of the bunches during the multi–turn injection,
  This will lead to a reduction of the tune shift to the level of around 0.2 (acceptable for the 2.86 ms storage time),
  There has to be enough space between the bunches in the bunch train from the linac to permit the beam distribution system to inject from one ring to the next one,
  Experience already exists from the CERN PS Booster of using 4 superimposed rings with the aim to avoid high space charge effects.
Injection
Extraction
Collimation
RF
Lattice

## Slide 18: Mitigation of high power effects (4-Target/Horn system for EUROν Super Beam)
Packed bed canister in symmetrical transverse flow configuration (titanium alloy spheres)
Helium Flow
4-target/horn system to mitigate the high proton beam power (4 MW) and rate (50 Hz)
target inside the horn
proton beam switchyard

## Slide 19: General Layout of the target station (copied from EUROν DS)
Split Proton Beam
Neutrino Beam Direction
Collimators
Horns and Targets
Decay Volume
(He, 4x4x25 m3)
Beam Dump
8 m concrete
Horn Support Module
Shield Blocks

## Slide 20: Physics Performance
little dependence on mass hierarchy (not so long baseline),
δCP coverage at 5 σ C.L. up to 60%,
δCP accuracy down to 6° at 0° and 180° (absence of CPV for these two values),
not yet optimized facility.

## Slide 21: Systematic errors and exposure
for ESSnuSB systematic errors see 1209.5973 [hep-ph] (lower limit "default" case, upper limit "optimistic" case)
P5 requirement: 75% at 3 σ
10 years
20 years
(courtesy P. Coloma)
High potentiality
5% syst.
7.5% syst.

## Slide 22: Which baseline?
~60% δCP coverage at 5 σ C.L.
>75% δCP coverage at 3 σ C.L.
systematic errors: 5%/10% (signal/backg.)
CPV (Nucl. Phys. B 885 (2014) 127)
Zinkgruvan
Garpenberg

## Slide 23: The Garpenberg mine (115 km from Uppsala)

## Slide 24: The Garpenberg mine
Distance from ESS Lund 540 km
Depth 1232 m
Truck access tunnel
Hoist shaft free to use by ESSnuSB
Rock-engineering prospection and studies in the Garpenberg-mine granite-zones
The owner of the Garpenberg mine, Boliden AB, has signed an MoU with Uppsala University, permitting agents of the University to access and make investigation in the Garpenberg mine.

## Slide 25: Garpenberg Research Infrastructure Project for Neutrinos (GRIPnu)

## Slide 26
Muons of average energy ~0.5 GeV at the level of the beam dump (per proton)
2.7x1023 p.o.t/year
ESS neutrino and muon facility
ESS proton driver
p decay
nm or nm
Decay
channel or ring
Front end
Cooling
Storage
ring
RCS
acceleration
Collider
ring
RLA
acceleration
Neutrons to ESS
Protons dump
Test Facility
Short
Baseline
Detector
Long
Baseline
Detector
Short
Baseline
Detector
Long
Baseline
Detector
m+ or m-
nm + ne
ne + nm
Muon Collider
nuSTORM
Neutrino
Factory
ESSnuSB
Accumulator
μ+ μ-
→ ←
more than 4x1020 μ/year from ESSS compared to 1014 μ used by all experiments up to now (1018 μ for COMET in the future).

## Slide 27: Muons at the level of the beam dump
x (cm)
muons at the level of the beam dump
(per proton)
y (cm)
x (cm)
4.2x1020 μ/year
(16.3x1020 for 4 m2)
4.1x1020 μ/year
2.7x1023 p.o.t/year
muons/proton
<Eμ>~0.46 GeV
<Lμ>~2.9 km
10-3
input beam for future 6D m cooling experiments (for muon collider),
good to measure neutrino x-sections (νμ, νe) around 200-300 MeV using a near detector,
low energy nuSTORM,
Neutrino Factory,
Muon Collider.

## Slide 28: Muons at ESS
Carlo Rubbia
Seminar at Uppsala
(PIC: Parametric Resonance Cooling of muons)

## Slide 29: ESS under construction
September 2014
target monolith
Linac
Beam Line Gallery

## Slide 30: ESS construction site
p
n
ν
H-
May 2017

## Slide 31: ESSνSB at the European level
COST application for networking has been succeeded: CA15139 (2016-2019)
  EuroNuNet : Combining forces for a novel European facility for neutrino-antineutrino symmetry violation discovery (http://www.cost.eu/COST_Actions/ca/CA15139)
  Major goals of EuroNuNet:
    to aggregate the community of neutrino physics in Europe to study the ESSνSB concept in a spirit of inclusiveness,
    to impact the priority list of High Energy Physics policy makers and of funding agencies to this new approach to the experimental discovery of leptonic CP violation.
  13 participating countries (network still growing).
specific session this afternoon
(room IV)

## Slide 32: ESSνSB at the European level
A H2020 EU Design Study has been submitted end of March (Call INFRADEV-01-2017)
Title of Proposal: Discovery and measurement of leptonic CP violation using an intensive neutrino Super Beam generated with the exceptionally powerful ESS linear accelerator
Duration: 4 years
Total cost: 4.7 M€
Requested budget: 3 M€
15 participating institutes from 11 European countries including CERN and ESS
6 Work Packages
Decision: end of August
ESSνSB
BENE (2004-2008)
ISS (2005-2007)
EUROν (2008-2012)
LAGUNA (2008-2010)
LAGUNA-LBNO (2010-2014)
COST Action CA15139 (2015-2019)

## Slide 33: Design Study ESSνSB
approved!

## Slide 34: Design Study ESSνSB (2018-2021)
The Grant Agreement has to be signed before the 23rd of November 2017.
ESSνSB will start engaging postdocs soon.
very supportive letter from ESS director
partners: IHEP, BNL, SCK•CEN, SNS, PSI, RAL

## Slide 35: Conclusion
Significantly better CPV sensitivity at the 2nd oscillation maximum.
The European Spallation Source Linac will be ready in less than 8 years (5 MW, 2 GeV proton beam by 2023).
ESS will have enough protons to go to the 2nd oscillation maximum and increase its CPV sensitivity.
CPV: 5 σ could be reached over 60% of δCP range (ESSνSB) with large potentiality.
Large associated detectors have a rich astroparticle physics program.
Rich muon program.
COST network project CA15139 supports this project.
The Design Study ESSνSB is approved and will start soon.

## Slide 36: Backup

## Slide 37: Possible locations for far detector
CERN
ESS
Kongsberg
Løkken
LAGUNA sites

## Slide 38: Systematic errors
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]

## Slide 39: δCP accuracy performance (USA snowmass process, P. Coloma)
for systematic errors see (7.5%/15% for ESSnuSB):
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]
arXiv:1310.4340 [hep-ex] Neutrino "snowmass" group conclusions
"default" column

## Slide 40: Comparisons

## Slide 41: δCP coverage
CPV (2 GeV protons)
"nominal"
x2
after 10 years
with 2 times more statistics
systematic errors (nominal values): 5%/10% for signal/background
more than 50% δCP coverage using reasonable assumptions on systematic errors