## Slide 1
UPPSALA UNIVERSITY GERSEMI
Project follow-up
Quality monitoring
Lery, 14-15/02/2017

## Slide 2: Quality monitoring
Existing documents
Dimensional control report
Cleaning control report
Thermal shock and leak test control report
Pressure test control report
PID check control report
Electrical insulation test control report
2-wire electrical resistance test control report
4-wire electrical resistance test control report
Between-wire insulation test control report
Objective: to increase the quality of delivered product to the customer
Why?
Limit post-delivery operations
How?
Advise the manufacturer to improve the production quality
Perform pre-shipment checks
When?
Milestones + workshop visits during production
What?
Compendium of control reports (cf. table)

## Slide 3: Quality monitoring: applications
Projects
Transfer Line L001(13/12/2016)
Inter Connection Box (13&15/12/2016)
Double Reheater (23/12/2016, 04/01/2017)
The control methodologies and the documents were used on the following projects (cf. table).
Improvement of the documents in collaboration with CD
Gain of experience
Following tasks:
Prepare compendium of control reports, dedicated to Vertical Cryostat and auxiliaries
Thermal shock and leak test

## Slide 4: Quality monitoring: sample of document (Thermal shock and leak test control report)
Référence (PCQ ou Spec.) : / Ref. (ITP or Tech. spec.) |  | PCQ 1721-1 §2.f |  | Ref. Outil de Contrôle : / Control tool reference |  |  |  | 
 |  |  |  | Ref. fuite étallon externe : / Calibrated leak Id. |  |  |  | 
Stade de fabrication / Fabrication stage |  |  | Cours d'assemblage / While building | 1 | Assemblage final / Final assembly | Autre : / Other |  | 
Méthode de test : / Control Methodology |  | Cocher / Select | Méthode / Methodology |  | Valeur de fuite max autorisée / Max. leak value allowed |  | Pression ou Vide / Press. or Vaccum | Manomètre / Mano Id.
Cas de test par jet / Case of test by spraying : Débit He / He flow rate > 10 l.min-1 /!\ Effectuer un choc thermique à l'azote sur les soudures avant leur He LT / Carry-out a nitrogen thermal choc on welds before the He LT /!\ |  |  | Par renniflage / Snifing |  |  |  | Phe = ……..barG | 
 |  |  | Au jet / Spraying |  | 5.10^(-9) mbar.l.s-1 |  | Pv < 5.10^(-2) mbarG | 
 |  |  | Par accumulation / Accumlating |  | 5.10^(-9) mbar.l.s-1 |  | Phe = ……..barG | 
 |  |  | Pression Helium / He pressure test |  | 5.10^(-9) mbar.l.s-1 |  | Phe = ……..barG, pendant …… min. | 
Repère de pièce ou soudure / Part or weld Ref. |  |  | Valeur mesurée / Measured Value |  | Conformité / Conformity | Commentaires / Comments |  | 
Plan / Drawing | Pièce ou Cahier de Soud. / Part or WB | Repère / Ref. |  |  |  |  |  | 
Personnel Qualifié / Qualified Operator |  |  |  |  | Client ou organisme Notifié / Client or NB |  |  | 
Date du PV / Date of the repport |  |  |  |  | Date de Validation / Validation Date |  |  | 
Signature / Visa |  |  |  |  | Signature / Visa |  |  |