## Slide 1: Gersemi Cryostat
Mechanical and cryogenic configurations
ACS – P. Bujard, J.P. Thermeau, F. Dieudegard, T. Junquera
3rd Follow-up meeting – 14th February 2017

## Slide 2: Outline
Cryogenic and mechanical Studies
Cryostat, valve box, liquid insert designs
Lambda Insert
Cryogenic schemes modifications
Simulator design

## Slide 3: Cryostat, valve box, liquid insert design
Mechanical design:
The mechanical designs of the cryostat, valve box, liquid insert are finalized,
The main CD mechanical drawings are checked.
Follow-up:
- Double re-heater : end of manufacturing and shipping in January 2017
- Liquid insert : manufacturing is started.

## Slide 4: Lambda Insert : several modifications
Magnet is around 5100kG
2 shorter Level Sensors
Shield design in one disc + external rib (as CD liquid insert)
Changes designed
  TopLid “bulked” (crane 7T)
Heat exchanger design ( SS304+copper)
Simplified Lambda-plate profile
flanges re-organised to clear central access
(racetrack clearance)
  More spares acces ?
  Still possible/nesseseary to add some acces holes ?

## Slide 5: Cryogenic schemes
The new cryogenic scheme and the nomenclature included the equipment modifications are available.
The modifications concerned :
  Cryostat thermal shield, new control valve to allow the end of the cooling without the end of the cooling of the valve box thermal shield : CV740 (valve installed on the body on the body of FT740)
  The vacuum gauge of the vacuum insert : PT080 and PT081 instead of PT070 and PT071
  Magnet insert, new electrical heaters : EH689AC associated with TT689AC
  Magnet insert, heat exchanger : HX683 instead of HX681.
  Simulator : a first version of the cryogenic scheme is available

## Slide 6: Simulator to test the valve box

## Slide 7: Simulator mechanical design
  Connections to Valve box
  Small dimensions in comparison with the cryostat size
  The main functions of the cryostat can be tested

## Slide 8: Simulator mechanical design
  Small LHe tank  40 l
  which can operate at 4K or 2K
  Thermal shield
  A loop to simulate the SHe circuit
  Vacuum gauge
  SHe electrical heater
  Cryogenic lines connected to the valve box cryogenic lines
  Vacuum vessel