## Slide 1: High Temperature High Power RF Loads
TIARA workshop
17. – 19. 06. 2013
M. Betz, F. Caspers,
S. Federmann

## Slide 2: Overview
Introduction
Two conceptional models of high temperature high power loads
Material studies: Coating materials
Conclusions

## Slide 3: Motivation
High power RF loads (but at low/moderate temperature) are commonly used in particle accelerators:
Travelling wave accelerating cavity
Standing wave accelerating cavity

## Slide 4: The problem Power dissipation in termination loads
Water-cooled termination loads in the tunnel
Average power dissipation in RL: 4 x 190.5 kW
Heat is not utilized and dissipated to the environment by heat exchangers on the surface
Annual:
  6.7 million kWh
  ~ 450 000 €
We assume: 0.067 € / kWh.
Which is the average energy cost for France in Nov. 2009
Source: http://www.energy.eu/#industrial
Distribution of the average (24 h)
Power dissipation per
Cavity (there are 4):
Σ = 254 kW
325 kW
Peak
Example: the CERN SPS
TL … transmission line
Rcu … copper losses
Beam … beam losses
RL … power in the termination loads

## Slide 5: First Idea
Recover energy directly before it is dissipated in the load
Problem: Extraction out of the transmission line has to be done somehow
The extracted RF energy has to be fed back into the grid
This problems were subject of the Master thesis of M. Betz

## Slide 6: Direct Energy Recovery concept Possible layout for the SPS
RF - Power splitter: 325 kW (peak) → 300 x 1 kW
300 x RF/DC modules
DC – Link: DC power of individual module outputs is combined
DC to AC (50 Hz): e.g., with commercial photopholtaik power converters
DC – power combination
(similar to solar cell arrays)
AC 50 Hz, fed to electric supply network

## Slide 7: Direct Energy Recovery concept Possible layout for the SPS
RF - Power splitter: 325 kW (peak) → 300 x 1 kW
300 x RF/DC Modules
DC – Link: DC power of individual module outputs is combined
DC to AC (50 Hz): e.g., with commercial photopholtaik power converters
Coaxial power splitter
DC – power combination
(similar to solar cell arrays)
AC 50 Hz, fed to electric supply network
Inner conductor
Outer
conductor
Capacitive coupling pin

## Slide 8: Requirements for a single RF/DC Module
fin = 200 MHz (+-2%), Pin = 1 kW
Good 50Ω input match (S11 <= -20 dB)
Failsafe operation: Failure of individual components shall not lead to disturbance of the SPS
No significant harmonic signals towards the input
4 resonant Rectifiers, 250 W each Narrowband matching network Circulator redirects input power if the rectifier fails
Requirement
Possible Solution

## Slide 9: Summary for this concept Solid State Energy Recovery
Rectifier with 2 x GS150TC25110 diodes
  Working frequency: 200 MHz
  Nominal power: 250 W
  Efficiency: > 85 %
  Harmonic radiation: - 30 dB
4 x RF/DC units = 1 kW module
300 x modules = Replacement for one SPS existing RF power load

## Slide 10: Next Idea
Looking at conventional loads and identifying limitations and potential for optimizations
Conventional RF power loads often produce cooling water at low pressure and moderate temperature (often below 50 °C)
  At this level, the energy is barely usable
It would be desirable to have cooling water with at least 80 °C - already foreseen for ESS. This can be done with selected conventional loads.
But > 150 °C and high pressure or maybe hot air at 600 - 800°C would even be better. Both media are technically usable (Domestic heating, Industrial process heat, Stirling engines, etc.)

## Slide 11: High Power High Temperature Loads
To adress the afore mentioned issues, two types of loads have been investigated:
  A waveguide loaded with silicon carbide (SiC) foam
  A ferrite coated stacked waveguide structure
Conceptional models for each version have already been built and preliminary measurements of their absorption properties look promising

## Slide 12: Air cooled RF load with ceramic foam
The solar energy absorber concept by I. Hischier [1] inspired us to this new kind of very high temperature air cooled RF load
[1] I. Hischier, Development of a pressurized receiver for solar-driven gas turbines, 2011 Diss. ETH 19723

## Slide 13: Air cooled RF load with ceramic foam
SiC foam is widely used in metal casting applications as a filter
Molten metal is guided through the foam to filter out impurities and to control fluid flow
Different shapes, sizes and porosities are commercially available
Maximum temperature for SiC: 1550 °C
http://www.hofmann-ceramic.de http://www.frank-landmesser.de

## Slide 14: Air cooled RF load with ceramic foam
This special ceramic foam is indeed a good microwave absorber and can be used in the design of an RF load in a similar way as the energy absorber in the design introduced in the solar high temperature structure by I. Hischier
Applying this concept to an RF load, would result in SiC foam embedded in a metal enclosure (ceramic NOT brazed to the enclosure)
This is the principle of using fire clay in the average oven

## Slide 15
Cross section of a Travelling wave structure
Ceramic foam with high RF losses
Metal enclosure at high temperature (800 °C)
Slightly pressurized air (<0.2 bar) at ambient temp.
Perforation serves as RF tight air inlet
Hot air
Thermal insulation
(rock wool)
An array of stainless steel pipes with ≈ 1 cm diameter serves as RF tight air outlet (honey-comb style RF-filter)
Standard waveguide
(e.g., WR-1150)
Air tight RF window (e.g., kapton foil)
RF wave
Tapering for
low RF-reflections
Length = 0.5 … 2 λ0
Height = 0.5 …1 λ0
Thin metal sheet to compensate thermal expansion
Air cooled RF load with ceramic foam

## Slide 16: Conceptional model A
Silicon carbide filled load

## Slide 17: Conceptional model A
First Results: Waveguide filled with SiC

## Slide 18: Another high temperature microwave load:
Some modern microwave ovens are equipped with a so called browning- or crisp-plate
Essentially a metal plate coated with a microwave absorbing material (ferrite) which can heat up to ≈ 200 °C
A proof of principle! High temperature loads based on ferrite do exist

## Slide 19: Plasma sprayed ferrite
We do not use tiles of solid ferrite brazed onto metal:
  The thermal expansion coefficient differs from its metal carrier
  The ferrite will get brittle and crack
ECCOSORB® MCS is based on ferrite powder in a rubber matrix. It is fairly elastic, thus brittleness is not an issue.
The ECCOSORB material is rated up to 177 °C

## Slide 20: Plasma sprayed ferrite
For higher temp., a better solution would be a very thin ferrite coating (150 - 300 μm)
The coating can be applied by plasma spraying [1]
Then the load could heat up to the curie temperature of the ferrite (can be > 300 °C)
[2]
[1] I. PREECE, C. W. D. ANDREWS, Plasma spraying of ferrites, JOURNAL OF MATERIALS SCIENCE 8 (1973) 964-967
[2] http://www.progressivesurface.com/newsArticle.php?id=25

## Slide 21: Conceptional model B
Ferrite load

## Slide 22: Conceptional model B
First Results: Stacked waveguide with Eccosorb material

## Slide 23: Material choices
  Plasma Sprayed Ferrite sample (provided by IOT Aachen)
  Painted Ferrite sample (provided by Shenzhen Cui Baolong Industry Co. Ltd.)
  Painted SiC sample (provided by Shenzhen Cui Baolong Industry Co. Ltd.)no. Ltd.)
  Commercial crisp plate (producer: Whirlpool)
  Ferrite loaded silicon rubber sample #1 (provided by Shenzhen Cui Baolong Industry Co. Ltd.) Ltd.)
  Ferrite loaded silicon rubber sample #2(provided by Shenzhen Cui Baolong Industry Co. Ltd.)aolong Industry Co. Ltd.)
  Eccosorb MCS (provided by Emerson & Cuming)
Tested samples - here equipped with the stripline for measurement
In order to find proper materials for coating the stacked waveguide structures, several material samples were measured according to their absorption properties:
1.
2.
3.
4.
5.
6.
7.

## Slide 24: Material choices
With ferrite (#1)
(#2)

## Slide 25: Conclusions
Direct energy recovery is a very promising concept providing a recovery efficiency of over 85%. However, due to the required volume and $$$ involved not feasible at the moment - this might change in the future!
An alternative load consisting of a silicon carbide foam in a waveguide would be able to provide pressurized hot air (up to 800°C) . First measurements of a dedicated conceptional model delivered encouraging results.
A conceptional model consisting of a waveguide incorporating coated absorber plates has also successfully been tested.
Different materials were investigated to find a suitable coating for a stacked structure. The most promising lead here is “crisp plate” technology which is readily available and rather cheap in production.

## Slide 26
Thanks for your attention!

## Slide 27
Additional slides

## Slide 28: Prototypes
Measurement setup
Iris to ensure weak coupling
waveguide

## Slide 29: Material choices
Measurement setup: