## Slide 1: High Energy Proton Synchrotrons
… by the example LHC
Erk Jensen, CERN
TIARA Workshop on RF Power Generation for Accelerators
17-19 June 2013
Ångström Laboratory, Uppsala, Sweden
Many thanks to T. Mastoridis , O. Brunner whose slides I took, and all the others in BE-RF who helped make this work!

## Slide 2: The LHC RF System
Two independent rings,
8 RF cavities per ring all installed at point4,
Klystrons and Cavity Controllers in a cavern ~150 m underground,
100kV, 40A (ex-LEP) power converter located at the surface,
Klystron modulators, fast protection systems in four HV bunkers,
Sixteen 330 kW klystrons + circulators + RF ferrite loads in UX45,
Power control system based on industrial PLCs, plus a fast Interlock protection system,
WR2300 HH WG distribution system to individual cavities,
LLRF for Cavity Controllers in two Faraday Cages,
Beam Control equipment in a surface building in SR4.
O. Brunner

## Slide 3: The LHC RF system
O. Brunner

## Slide 4: The Klystrons
Klystron power sweep CW @ 400.8 MHz
Pout
Pin
Operating point
≈ -1.5dB below saturation
Clamped (SWAP)
  1 klystron per cavity
    330 kW max (58 kV, 8.4 A)
    130 ns group delay (~ 10 MHz BW)
    CW gain 39 dB @ 200 kW, 36 dB @ 300 kW
    In operation ≈ 200 kW CW
    21 klystrons @ CERN, 16 in operation
    Klystrons had problems with boilers – now replaced
O. Brunner

## Slide 5: Circulators, Loads, WG’s
1 circulator per cavity
  330 kW max
  60 ns group delay
  Circulator equipped with temperature control system
    Affects the Qext of the cavity
1 RF ferrite load per circulator
  330 kW CW
  RF loads reflection < -28 dB
Wave guide system
  WR2300 HH
  Length: 15 to 30 meters
O. Brunner

## Slide 6: The Cavities
8 RF cavities per ring at 400.790 MHz:
  Super Conducting Standing Wave Cavities, single-cell, , 6 MV/m nominal
  Equipped with movable Main Coupler ()
  Mechanical Tuner range = 100 kHz
4 spare cavities assembled in a cryomodule + 1 spare cavity
more new spare cavities/cryomodule shall be built in the next years
O. Brunner

## Slide 7: Planned module swap
T. Mastoridis: Evian 2012

## Slide 8: LLRF System

## Slide 9: LHC performance 2012
S. Myers, EuCARD13

## Slide 10: RF Performance 2012: no limits
T. Mastoridis: Evian 2012

## Slide 11: Performance 2012: steps ahead
T. Mastoridis: Evian 2012

## Slide 12: Improvements
T. Mastoridis: Evian 2012

## Slide 13: Performance 2012: fault summary
T. Mastoridis: Evian 2012

## Slide 14: Performance 2012: fault summary
T. Mastoridis: Evian 2012

## Slide 15: Preparing for after LS1 (2015):
T. Mastoridis: Evian 2012
Getting ready for 6.5 TeV per beam:

## Slide 16: Preparing for after LS1 (2015):
T. Mastoridis: Evian 2012
Getting ready for 25 ns bunch spacing

## Slide 17: Cavity set-point modulation
T. Mastoridis: Evian 2012

## Slide 18: Thank you very much!