## Slide 1: Tetrode Power Amplifiers
TIARA & Uppsala University
Workshop on RF Power Generation for Accelerators
Eric Montesinos, CERN, BE-RF-PM

## Slide 2: Introduction
Workshop on novel concepts for RF power generation for accelerators
Experienced researchers and leading companies in the field of RF power generation will gather to explore the technical challenges emerging from the design of new accelerators and to match them with state-of-the-art industrial solutions for RF power generation
Through knowledge exchange between research institutes and commercial partners, the workshop will address technical challenges shared by European research infrastructures collaborating in TIARA
The workshop will focus on the main areas of
  electron tube devices (Tetrodes-Diacrodes, IOTs, Klystrons,…)
  solid-state amplifiers
  phase-stability and timing

## Slide 3: Content
UN-FAQ about tetrode (Unfortunately Not - Frequently Asked Questions)
Study case
  new CERN SPS 2 x 1.7 MW @ 200 MHz
Conclusion

## Slide 4: Power vs Frequency
Chart: Tetrodes & Diacrodes available from industry
| 30 | 30 | 30 | 30 | 30 | 30 | 50 | 50 | 60 | 80 | 80 | 110 | 110 | 110 | 120 | 120 | 130 | 200 | 200 | 200 | 200 | 200 | 200 | 210 | 220 | 352 | 352 | 400 | 400 | 450 | 450
peak < 1 ms | 1000 | 700 | 500 | 1500 | 500 | 4000 | 600 | 1000 | 1000 | 120 | 2500 | 500 | 3000 | 120 | 200 | 30 | 100 | 15 | 200
CW | 750 | 700 | 400 | 300 | 150 | 1500 | 2000 | 1500 | 2000 | 100 | 100 | 1700 | 60 | 200 | 60 | 450 | 40 | 20 | 60
#REF! | 1

## Slide 5: Output Power vs Input Power
Chart: YL1530, 35 kW nominal @ 200 MHz
| 0 | 104 | 206 | 315 | 430 | 555 | 700 | 920 | 1321 | 2250 | 4500
Pout | 0 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54 | 60
1 s (x1.4)
100 µs (x1.5)
10 µs (x1.7)
CW (x1.2)
35 kW nominal

## Slide 6: Output Power vs Input Power
Chart: Tetrodes, Klystrons, SSPA
| 0 | 0.14857142857142858 | 0.29428571428571426 | 0.45 | 0.61428571428571432 | 0.79285714285714282 | 1 | 1.3142857142857143 | 1.8871428571428572 | 3.2142857142857144 | 6.4285714285714288 | 0.54545454545454541 | 0.61818181818181817 | 0.72727272727272729 | 0.83636363636363631 | 0.98181818181818181 | 1 | 1.1272727272727272 | 1.3090909090909091 | 1.509090909090909 | 1.7636363636363637 | 2.0363636363636362 | 2.3636363636363638 | 2.4727272727272727 | 3.676408537275877E-2 | 0.16810482465774959 | 0.30804216967959258 | 0.44534997545593652 | 0.59379996727458195 | 0.75953918166077616 | 0.999381782168974 | 1.2091871815897948
Tetrode | 0 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.1667 | 1.3333 | 1.5 | 1.6667
Klystron | 0.593 | 0.67 | 0.763 | 0.876 | 0.979 | 1 | 1.092 | 1.219 | 1.284 | 1.312 | 1.311 | 1.282 | 1.275
SSPA | 0.025333 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.0833

## Slide 7: Special thanks to SSPA
An allegation against tetrodes is lack of gain
Gain for a tetrode is about 14 dB
For an output power of 100 kW, a 4 kW driver is required
In the past, this was achieved with a small tetrode, HVPS, Grids supplies, …
Nowadays, up to ~ 25 kW it will be SSPA
Perfect combination with tetrodes
LLRF
Final
gain = 14 dB
Pout = 100 kW
Driver
gain = 14 dB
Pout = 4 kW
SSA
gain = 52 dB
Pout = 160 W

## Slide 8: Special thanks to SSPA
An allegation against tetrodes is lack of gain
Gain for a tetrode is about 14 dB
For an output power of 100 kW, a 4 kW driver is required
In the past, this was achieved with a small tetrode, HVPS, Grids supplies, …
Nowadays, up to ~ 25 kW it will be SSPA
Perfect combination with tetrodes
Chart: Tetrodes & Diacrodes
| 30 | 30 | 30 | 30 | 30 | 30 | 50 | 50 | 60 | 80 | 80 | 110 | 110 | 110 | 120 | 120 | 130 | 200 | 200 | 200 | 200 | 200 | 210 | 220 | 400 | 400 | 450 | 450
peak < 1 ms | 1000 | 700 | 500 | 1500 | 500 | 4000 | 600 | 1000 | 1000 | 120 | 2500 | 500 | 3000 | 120 | 30 | 100 | 15 | 200
CW | 750 | 700 | 400 | 300 | 150 | 1500 | 2000 | 1500 | 2000 | 100 | 100 | 1700 | 60 | 200 | 60 | 20 | 60
Tetrodes
SSPA

## Slide 9: Combining
Minimum 0.1 dB losses per combiner
Up to few kW
  λ/4 wavelength combiners
  Up to 10 to 1 combiners
With higher power
  3 dB combiners
  Magic Tees
Has to be taken into account
  For overhead specification
  Regarding average power for building Cooling and Ventilation
10 x 4 kW
to 40 kW
2 x 40 kW
to 80 kW
3 dB : 550 kW & 160 kW
3 dB : 1.1 MW
200 MHz CW combiners

## Slide 10: SPS 1.1 MW @ 200 MHz 5 s - 0.1 Hz

## Slide 11: SPS 1.1 MW @ 200 MHz 5 s - 0.1 Hz

## Slide 12: Efficiency
Chart: YL1530 @ 200 MHz, measured last week
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40
YL1530 @ 200 MHz | 0 | 26.85 | 37.8 | 47.2 | 54.9 | 60.7 | 64.6 | 66.4 | 63.8
Nominal power 35 kW
η = 66.4 %
Pulsed 1 µs to cw, no variation

## Slide 13: PS efficiency - pulsed system
Tetrodes will provide output power following any kind of driver amplitude modulation from pulsed to CW
Klystrons have additional losses as HV has to be stabilized prior to RF pulse
HVPS Modulator for klystron
-> additional overall losses
RF pulse
RF pulse
RF pulse
Rise time losses
HV modulator envelope
RF pulse
Rise time losses
HV modulator envelope
time
time
power
power
Tetrode direct RF
-> neglictible additional losses

## Slide 14: Statistics
Chart: YL1530 SPS 200 MHz, 2 x 32 tubes in parallel
| 1 y | 2 y | 3 y | >= 4 y
Series 1 | 12 | 13 | 30 | 42
Series 2 | 59
Series 3 | 39
Series 4 | 38
Series 5 | 21
Total 1980-2013 : 254 tubes
Average lifetime : 32’000 hours
Tubes with > 28’000 hours : 78 %
(also true for tubes stored 20 years !)

## Slide 15: Statistics
Chart: 
| Loss of emission | Input reflections | Unknown | Over temp | Arcing
Reason of fault | 99 | 97 | 20 | 20 | 18
Reason of fault | # of faults | % of faults
Loss of emission | 99 | 39
Input reflections | 97 | 38
Unknown | 20 | 8
Over Temp | 20 | 8
Arcing | 18 | 7
Unpredictable : 23 %
Graceful degradation : 77 % (possible to monitor and predict)
Graceful operation : 99.5 % (2012)
YL1530 SPS 200 MHz, 2 x 32 tubes in parallel

## Slide 16: Statistics
Chart: Year of operation
| 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
% RF faults | 0.59 | 0.61 | 0.83 | 0.45 | 1.8 | 1.41 | 1.1 | 0.81 | 0.48 | 0.3
Availability not only depends upon the technology
but also upon the exploitation strategy
spares, manpower, schedules, …
SPS 200 MHz : 100 tube sockets + transmitters (HVPS, controls, combiners, etc.)

## Slide 17: Supplier
Nowadays tetrodes are mainly Thales
Frame contract
  Known prices with a known % price increase per year
  25 years production guaranteed
  If not, end of production: drawings, cooking recipes and Intellectual Property for free, we will be allowed to subcontract the construction of the tube
In the past, some tetrodes have already been discontinued
  They have been replaced by a ‘pin to pin’ compatible tube from another supplier
  An alternative tube has always been provided
Are there so many suppliers for the other technologies ?
  Who can guaranty NO obsolescence ?

## Slide 18: Supplier
Chart: Tetrodes & Diacrodes available from industry
| 30 | 30 | 30 | 30 | 30 | 30 | 50 | 50 | 60 | 80 | 80 | 110 | 110 | 110 | 120 | 120 | 130 | 200 | 200 | 200 | 200 | 200 | 200 | 220 | 352 | 352 | 400 | 400 | 450 | 450
peak < 1 ms | 1000 | 700 | 500 | 1500 | 500 | 4000 | 600 | 1000 | 1000 | 120 | 2500 | 500 | 3000 | 120 | 200 | 30 | 100 | 15 | 200
CW | 750 | 700 | 400 | 300 | 150 | 1500 | 2000 | 1500 | 2000 | 100 | 100 | 1700 | 60 | 200 | 60 | 1000 | 40 | 20 | 60
#REF! | 1
  Still more new powerful applications with tubes within the last 10 years (tetrodes + diacrodes)

## Slide 19: Miscellaneous
Tetrode amplifiers are radiation capable
Single power source per cavity allows individual LLRF, clear advantage
High peak short excursion is mandatory with cyclotrons LLRF
SPS SWC 200 MHz with
its Tetrode amplifier

## Slide 20: Study case
New SPS amplifiers plant @ 200 MHz
2 transmitters
  Pulse mode from 1 µs to 5 s
  1.7 MW peak with respect to 850 kW average

## Slide 21: Possible transmitters
16 tetrodes (or 16 IOTs)
  16 is a very good number to combine tetrodes
  This allows to ensure a graceful operation even with 14/16 tetrodes
  Each power source, 140 kW capable, operated 106 kW
  Gain is 14 dB, 16 individual 6 kW SSPA drivers, perfect combination
2 diacrodes (2 MB-IOTs)
  Less combiners
  Each diacrode, 850 kW capable, operated 785 kW
  Gain is 14 dB, 2 individual 32 kW SSPA drivers
2’000 SSPA
  Graceful degradation, only 10 % oversized, 2’000 x 1 kW units
  Additional combiners, more losses, building Cooling and Ventilation

## Slide 22: Combining losses
Power level | Combiner | SSPA 1 kW transistor | Tetrode 140 kW | Diacrode 850 kW
# units operated x nominal power |  | 2’000 x 900 W | 16 x 106 kW | 2 x 785kW
8 kW | 8 to 1 λ/4 | 0.1 dB | - | -
50 kW | 6 to 1 λ/4 | 0.1 dB | - | -
100 kW | 3 dB | 0.1 dB | - | -
200 kW | 3 dB | 0.1 dB | 0.1 dB | -
400 kW | 3 dB | 0.1 dB | 0.1 dB | -
800 kW | 3 dB | 0.1 dB | 0.1 dB | -
1600 kW | 3 dB | 0.1 dB | 0.1 dB | 0.1 dB
To cavity |  | 1’500 kW | 1’500 kW | 1’500 kW

## Slide 23: Foot print
2 x
2 Diacrodes
2 x
16 Tetrodes
2 x
2000 SSPA
New building

## Slide 24: SPS Supercycle
Magnets
cycle
Particles
FT
CNGS
CNGS
CNGS
CNGS
LHC
MD

## Slide 25: SPS Supercycle
Magnets
cycle
FT
CNGS
CNGS
CNGS
CNGS
LHC
MD
RF

## Slide 26: SPS Supercycle
For such a machine the key parameter is AVAILABILITY
FT
CNGS
CNGS
CNGS
CNGS
LHC
MD
0
425
850
1700
RF Power
kW
0
3.2 s
2.8 s
48
Time
sec
14.7 s
48 s
6.1 s
6.1 s
6.1 s
6.1 s
6.6 s
2.3 s
2.8 s
2.8 s
4.0 s
2.0 s
2.8 s
1.2 s
3.5 µs 172 kHz
12 µs 43 kHz
1 µs – x Hz
to
CW

## Slide 27: Efficiency
Chart: % of maximum output Power
| 0 | 45 | 51 | 58 | 65 | 73 | 81 | 90 | 97 | 100 | 0 | 2 | 15 | 30 | 46 | 61 | 76 | 92 | 100 | 0 | 12 | 25 | 37 | 50 | 62 | 75 | 87 | 100
1 kW transistor unit : ηaverage = 50 % | 0 | 11.2144 | 29.6433 | 41.6743 | 50.9906 | 58.5461 | 65.1417 | 70.6812 | 72.4173
140 kW tetrode : ηaverage = 47 % | 0 | 26.85 | 37.8 | 47.2 | 54.9 | 60.7 | 64.6 | 66.4 | 63.8
CNGS flat top
11.2 s
Flat bottom
6.0 s
FT + LHC + MD
4.6 s
At maximum power
SSPA operated at 90 %
Tetrode operated at 76 % (106/140 kW)
(availability AND lifetime)
SSPA Pmax
1000 W
Tetrode Pmax
140 kW

## Slide 28: Overall efficiency
Technology | ηRF source [%] | ηPS [%] | ηRF dist. [%] | ηRF tot [%]
Tetrode | 47 | 90 | 89 | 38
Diacrode | 48 | 90 | 93 | 40
SSPA | 50 | 90 | 83 | 38
SSPA cavity combiner | 50 | 90 | 89 | 40
Power Supply
& infrastructure
LLRF
Combiners
RF source
Cavity

## Slide 29: Why tetrodes are so beautiful
Within their frequency range, few MHz to 400 MHz, they are powerful
In association with SSPA drivers, they are the perfect RF Power Source
Their efficiency is good, over 65 % at nominal power
Almost same overall efficiency as SSPA
Graceful operation with redundant amplifiers
Graceful operation as predictable end of life

## Slide 30: Why tetrodes are so beautiful
A single power source per cavity is a clear advantage having an individual LLRF
They allow short pulses peak excursion
They offer a reduced foot print, important regarding acquisition cost
Regarding combining, reduced losses, easier to be ‘Green’ and easier for building Cooling and Ventilation
Tetrode amplifiers are radiation capable

## Slide 31: Why tetrodes are so beautiful
Under certain circumstances, full reflection can be sustained
Reduced HV compared to klystron, less than 25 kV, no oil HV transformers
Tetrodes and their amplifiers are a very well known technology
We have very good statistics
Tetrodes kept their characteristics even after 20 years of storage
Single supplier is not a problem as we have a frame contract

## Slide 32: Conclusion
Workshop on novel concepts for RF power generation for accelerators
Experienced researchers and leading companies in the field of RF power generation will gather to explore the technical challenges emerging from the design of new accelerators and to match them with state-of-the-art industrial solutions for RF power generation
Tetrodes are not young, but their characteristics are constantly evolving to match new RF power generation requests
We should always consider tetrode power amplifiers for new accelerators !

## Slide 33: Thank you very much
Anode
Screen grid
G2
Cathode
Filament (or heater)
Control grid
G1
Schematic of a tetrode amplifier