## Slide 1
Prospects for developing new tubes
I. Syratchev, CERN

## Slide 2
Mostly 704 MHz, ~3msec, 14 Hz.
Theme: RF power sources for the future ‘Big’ science.
(It should become ‘Big’, when the number of sources exceeds few hundred)
~50 kW average
ESS. Conventional single beam klystrons
CLIC MBK (specifications).
Frequency: 1.0 GHz
Peak RF power: 20 MW
Efficiency: >70%
Pulse length: up to 150 sec
Rep. rate: 50 Hz
P average: up to 150 kW
ILC MBK (demonstrated).
Frequency: 1.3 GHz
Peak RF power: 10 MW
Efficiency: ~69%
Pulse length: up to 1.50 msec
Rep. rate: 10 Hz
P average: ~150 kW
The L-band klystron development is amongst the most strong synergies between CLIC and ILC.

## Slide 3
Peak power
Efficiency
Cost (per MW)
Life time
 Beam power
 High voltage
(space charge limited)
RF breakdown limited
Klystron cluster
 Perveance
 High voltage
(space charge limited)
RF circuit topology
Depressed collector
PPM focusing
/SC solenoid
Modulator
 Peak power
CLIC MBK#6
Max. 180 kV
 High voltage
(space charge limited)
Similar scaling for modulator cost
 Current density
New cathode topology/technology
CLIC MBK#6
What kind of performance we need to improve ?
Targeting the higher voltages brings many benefits. But for the long pulses it soon will be limited at about 160-180 kV.
The most efficient way out is to use Multi-Beam technology.
We need all of it !
The subjects for the new tubes development

## Slide 4
State of art: L-band 10 MW MBK klystrons for ILC.
In terms of achieved efficiency at 10 MW peak RF power level, the existing MBK klystrons provides values very close to the 70%, as is specified in CLIC CDR.
Minimizing the cost and increasing peak RF power still remain for CLIC as an important objective towards TDR phase

## Slide 5
Extending technology: L-band 20 MW MBK klystron for CLIC.
We made a study which indicates that the scaling of existing tubes down in frequency may end up in rather powerful (>20 MW) and efficient (>70%) MBK.
Currently we are in process of preparing “call for tender” for fabrication of such a tube.

## Slide 6
What else people are working at?
ABK (CCR)
SBK (SLAC)
Cluster X-band (SLAC)
Super MBK (KEK)
PBGK
None of them have clear advantages compared to the existing MBK technology.
http://www.osti.gov/bridge/servlets/purl/1045838/1045838.pdf
http://accelconf.web.cern.ch/accelconf/IPAC10/papers/thpeb066.pdf
http://accelconf.web.cern.ch/accelconf/pac2009/papers/tu5pfp093.pdf
http://indico.cern.ch/confRegistrantsDisplay.py/list?confId=204269

## Slide 7
New cathode topology
The multiple beam guns with two stages of compression opens a wide range of opportunities. Even existing MBK designs can be improved in terms of peak power, beam voltage, efficiency and life time.
http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=5452975
http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4283375
Doubly Convergent Multiple-Beam Electron Guns

## Slide 8
Planar MBK with ‘pencil’ beams. Build and tested in 1961
http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=1473207&tag=1
Planar RF topology combined with doubly convergent gun.
New guns with double compression, being combined with planar technology might be an attractive solution. It allows integration of the individual (for each beam) drift channels.
The use of this technology naturally suggests application of PPM focusing and relatively ‘simple’ fabrication processes, thus substantial cost reduction:
ILC–type MBK
Planar MBK

## Slide 10
Efficiency and klystron RF circuit design
New method of increasing efficiency in klystrons has been developed and tested. Method is based on the velocity re-distribution of electrons in a bunch prior to its deceleration in the output cavity.
IVEC 2013
One also may expect, that spent beam velocity spread can also be reduced, thus depressed collector (if used) will require less stages.
Harmonic cavities
Implementation of higher (2nd, 3rd ) harmonic cavities is a well established technique which allows to increase efficiency and reduce the cost (length) of the tube.
(see also presentation by Chiara Marrelli)

## Slide 11
Efficiency and depressed collector
A pulsed depressed collector which uses a novel feed-forward energy recovery scheme. It also allows to recover the rise and fall time of the modulator pulse (opens a potential to reduce modulator price).
Simulated with 2D-PIC code efficiency using a five-stage, un-optimized collector was as high as 55%.
IVEC 2013

## Slide 12
Output Power, MW | 1.0 | 1.5 | 1.0 | 1.0
Frequency, MHz | 704 | 704 | 704 | 704
Beam Voltage, kV | 50 | 113 | 51 | 43.3
Beam Current, A | 32 | 20.8 | 27.6 | 32.4
Efficiency, % | >65 | >65 | >71 | >73
Gain, dB | 22 | 46 | 50 | 50
Bandwidth (1dB),MHz | 3 | 4 | >4 | >4
Predicted Performance
MBIOT
Scaled VKP-8291
Hypothetical 6 beams MBK
(microperveance / beam=0.4)
704 MHz MBIOT vs. MBK
Objectively, MBK performance at this RF power level and frequency can be even better, compared to MBIOT.
It does not require dedicated R&D (low risk).
It provides high power gain (driver cost)
But it might be more expensive.
VHP-8330A HOM IOT
Hypothetical 12 beams Planar MBK
(microperveance / beam=0.3) + R&D

## Slide 13
Given enough attention and resources, the battle for efficiency (more general for PECL) can gain enough momentum, so that in 5 years we will operate MW(s) RF power stations with overall efficiency above 70%!
John Lennon