## Slide 1
Uppsala, June 17th - 19th, 2013
Massamba DIOP, R. LOPES, P. MARCHAND, F. RIBEIRO
DEVELOPMENTS OF HIGH POWER
CW SSAs at SOLEIL
TIARA Workshop on RF Power Generation for Accelerators

## Slide 2
OUTLINE
  SSA operation at SOLEIL
  BOOSTER 35 kW
  STORAGE RING 180 kW
SOLEIL 352 MHz SSA State of the Art
500 MHz SSA R&D and new projects
  LNLS : 2 x 45 kW (476 MHz)
  SESAME : 2 x 75 kW
  THOM-X : 50 kW
R&D at other frequencies

## Slide 3
26 beamlines funded: 18 with insertion devices and 8 with bending magnets
2012: 22 beamlines opened to users
Opened to users since 2007
SOLEIL OVERVIEW
S-Band (3 GHz) LINAC
BOOSTER: 100 MeV => 2,75 GeV (3 Hz)
2,75 GeV STORAGE RING (500 mA)

## Slide 4
En : 100 MeV  2.75 GeV (rep. 3 Hz) ; Vcav : 100  900 kV @ 352 MHz
1 x 5-cell Cu cavity (CERN LEP)  Ptot : 20 kW (Pdis : 15 kW, Pbeam : 5 kW)
1 x solid state amplifier  35 kW CW @ 352 MHz (developed in house)
Cavity in the BO ring
BO RF room (amplifier & LLRF)
BOOSTER (BO) RF SYSTEM

## Slide 5
330 W amplifier module -
(VDMOS Transistor - Semelab D1029UK05)
600 W, 300 Vdc / 30 Vdc converter
35 kW SSA OF THE SOLEIL BOOSTER
147 amplifier modules and power supplies on 8 water-cooled dissipaters

## Slide 6
24 W
240 W
330 W
20 kW
30 W
64 x
x 2  40 kW
2.5 kW
35 kW SSA POWER COMBINATION
19 W
192 W

## Slide 7
DIAGRAM OF THE BO RF CONTROL SYSTEM
AMPLIFIER
CAVITY
AND LLRF
SOLEIL
CONTROL
« TANGO »
µcontroller
Hardwired
fast interlock
I x 2 x 147 modules
Pi, Pr x 16
MULTIPLEXING
AI
Cmd
Ethernet
An. & dig. I / O
Vacuum
Machine intlk
PSS
Pref
Water flows,
Temperatures, …
Pin
Pout
to amplifier
Power supplies off
RF switch
RS232
LLRF : Low Level RF Electronics
(amplitude, phase & frequency loops)
CPCI
PLC
PC

## Slide 8
OPERATIONAL EXPERIENCE WITH THE BO RF SYSTEM
The Booster RF plant is in operation since mid 2005.
Up to date, after 7 years operation (> 44 000 running hours),
only a single trip in operation, due to a human mistake (2006)
The 35 kW solid state amplifier has proved to be very reliable.
Only 8 (out of 150) module failures: 5 bad solder quality and 3 broken transistors,
which did not affect at all the operating conditions
and could be quickly repaired during scheduled machine shutdowns.
 Advantage of the high modularity and redundancy

## Slide 9
STORAGE RING (SR) RF SYSTEM
E = 2.75 GeV, E = 1.2 MeV, Ib = 500 mA
 PRF = 600 kW & VRF = 4 MV @ 352 MHz
2 cryomodules (CM), each containing a pair of single-cell s.c. cavities
Each cavity is powered with a 180 kW solid state amplifier
Both CM supplied with LHe (4.2 K) from a single cryo-plant

## Slide 10
Same principle as for the BO one, extended to 4 towers of 45 kW
 726 modules / amplifier x 4 cavities  16 towers & ~ 3000 modules
SR 180 kW RF SYSTEM

## Slide 11
COMPONENTS OF THE SR AMPLIFIER
600 W – 280 Vdc / 28Vdc converter
352 MHz - 315 W amplifier module
(LDMOS transitor - Polyfet LR301)

## Slide 12
COMPONENTS OF THE SR AMPLIFIER
Power splitters
2 , 8 and 10 ways (90, 350 & 20 pcs, respectively)
Power combiners
2.5, 25, 100, 200 kW; 320, 34, 26 & 6 pcs, respectively
(S11 < - 30 dB)

## Slide 13
AMPLIFIERS 1 & 2 => 2 CAVITIES OF CM1

## Slide 14
AMPLIFIER
CAVITY
AND LLES
SOLEIL
CONTROL
« TANGO »
µcontroller
Hardwired
fast interlock
I x 2 x 680 modules
Pi, Pr x 80
MULTIPLEXING
AI
Cmd
Ethernet
An. & dig. I / O
Vacuum
Machine intlk
PSS
Pref
Water flows,
Temperatures, …
Pin
Pout
to amplifier
Power supplies off
RF switch
PLC
CPCI
RS232
PLC
Cryo
PC
DIAGRAM OF THE SR RF CONTROL SYSTEM

## Slide 15
AMPLIFIER CONTROL via the UCONTROLLER
Transistor Currents, Pi, Pr For A Tower

## Slide 16
STORAGE RING
OPERATIONAL EXPERIENCE
Significant improvement expected from the new generation modules
with more robust transistors and less thermal stress
RF power amplifiers
- Proved to be very reliable : after > 38000 running hours over ~ 7 years,
only 5 short beam dead times  ~ 100 % operational availability, MTBF > 1 year
- Module failure rate of ~ 3.5 % per year  ~ no impact on the operation
 Matter of maintenance : 1 hour @ each shutdown for ~ 10 mod. change
 Yearly repair cost of ~ 5 k€ (for the four 200 kW amplifiers)
Chart: 
| 2006-2007 | 2008 | 2009 | 2010 | 2011 | 2012
Transistor Failure | 0.04 | 0.03 | 0.011 | 0.017 | 0.006 | 0.012
Soldering Failure | 0.007 | 0.022 | 0.024 | 0.033 | 0.014 | 0.006
Soldering preventive maintenance

## Slide 17
After 7 years of operation, SSA innovative design has proved itself and demonstrated that it is an attractive alternative to the vacuum tube amplifiers, featuring an outstanding reliability and a MTBF ( > 1 year).
Thanks to the acquired expertise and the arrival of the 6th generation LDMOS, SOLEIL has carried out developments which led to doubling the power of the elementary module (650 W) while improving the performance in terms of gain, linearity, efficiency and thermal stress.
Advantages of SSA technology: low phase noise, good linearity, high reliability, long life time, easy maintenance, simple spare parts, no HV, no X ray.
SOLEIL RF STATUS
=> UPGRADE to benefit from 6th generation improvements

## Slide 18
Why SSA upgrade at SOLEIL?
Easier maintenance, better performances
  Low gain and phase dispersion (+/-0,2dB and +/-5° instead of +/-1,5dB and +/-7,5°)
  More power capability => optional operation with 2 or 3 amplifiers out of 4
  More robust transistors
  Transistor supply made easier (NXP, Freescale…)
Cost savings
  6% increase in module efficiency => less modules => electrical power savings
  => compensation for upgrade costs within 4 years
  Old PCB re-used and only transistors are changed => less than 10% of the amplifier cost
At the beginning, we thought about replacing only the damaged modules with new transistors. But the very strong performance and cost advantages made us change our strategy for a controlled and planned massive upgrade.

## Slide 19
SSA upgrade at SOLEIL in details
Transistor LR301 replaced by BLF574XR
  Same footprint as LR301
  Up to 500W CW (high power margin)
  Better robustness and relialibity
Add gain and phase compensation circuits
Components change for matching
RF parameters | LR301 | BLF574XR | Advantages of BLF574XR
Gain | 13,7 | 20 | Less drivers (+0,5% for overall efficiency)
Efficiency | 62% | 68% | Better efficiency ( +4,5% for overall efficiency)
Output power | 315W ( 350W tested) | 330W (450W tested) | More Power Margin
Gain Dispersion | +/-0,8dB at Pnom | +/-0,2dB at Pnom | No sorting
Phase Dispersion | +/-7,5° at Pnom | +/-5° at Pnom (+/-2,5° expected) | Better combining efficiency
Comparison LR301 vs BLF574XR
Test of 10 BLF574XR samples:
  Assembling and test of 2,5kW unit based on BLF574XR modules during 4000h on dummy load
  Mounting them in our amplifier (AMP1) since one year in operation without any problem
Gain & phase
compensation
Inner
circuit
Outer
circuit

## Slide 20
SSA upgrade at SOLEIL in details
Jan-Feb 2013: Supplying all components (RF capacitors, transistor, etc…)
March & April 2013 : Modifications and adjustments of 100 modules
May 2013 : Replacement of 90 drivers on two 180kW amplifiers
Oct 2013 : Replacement planned of 90 drivers on two last 180 kW amplifiers
Replacement of last stage modules ~ 4-8 years (1 or 2 tower per year)
Chart: 
| 19.2 | 19.21 | 19.27 | 19.28 | 19.32 | 19.329999999999998 | 19.34 | 19.350000000000001 | 19.38 | 19.399999999999999 | 19.43 | 19.440000000000001 | 19.45 | 19.46 | 19.47 | 19.48 | 19.5 | 19.52 | 19.55 | 19.559999999999999 | 19.57 | 19.579999999999998 | 19.600000000000001 | 19.64 | 19.649999999999999 | 19.66 | 19.690000000000001 | 19.7 | 19.8 | 19.829999999999998 | 19.850000000000001 | 19.86 | 19.88 | 19.899999999999999 | 19.91 | 19.920000000000002 | 19.93 | 19.940000000000001 | 19.96 | 19.97 | 19.98 | 19.989999999999998 | 20 | 20.010000000000002 | 20.02 | 20.03 | 20.04 | 20.05 | 20.059999999999999 | 20.079999999999998 | 20.100000000000001 | 20.11 | 20.12 | 20.13 | 20.14 | 20.149999999999999 | 20.16 | 20.170000000000002 | 20.190000000000001 | 20.2 | 20.8 | 20.83 | 20.84 | 20.86 | 20.87 | 20.9 | 20.91 | 20.92 | 20.94 | 20.96 | 20.97 | 20.98 | 20.99 | 21 | 21.01 | 21.03 | 21.04 | 21.05 | 21.06 | 21.07 | 21.08 | 21.09 | 21.1 | 21.11 | 21.12 | 21.13 | 21.14 | 21.15 | 21.16 | 21.17 | 21.18 | 21.19 | 21.2 | 21.21 | 21.23 | 21.25
Gain 350W | 3 | 1 | 1 | 1 | 1 | 3 | 4 | 2 | 2 | 7 | 1 | 1 | 4 | 2 | 2 | 3 | 11 | 2 | 2 | 4 | 4 | 2 | 17 | 1 | 4 | 3 | 1 | 1
Gain 330W | 1 | 2 | 1 | 1 | 1 | 4 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 3 | 2 | 3 | 2 | 3 | 5 | 1 | 3 | 7 | 4 | 1 | 3 | 2 | 5 | 6 | 3 | 3 | 12
Gain 200W | 2 | 1 | 1 | 2 | 1 | 3 | 2 | 4 | 1 | 1 | 2 | 1 | 1 | 3 | 5 | 1 | 3 | 3 | 4 | 1 | 1 | 1 | 9 | 1 | 3 | 1 | 4 | 7 | 3 | 1 | 1 | 4 | 4 | 3 | 2 | 3
Gain Dispersion
Distribution of 100 first BLF574XR modules
Number of modules
Gain
Phase Dispersion
Number of modules
Phase
Chart: 
| 162,7 ° | 163,5 ° | 163,6 ° | 163,8 ° | 163,9 ° | 164,0 ° | 164,2 ° | 164,4 ° | 164,5 ° | 164,6 ° | 164,7 ° | 164,8 ° | 165,0 ° | 165,1 ° | 165,2 ° | 165,3 ° | 165,4 ° | 165,5 ° | 165,6 ° | 165,7 ° | 165,8 ° | 165,9 ° | 166,0 ° | 166,1 ° | 166,2 ° | 166,3 ° | 166,4 ° | 166,5 ° | 166,6 ° | 166,7 ° | 166,8 ° | 166,9 ° | 167,0 ° | 167,1 ° | 167,2 ° | 167,3 ° | 167,4 ° | 167,5 ° | 167,6 ° | 167,8 ° | 167,9 ° | 168,2 ° | 168,4 ° | 168,5 ° | 168,8 ° | 169,0 ° | 169,1 ° | 169,2 ° | 169,3 ° | 169,4 ° | 169,6 ° | 170,2 ° | 170,3 ° | 170,7 °
Pout=200W | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 3 | 2 | 3 | 2 | 6 | 4 | 2 | 8 | 3 | 1 | 4 | 3 | 1 | 2 | 4 | 3 | 2 | 4 | 2 | 2 | 4 | 1 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Pout=330W | 1 | 1 | 3 | 7 | 12 | 41 | 9 | 2 | 2 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Pout=350W | 1 | 3 | 1 | 9 | 9 | 11 | 11 | 11 | 9 | 6 | 5 | 2 | 4 | 1 | 1 | 1 | 2 | 1 | 1 | 1

## Slide 21
SOLEIL 352 MHz SSA STATE OF THE ART
6th generation transistors (Vdc = 50 V) + SOLEIL expertise  fast progress
 At 352 MHz, Pmod ~ 700 W, G > 20 dB,  > 70%
[ Current LR301 mod. (Vdc = 28 V) : P = 315 W, G = 13 dB,  = 62 % @ 352 MHz ]
 Huge improvement : Pmod x 2.2 , better performance (G ,  , linearity)
& thermal stress strongly reduced (ΔT : - 60 °C)  longer lifetime
 Beg. 2009, transfer of technology agreement concluded with ELTA-AREVA
ESRF contract for 7 SOLEIL type amplifiers of 150 kW (14 x 75 kW towers)
June 2010 : A 10 kW unit (16 modules) successfully tested at SOLEIL
June 2011 : Commissioning of the first 75 kW tower at ESRF
March 2012 : Commissioning of the 4 x 150 kW amplifiers for the booster,
which, up to now, have run quite satisfactorily for 1.5 year
2013 – 2014 : Delivery of the 3 amplifiers for the SR, slightly modified as compared to the Booster for handling high CW VSWR ( Jorn Jacob)

## Slide 22
 | Transistor type | Power supply per module | Module Parameters at nominal conditions | Amplifier design & nominal power | VSWR limitation * | Comments
SOLEIL Booster | D1029UK05  SEMELAB | 1 x 600 W 280/28 Vdc | P1dB = 330 W, G = 11 dB  = 60 % , Tmax = 130°C | 1 tower of 8 dis Pnom = 35 kW modulated | No limit with SOLEIL Booster duty cycle | 1 trip over 7 years due to a human mistake
SOLEIL SR (actual) | LR301 Polyfet | 1 x 600 W 280/28 Vdc | P1dB = 315 W, G = 13 dB  = 62 % , Tmax = 130°C | 4 towers of 10 dis Pnom = 180 kW cw | 70 kW full reflection Pr = 35 kW @ 180 kW | MTBF > 1 year
SOLEIL SR (upgrade) | BLF574XR NXP | 1 x 600 W ♯ 280/48 Vdc | P1dB = 350 W, G = 22 dB  = 69 % , Tmax = 90°C | 4 towers of 10 dis Pnom = 200 kW cw | 70 kW full reflection Pr = 32 kW @ 200 kW | Much more robust than LR301
ESRF Booster (800W load) | BLF578 NXP | 2 x 600 W 280/48 Vdc | P1dB = 650 W, G = 20 dB  = 71 % , Tmax << 75°C | 2 towers of 8 dis Pnom =150 kW modulated | No limit with ESRF Booster duty cycle | In CW Pr limited at 5 kW for Pi = 150 kW
ESRF SR V2 (1.2kW load) | = | = | = | 2 towers of 8 dis Pnom = 150 kW cw | 85 kW full reflection Pr = 50 kW @ 150 kW |  modified combination  + 1.2 kW load
ESRF SR V3 (power circul) | = | = | = |  Pnom = 140 kW | 140 kW CW full reflection | + 5% power loss - 3% on efficiency Extra costs
* VSWR limitation: when operating the amplifier at high CW incident power, Pi, with a high VSWR and the worst phase condition, an unpowered module (ie, both of its power supplies, or both sides of its push-pull broken) can see a power on its circulator load, Pload > Pi
Rem: full reflection for a short time (~10 ms) is not a problem ( Pr interlock)
♯ 2 PS in series on 2 modules in //
 VDMOS ; all the other cases are LDMOS
SOLEIL 352 MHz SSA STATE OF THE ART

## Slide 23
500 MHz R&D ON SSA
High efficiency (96%) 230 V_ac / 50 V_dc power converters
6th generation LDMOS  BLF578 : 650 W modules
RF characteristics:
RF Output Power: 650 W CW at 1 dB
Gain : 17dB
Efficiency: > 60% at Pn
Gain dispersion : +/- 0.2 dB at Pn
Phase dispersion :+/- 5° at Pn
Input Return Loss : < - 40 dB at Pn
Unconditional stability (K>10 dB)

## Slide 24
500 MHz R&D ON SSA
10 kW unit prototype for long term test (> 500 hours)
Efficiency ~ 55%

## Slide 25
500 MHz R&D ON SSA
2-way splitter
8-way splitter
Pi - Pr monitoring coupler
Power combination components
8 x 650 W
8 x 5 kW
2 x 40 kW
2 x 80 kW

## Slide 26
WAVEGUIDE-to-COAXIAL COMBINER (WaCCo)
Two 6 inches coaxial input ports (2 x 80 kW)  1 WG output
Replace a coaxial combiner + a coaxial-to-WG transition
Design optimization with HFSS and Microwave Studio
 A 500 MHz prototype has been validated at signal level
Movable SC  can ensure a good matching for different configurations with diff nb of dissipaters per tower or diff nb of modules per dissipater
2 coaxial inputs
WG
output
dl

## Slide 27
Collaboration agreements
  LNLS (Brazilian LS) : 2 x 45 kW @ 476 MHz, in operation
  SESAME (LS in Jordan) : 4 x 150 kW @ 500MHz
  THOM-X (Compact source of hard rays): 50 kW @ 500MHz
R&D at other frequencies
  FM band (88 – 108 MHz)  1 kW module with G > 25 dB and  ~ 80 %
  L band (1.3 & 1.5 GHz) for 4th generation LS  Pmod > 400 W
    LUNEX5 : 20kW @ 1.3 GHz – R&D for the TDR
The SSA technology is ideally suited to the ERL requirement, which is typically of a few tens of kW at 1.3 – 1.5 GHz.
SOLEIL R&D ON SSA

## Slide 28
SOLEIL-LNLS COLLABORATON
April 2010 : the SOLEIL - LNLS team in Campinas-Brazil,
after successful tests of the amplifiers
Two amplifiers of 50 kW @ 476 MHz for the LNLS storage ring with components designed by SOLEIL (400 W RF modules with BLF574)

## Slide 29
LNLS 50 kW RF PLANTS
The two 50 kW SSA have run satisfactorily on the LNLS SR for ~ 3 years

## Slide 30
THOM-X 500 MHz 50 kW AMPLIFIER (PRELIMINARY DESIGN)
16 Amplifiers per Dissipator
2 m
2 m
Cabinet Design
AC-DC Power Supplies
Tower Design
2 m
2 m
High Power Combination

## Slide 31
PROPOSAL FOR THOM-X AMPLIFIER CONTROL SYSTEM
MUX D numérique
(1 par dissipateur de 16 modules)
MUX D1
µC
MUX
Maitre
RS-485
6 MUX Esclaves
16 modules
16 modules
16 modules
16 modules
16 modules
16 modules
Ethernet
PC local
supervision
TANGO
4 préampli
MUX D2
µC
MUX D3
µC
MUX D4
µC
MUX D5
µC
MUX D6
µC
8 x (2 courants + 1 temp. )
½ dissipateur haut
P_incidente
P_réfléchie
P_incidente
P_réfléchie
µC
Multiplexeur
Multiplexeur
Comparateurs
Bus RS-485
ADC
ADC
ADC
ADC
ADC
ADC
Débit eau
Thermo-switch
Interlock alims
Interlock RF
I/O
8 x (2 courants + 1 temp.)
½ dissipateur bas
I/O
RS485
adresse
½ dissip. haut
(8 mod.)
½ dissip. bas
(8 mod.)

## Slide 32
2 m
AC-DC Power Supplies
(160 x 2kW modules)
1 Waveguide Combiner (WaCCo)
2 x 75 kW RF combination
64 8-way splitters
16 dissipators
256 amplifier modules
SESAME 500MHz 140kW AMPLIFIER (PRELIMINARY DESIGN)
3 m

## Slide 33
SUMMARY & CONCLUSIONS
BOOSTER 35 kW SSA (D1029UK05)
  STORAGE RING 180 kW SSA (LR301)
  Operation and upgrade to 6th generation BLF574XR
SOLEIL 352 MHz SSA State of the Art
  Pmod ~ 700 W, G > 20 dB,  > 70%
500 MHz SSA R&D (BLF578)
    Pmod ~ 650 W, G ~ 17 dB,  > 60%
500 MHz SSA based projects
  LNLS : 2 x 45 kW (476 MHz)
  SESAME : 2 x 75 kW
  THOM-X : 50 kW
R&D at other frequencies
  FM band (88 – 108 MHz)  1 kW module with G > 25 dB and  ~ 80 %
  L band (1.3 & 1.5 GHz) for 4th generation LS  Pmod > 400 W
    LUNEX5 : 20kW @ 1.3 GHz

## Slide 34
Thank you for your attention