## Slide 1
Two electrons source, for two different projects at CERN
Dr Kévin Pepitone

## Slide 2
Outline
AWAKE
  Electron beam line and electron source
  Beam instrumentation (BPM, Faraday Cup, PepperPot)
  Booster structure
  Klystron and modulator
CLIC
  Layout
  Electron source
  Cathode and connector
  Experimental results
  Simulations
  Comparison experiments/simulations
  Emittance estimation
Conclusions

## Slide 3
Outline
AWAKE
  Electron beam line and electron source
  Beam instrumentation (BPM, PepperPot)
  Booster structure
  Klystron and modulator
CLIC
  Layout
  Electron source
  Cathode and connector
  Experimental results
  Simulations
  Comparison experiments/simulations
  Emittance estimation
Conclusions

## Slide 4
AWAKE - Introduction
Comparison to the proton bunch longitudinal profile (left, no plasma) with the profile for a bunch passing through the plasma (right). The strong modulation of the bunch is clearly seen

## Slide 5
Parameters | Phase 1
Beam energy | 16 MeV
Relative energy spread | Dp/p = 0.5%
Bunch Length | σz = 4 ps (1.2 mm)
Bunch size at focus | σ*x,y = 250 um
Normalized Emittance | 2 mm.mrad
Electrons/bunch (bunch charge) | 1.25E9 (0.2 nC)
AWAKE – Electron source

## Slide 6
AWAKE – Electron transfer line layout

## Slide 7
Instrument | How many | Resolution | Who
BPMs | 3 | 50 um | Triumf, new
Fast current transformer | 1 | 10 pC | CERN, existing
Faraday cup | 1 | 10 pC | Triumf, new
Screens | 3 | ~ 20 um | CERN, partly existing
Multi slit (emittance) | 1 | < mm mrad | University of Manchester
Quad scan (emittance) | 1 | < mm mrad | CERN
Spectrometer | 1 | 10 keV | CERN
FC
MS
BPM
Laser +Diagnostics
RF GUN
Emittance
Spectrometer
Corrector
MTV
VPI
FCT
Accelerator
MTV, Emittance
Matching triplet
BPM
Klystron from CTF3
AWAKE – Beam instrumentation

## Slide 8
AWAKE – Booster structure fabrication and tuning

## Slide 9
AWAKE – BPM and Faraday Cup

## Slide 10
AWAKE – Pepper pot
Pepper Pot has been delivered at CERN and installed
OTR
YAG:Ce
Mask
Calibration screen.

## Slide 11
Power
supplies
Modulator
Control
Klystron tank and
retention box
Thales TH2100
Parameters | Specifications
RF frequency | 2998.5 MHz
Peak RF power | 45 MW
RF gain | 54 dB
Efficiency | 43 %
Anode voltage | 307 kV
Beam current | 340 A
High voltage pulse length @75% | 7.6 us Needed : 1-2 us
Total height | 1.7 m
AWAKE – Klystron and modulator

## Slide 12
AWAKE – Picture

## Slide 13
Outline
AWAKE
  Electron beam line and electron source
  Beam instrumentation (BPM, PepperPot)
  Booster structure
  Klystron and modulator
CLIC
  Layout
  Electron source
  Cathode and connector
  Experimental results
  Simulations
  Comparison experiments/simulations
  Emittance estimation
Conclusions

## Slide 14
Conceptual design report (EDMS 1234244)
LEETCHI – Electron source and beam parameters

## Slide 15
LEETCHI
Parameters | Baseline
Beam energy | 140 keV
Beam current | 5 to 7 A
Pulse length | 140 µs
Emittance (RMS) | < 20 mm mrad
Repetition rate | 50 Hz
Beam power | 4,9 to 6,9 kW
Shot to shot charge variation | 0.1 %
Flat top charge variation | 0.1 % after correction
LEETCHI – Electron source and beam parameters

## Slide 16
CPI YU-156
LEETCHI – Cathode and connector

## Slide 17
1000 shots @ 50 Hz, extracted from 180 000 shots (1 hour @ 50 Hz)
VHV = 140 kV ; t = 8 µs ; IB = 4.5 A
Measured pulse to pulse stability on beam current: 0.3-0.4 %
LEETCHI – Experimental results
Pulse to pulse current stability
Allan Standard Deviation = A metric for stability = Two-sample Standard Deviation taken over variable interval of time or variable interval of pulses

## Slide 18
300 shots @ 6 Hz, extracted from 1800 shots (5 minutes @ 6 Hz)
VHV = 140 kV ; t = 140 µs ; IB = 4.5 A
Experimental results
Beam stability from the electrical results
Capacitor discharge during the pulse, the energy of electrons decreases during the pulse (140 keV to 90 keV)
New
Modulator
Measured pulse to pulse stability on beam current: 0.3-0.4 %
Flat top current stability 10 %
The grid of the cathode resists to 4.5 A (mean current) during 140 µs

## Slide 19
t = 5 µs, Ibeam = 4.5 A, E = 140 keV
Isolenoid = 5.0 A
Isolenoid = 5.5 A
Isolenoid = 6.0 A
Isolenoid = 6.5 A
Isolenoid = 7.0 A
Isolenoid = 7.5 A
Isolenoid = 8.0 A
rrms = 9.8 mm
rrms = 13.5 mm
rrms = 5.9 mm
rrms = 6.8 mm
rrms = 11.3 mm
rrms = 8.2 mm
rrms = 12.6 mm
LEETCHI – Experimental results
RMS radius from OTR images

## Slide 20
LEETCHI – Experimental results
OTR images
t = 5 µs, E = 140 keV
5 5.2 5.4 5.6 5.8 6 6.2 6.4 6.6 6.8 7 7.2 7.4 7.6 7.8 8
ISolenoid (A)
Ibeam
0.5 A
1 A
4.5 A

## Slide 21
LEETCHI – CST layout

## Slide 22
X-Z plane
Y-Z plane
E field
Pierce geometry
Anode
Second grid
LEETCHI – Micro focalization

## Slide 23
The minimal radius at waist is linked to
the space charge and to the emittance
The emittance calculation will be performed by a comparison between experimental results and CST, Magic simulations for different value of the solenoid and beam currents.
LEETCHI – Comparison experiments / simulations
t = 5 µs, E = 140 keV

## Slide 24
Emittance formulas (Lapostolle and Lee, Cooper)
and
MAGIC-2D PIC, CST-PIC, CST-Tracking comparison (without cathode grids)
CST-Tracking emittances calculations (with and without cathode grids)
LEETCHI – Emittance
Second grid
Third grid
, ,

## Slide 25
Outline
AWAKE
  Electron beam line and electron source
  Beam instrumentation (BPM, PepperPot)
  Booster structure
  Klystron and modulator
CLIC
  Layout
  Electron source
  Cathode and connector
  Experimental results
  Simulations
  Comparison experiments/simulations
  Emittance estimation
Conclusions

## Slide 26
Conclusions
LEETCHI
  Perfectly working at 140 kV
  The mean current is 4.5 A @ 140 µs
  Repetition rate is 6 Hz @ 140 µs and 50 Hz @ 8 µs (vacuum limitation)
  Shot to short variation of the order of 0.1 %
  The grid of the cathode resists to the current
  Simulations are in a well advanced phase
AWAKE
  AWAKE is working with the laser, the plasma cell and the proton beam
  Klystron, modulator and waveguides installed
  The installation of the laser line is ongoing
  Electron line installed and leak tied
  Installation of diagnostics ongoing
  Beams requirements are clearly defined
  Tests of AWAKE with the electron beam in 2018

## Slide 27
Thank you for your attention