## Slide 1
Younguk Sohn
@RREIA, Uppsala University
September 11, 2017
Introduction of PAL and
Activities in Superconducting RF

## Slide 2: Topics
Introduction of PAL
Experience and Activities in SRF

## Slide 3: What’s PAL ?
Pohang Accelerator Laboratory is belonged to POSTECH (Pohang University of Science & Technology). Private Institute supported by Korean government.
POSTECH, founded by Pohang Steel Company (POSCO) in 1986
PAL operates
PLS-II (3rd generation synchrotron): superconducting RF
PAL-XFEL (4th Gen. Syn.): normal conducting RF
Pohang is one of industrial & Science cities in Korea.

## Slide 4
Pohang
Seoul
China
Japan
Korea
Russia
We are here
USA
East Asia

## Slide 5: Younguk Sohn
Nuclear power plant for 2 years
In accelerator for 26 years
- Magnet (especially superconducting) design
- Beamline (synchrotron light) design
- Superconducting system
(孫 永旭, 손영욱)

## Slide 6: Bird View of PAL Site
PAL-XFEL, 2 km long
PLS-II, 286 m circumference

## Slide 7: PAL-XFEL Parameters
  Main parameters
  e- Energy 10 GeV
  e- Bunch charge 20-200 pC
  Slice emittance 0.5 mm mrad
  Repetition rate 60 Hz
  Pulse duration 10 fs – 100 fs
  Peak current 3 kA
  SX line switching DC (Phase-1)
  Kicker (Phase-2)
Undulator Line | HX1 | SX1
Wavelength [nm] | 0.1 ~ 0.6 | 1 ~ 4.5
Beam Energy [GeV] | 4 ~ 10 | 3.15
Wavelength Tuning [nm] | 0.6 ~ 0.1 (energy or gap) | 4.5 ~ 3 (energy) 3 ~ 1 (gap)
Undulator Type | Planar, out-vac. | Planar
Undulator Period / Gap [mm] | 26 / 8.3 | 35 / 8.3
30A
2 ps
300A
200fs
3kA
22fs
8
12
Und.
7 und.
Hard X-ray
Soft X-ray
2130 m

## Slide 8: Milestone PAL-XFEL
2002 ~ Studying and persuading government
Apr. 2011 PAL-XFEL project started
Jun. 2012 Ground-breaking
Apr. 2016 Commissioning started
Jun. 2017 User-service started
14 Jun. 2016 First SASE lasing at 0.5 nm
28 Oct. 2016 Lasing at 0.15 nm
27 Nov. 2016 Saturation of 0.15 nm
16 Mar. 2017 Saturation of 0.1 nm: Goal
0.1 nm

## Slide 9
Klystron Gallery - PAL-XFEL

## Slide 10
Linac Tunnel - PAL-XFEL

## Slide 11
Undulator Hall - PAL-XFEL

## Slide 12: Storage Ring, PLS-II
Parameters | Values
Energy [GeV] | 3
Current [mA] | 400
Emittance [nm-rad] | 5.9
Harmonic number | 470
No. of Insertion Devices | 20
Electron energy loss / turn [KeV] | 1242
RF frequency [MHz] | 499.973
Number of RF cavity | 3
Accelerating Voltage [MV] | 4.5
RF Voltage per cavity [MV] | 1.5 (5 MV/m)
Klystron amplifier [kW/each] | 300
Cryogenic Cooling Capacity @4.5 K [w] | 700
※ PLS-II has 32 beamlines (16 ID and 16 BM)

## Slide 13: LINAC (3 GeV) as Injector
Injector LINAC
Thermionic Electron Gun
16 Pulse Modulators (200MW, 7.5µs)
16 Klystrons (80 MW, 4µs)
15 Energy Doublers (gain=1.5)
46 Accelerating Sections
Length = 170m
3.0 GeV, full energy injection
2,856 MHz (S-band)
10Hz, 1.5 ns, 1Å pulsed beam
Norm. emmittance : 150µmrad
Gallery
Tunnel

## Slide 14: PLS-II Storage Ring
Beam Energy 3.0GeV
Beam Current 400mA
Lattice DBA
Superperiods 12
Emittance 5.8 nm∙rad
Tune 15.37 / 9.15
RF Frequency 499.97 MHz
Circumference 281 m

## Slide 15: User Statistics
1366 experiments
5234 by users

## Slide 16
Introduction
Superconducting RF System in PLS-II

## Slide 17: 3 SRF Modules @Tunnel
SRF module 2
SRF module 3

## Slide 18
LHe Vessel
Wave-guide
Vacuum Vessel
E-beam
RF Window
Thermal Transition
HOM Absorber
70K Thermal Shield
CESR-3 Cryomodule, Designed by Cornell University

## Slide 19: PLS-II, SRF 500 MHz Cavities
Orbit stability @ high beam current to 400 mA
High beam power W/ 20 insertion devices
Higher synchrotron radiation brightness,
order of 2 (100 times) compared to PLS
→
PLS-II operated with 380mA topup mode,
But, nominal is 400 mA.

## Slide 20: Specifications of SRF System
Specification | 
Resonant frequency [MHz] | 499.973
R/Q [Ω] | 89
Q0 | >1109 @ Vacc  2.0 MV (~7 MV/m)
Qe | 1.37E5 +/- 0.2E5
Frequency tuning range (step-motor) | 150 kHz with resolution of 10 Hz
Operating Temperature [K] | 4.4
Accelerating Voltage / Cavity [MV] | 1.3 – 2.5 (4.5 – 8.5 MV/m)
Max. RF Power(CW) / Cavity [kW] | 300 (operation < 200 kW)
HOM Removal | Ferrite Absorber
Input power coupler | Waveguide
Window | 300 kW in TW cw 150 kW SW cw at full reflection

## Slide 21: Superconducting 500 MHz RF Cavities
CESR Type

## Slide 22: Accelerating Voltages @ Bare Cavity
@vertical test
@cryomodule test

## Slide 23: Q0 Degradation, VT vs HT (SAT)
※ Cavity 2 was less Q0 than spec. 1.0E9 @2 MV/m
1.0E+09

## Slide 25: Window Conditioning & Test
9 days (~10 hours/day) for conditioning and test of RF window at Test Stand @warm temperature
Travelling Wave Mode; Spec.
- 8 hours @300 kW CW
- Max △T=29 C (<60 C)
- Vacuum pressure: 2.9~4.9E-9 mbar, no trip (<1E-7)
Standing Wave Mode; Spec.
- 4 hours @150 kW CW
- Max △T=47 C (#24), 56.5C (#25)
- Vacuum pressure: 1.2E-8 ~ 5.9E-9 mbar, no trip

## Slide 26: Site Acceptance Test (SAT) @PLS-II
Leak Check: Cavity from atmosphere and He vessel
Spec. (@warm & cold temp.) < 2e-10 mbar l/s
Q external: 1.65E5
RF Voltage (Vacc) and Q0 Measurement
Long term operation: 2.03 MV, Q0=6.8e8 (Spec: >5.0e8)
Maximum Vacc: 2.5 MV (8.5 MV/m), Q0=6.4e8
Window & cavity conditioning
On-resonance and off-resonance
Pulse conditioning: 1, 2, 5, 10, 20, 50 msec and CW mode
Repetition rate: primarily 10 Hz with 1, 2, 5 Hz
Tuner performance test: stroke > +/- 150 kHz, resolution <10Hz

## Slide 27: Site Acceptance Test
Test-pit With radiation shield
Pulse-1,2,5,10,20,50 &100 msec
Cryomodule control system

## Slide 28: Cooling with Liquid He
~15 hours: room temp. to 4.4 k

## Slide 29: Conditioning Window & Cavity
Aug. 14, 2012
Window Vacuum Pressure
1 msec
2 msec
5 msec
10 msec
20 msec
50 msec
CW mode
Window Vacuum
Cavity Vacuum
2.03 MV !!
Last 16 hours

## Slide 30: Management, Cavity & Window Vacuum
Partial warming-up cavity up to 40K
Threshold pressure vacuum bursts >1 x 109 mbar

## Slide 31: Partial Warmup & Cooldown Mass-Spectrometer (RGA)
4 days before partial warmup, and 3 days after re-cooldown
Before partial warmup
After re-cooldown
Partial warmup
Partial Pressure of Hydrogen (Black)

## Slide 32: Partial Warmup & Cooldown
During partial warmup & cooldown with TMP operation
Ion pump off
(00:28)
TMP on
1.4e-8 mbar
(01:00)
1 Ion pump @window on by mistake
(03:40)
H: Mass 2
N2: Mass 28
O:Mass 16
N:Mass 14
C, Mass 12
All Ion pump on
TMP off
Cavity top:43K
Cavity bottom: 31K
(06:07), 2.9e-9 mbar
~22K
~15K
~26K

## Slide 33: 3rd Harmonic Cavity for PLS
Increase beam lifetime by lengthening e-beam bunches
Reduce coupled-bunch instabilities from higher order mode (HOM)
For;
(Mar. 2004 – Dec. 2007)

## Slide 34: Prototype 3rd Harmonic SRF Cavity for PLS
Prototype 3rd H Cavity
Cavity Performance from vertical test
First SRF Cavity developed in Korea !!
Design/fabrication @ PAL, surface preparation @KEK, vertical test @Jlab.

## Slide 35: R&D for ILC SRF
  Cavity (KEK-Low loss) design by K. Saito
  Design/Fabricating dies, jigs & fixtures by PAL
  Fabricating two 9-cell cavities with simple straight beam pipe
  Surface preparation and vertical test at KEK, Japan

## Slide 36: Fabrication of 9-cell Cavity - PAL #1 and 2
3 Measurements of Eacc
- Average Eacc = 23.0 MV/m
- Max. Eacc = 27.2 MV/m

## Slide 37: Results of Vertical Test for 9-cell Cavity
3 Measurements of Eacc
- Average Eacc = 23.0 MV/m
- Max. Eacc = 27.2 MV/m

## Slide 38: Tack ! 감사합니다 ! (Gam-Sa hap-ni-da !)