## Slide 1: Test plan of ESS HB elliptical cavity
Han Li
On behalf of FREIA team
FREIA Laboratory, Uppsala University
24th of Oct. 2017

## Slide 2
 | Dressed cavity packet conditioning first (on-resonance) | Coupler Cold conditioning first (off-resonance)
advantage | With an activated surface, lower risk of contamination in the cavity during the conditioning from low field to nominal Eacc | easier mechanical operation Power regulation automaticlly by softerware
disadvantage | Complex mechanical operation More human intervention during conitioning like changing power level and pulse length, if possible changing interlock set values | Have a high risk of cavity contamination
Loop and special device | Lund or SEL | SGD: Signer generator RF station, Conditioning software interlock system, RF switch, Data acquisition system, Personal safty system

## Slide 3
Current progress
704 MHz SEL>
Hardware:
SEL box is under design and will be finished at the begining of Nov.
---key people: Tord peterson, Tor and Han
Validation of Interlocks
---key people: Konrad and Kjell
Temperature sensors attached the cavity
Temperature sensors location of interested.
---key people: Rocio, Magnus, Younguk and Han
Four wire heater for power calibration
Wiers extending of hearter;
One current meter is need to connect in the loop.
---key people: Rocio

## Slide 4
Current progress (cnt.)
Quench detection>
Simulation:
cavity quench profile simulation
Quech detection analog loop simulation
Hardware: prototype od quench detector
---key people: Magnus and Han
Coupler conditioning factor>
FPC conditioning | Source frequncy | cavity frequency
Warm | 704.42MHz | <704.0947MHz
Cold | 704.42MHz | 704.0947MHz

## Slide 5
Current progress (cnt.)
704 MHz Conditioning system
  Software:
  Modify the parameter in conditioning program
  Manage to control the pulse shape, amplitude and pulse length
---key people: Konrad and Han
Pressure gauge test
Get rid of the step-wise reading from pressure gauge. (The resolution between two reading?)
---key people: Rocio, Konrad
Flowmeter reading
Improve the reading of the absolute flow. A smoothing is added in the system.
---key people: Konrad and Rocio

## Slide 6
704 MHz Conditioning system
  Power limitation and interlock
---key people: Magnus, Konrad and Han
  SEL Labview interface will be modified
---key people: Han and Tor
  SEL auto conditioning programme
---key people: Han and Tor
Two pressure sensor in the tank for crosscheck of the Helium pressure
---key people: Lars and Rocio
To do list

## Slide 7
question
1, CEA colleague would like to start the conditioning from slow frequency ,such as 1 Hz. Is it OK for the klystro ,Lund system and SEL?
Change the repetition rate in the Lund system ?
For the SEL, could we use FPGA to control the repetition rate , and pulse length?(Pulse amplitude could be control by the gain factor)
2, After the conditioning, should we warm up the cavity package to 40 K?