## Slide 1: RF R&D at CERN
Seminar at Uppsala University December 2017

## Slide 2: Outline
RF R&D at the existing CERN accelerator complex
  PSB Finemet® based wideband system
  PSB controlled longitudinal emittance low-up
  PS new beam gymnastics
  PS transversely biased ferrite tuner
  SPS wideband transverse kicker
  High-power RF going solid-state (ex. SPS)
  LHC full detuning
Preparing the future
  CLIC
  High efficiency klystron research
  SRF Technology
    HL-LHC Crab Cavities
    HIE-ISOLDE cavities
    Nb3Sn thin film technology R&D
Summary

## Slide 3: CERN Accelerator complex
LHC Large Hadron Collider
SPS Super Proton Synchrotron
PS Proton Synchrotron
AD Antiproton Decelerator
CTF3 CLIC Test Facility
AWAKE Advanced WAKefield Experiment
ISOLDE Isotope Separator OnLine
REX Radioactive EXperiment
HIE-ISOLDE High Intensity and Energy ISOLDE
LEIR Low Energy Ion Ring
LINAC LINear ACcelerator
n-TOF Neutrons Time Of Flight
HiRadMat High-Radiation to Materials
CHARM CERN High Energy AcceleRator Mixed field facility
IRRAD proton IRRADiation facility
GIF++ Gamma Irradiation Facility
CENF CErn Neutrino platForm

## Slide 4: PSB Finemet® System
Finemet® is a composite magnetic material, developed and commercialized by Hitachi Metals, Japan.
It allows to build a “cavity” without a resonance, with a flat frequency response covering without any tuner. (almost 5 octaves!)
M. Paoluzzi

## Slide 5: PSB RF SYSTEM – fabrication completed
New PSB RF System, working between 0.5 and 20 MHz without tuning, to be operational after LS2.
27 cavities assembled, 24 will be installed. Collaboration work with KEK - Japan
M. Paoluzzi et al.

## Slide 6: PSB RF SYSTEM – fabrication completed
Most of fabrication, complete assembly and cabling performed at the RF workshop

## Slide 7: PSB: new controlled longitudinal emittance blow-up
MOVIE: emittance blow-up during ramp
Controlled longitudinal emittance blow-up is performed in present operation using
phase modulation of high harmonic RF system C16
in MDs and probably in future operation → band-limited phase noise in main RF C02
Stable and
reproducible
bunches at
PSB extraction
1.4 - 2.8 eVs
S. Albright et al.

## Slide 8: PS Beam manipulations from nominal to 8b4e BCS: mitigating e-cloud in LHC
“8b+4e” beam
1600b.
1600b.
Standard 25 ns beam
Nominal scheme: 6 PSB bunches 18  36  72
BCMS 25 ns: 8 PSB bunches  4  12  24  48
BCS 8b4e: 8 PSB bunches  16  32
Record luminosity in LHC with BCS 8b4e: > 2x1034 cm-2s-1
power loss from stable phase measurement
standard 72b
BCS 32b 8b4e
BCMS 48b

## Slide 9: PS 80 MHz Fast Tuner – R&D work in progress
The prototype of 80 MHz fast tuner was installed in the PS during EYETS, however preliminary measurements performed under a tight schedule were not able to indicate a usable working point for the device.
C. Vollinger et al.

## Slide 10: SPS: R&D for wideband transverse feedbacks
GHz wideband transverse feedback (WBTF) for SPS
Study for FCC transverse feedbacks with head-tail code simulations
Implementation of signal processing for PSB and PS transverse feedback upgrades
single bunch in 25 ns train, Q2O optics
The new WBTF slot line kicker is made from two half cells, laser soldered, each having its own cover with its copper electrode
W. Hofle, G. Kotzian, D. Valuch, E. Montesinos, S. Calvo et al.

## Slide 11: LIU-PS 10 MHz Upgrade
The final prototype of the upgraded feedback amplifier is getting ready to be installed in the PS during the next YETS.
A more advanced option, based on solid state amplifiers, is also being developed, preliminary simulations show promising results.
10 MHz
3 MHz
G. Favia, M. Morvillo, C. Rossi et al.

## Slide 12: LIU-SPS-RF turning solid-state
SPS 200 MHz, 1250 Wp 5 seconds – 700 W CW Solid State Power Amplifiers from TTi Norte (Spain)
In operation since beginning 2017
SPS 200 MHz, 144 kWp 5 seconds – 72 kW CW Solid State Power Amplifiers from Thales (France)
Still under (difficult) qualification
E. Montesinos et al.

## Slide 13: Power combiners Key to go to solid-state!
We validated several cavity combiners, for the MB-IOT and the LIU-SPS-RF, including a VHPCC (Very High Power Cavity Combiner)
This is very important as opening the doors of the high power levels (MW) to the SSPA based amplifiers
CERN 16:1 radial cavity combiner 2.4 MW CW @ 200 MHz,
Still to be power tested, validated at VNA level with only -0.2dB insertion losses
Machined by EN-MME in-house from a massive block of aluminium
CERN 144:1 cavity combiner 144 kW @ 200 MHz
Calculations by ESRF, construction by CERN
E. Montesinos et al.

## Slide 14: LHC Adaptive Set-point (Full Detuning)
FPGA implementation of adaptive setpoint algorithm in SetPoint VME module
Operational in LHC in 2017: achieves a factor 2 reduction in klystron power
Phase modulation
Klystron power
Algorithm switched ON before start of ramp
Power and phase modulation during LHC ramp
P. Baudrenghien, G. Hagmann, T. Mastoridis, O. Brunner et al.
Notes: Algorithm developed by Themis and Philippe enabling ‘full detuning’ operation of the LHC cavities was implemented in FPGA by John Molendijk.
The algorithm is switched on at the end of filling and before the start of the ramp. The phase modulation takes a few minutes to settle, during which time we see the klystron power reduce. The power then increases through the ramp due to the increase in cavity voltage. At flat top the power along 1 turn is < half of what would previously be necessary.
Demonstrates the flexibility of digital LLRF with programmable logic: can survive a complete paradigm change!

## Slide 15: LHC: Phase modulation in production
Fill 5737
  old scheme
  power increases during ramp
  noise ripples caused by the beam/no beam transients
  power scales as beam current  190 kW at 1.5 MV, 0.5 A DC
Fill 5887 ( summer 2017 onwards)
  new scheme
  power independent of beam current
  very small power change following beam dump
  power scales quadratic with beam voltage  104 kW at 1.5 MV, QL=60k
Beam gone..
Minimal change in power
Minimizes power required from klystron

## Slide 16: Medical RFQ amplifiers
Construction of the HPRF, i.e. 4 * 100 kW IOT 20 µs - 200 Hz @ 750 MHz
  Capacity charger and capacitor, HV cage, Grid – Focus – Ion pump supplies, RF drivers, PLC + Fast interlock, RFQ Conditioning system, Instrumentation, Four IOT and trolleys, RF lines, FPC
Started in March 2016, fully delivered to in June 2017, property transfer to ADAM in October 2017
The four IOT + RF lines + air cooling + FPC connected to the RFQ
The compact FPC with PEEK windows
The SSPA Drivers + HVPS + controls
E. Montesinos et al.

## Slide 17: Multi Beam IOT (work for ESS)
Test bench completed in 2017, including
  Capacity charger, HV Capacitors 80 µF, HV cage, Grid – Focus – Ion pump supplies, LEP crowbar, RF drivers + cavity combiners, PLC + Fast interlock, Compact RIO, Instrumentation
CPI-Thales tube tested in June up to 1.2 MW 4 ms 14 Hz @ 704 MHz (tube failure after 1 hour, being repaired, test to restart soon)
L3 com tube tested in October up to 1.1 MW 4ms 14 Hz @ 704 MHz (Limited by Drivers and tube internal crowbar, test to restart soon)
CPI-Thales MB-IOT has performed 1.2 MW 4 ms – 14 Hz for few seconds before an output line vacuum internal default stopped the tests, it is under repair
The proof of feasibility has been made
L3 MB-IOT has performed 1.1 MW 4 ms – 14 Hz for an hour before a strong crowbar stopped the tests, Drivers have been damaged and are under repair, tests to restart soon
The proof of feasibility has been made
E. Montesinos et al.

## Slide 18: R&D to prepare the future of CERN some possible future colliders
ILC e+e-: Pulsed, 1.3 GHz, 500 GeV
0.5 TeV
FCC ee: CW, 0.4 & 0.8 GHz, up to 350 GeV
FCC hh: 0.4 GHz, 100 TeV!
CLIC e+e-: Pulsed, 1.0 GHz, 3 TeV
3.0 TeV

## Slide 19: CLIC
Features:
High-gradient, 100 MV/m, acceleration for a shorter, less expensive linac
Nano-meter sized beams at the interaction for high luminosity
Two-beam rf power generation for efficient high peak power

## Slide 20: 3 TeV version of CLIC

## Slide 21: Two 380 GeV versions: drive beam or klystrons

## Slide 22: CLIC baseline accelerating structure
11.994 GHz X-band
100 MV/m
Input power ≈50 MW
Pulse length ≈200 ns
Repetition rate 50 Hz
Micron–precision disk
6 mm diameter beam aperture
25 cm
HOM damping
waveguide
W. Wuensch et al.

## Slide 23: Prototype testing X-band - XBoxes
W. Wuensch et al.

## Slide 24: X-band
COOLING FITTING
HALF
COOLING CHANNEL
VACUUM FLANGE
WAVEGUIDE
ALIGNMENT PIN
COVER
Manufacturing ongoing
New CLIC improved prototype in productionTD26CC_R1 (4)
CLIC 380GeV prototype under fabrication TD31CC (4)
New company qualification and technology transfer with T24(2) and TD26CC_R1(1)
Crab cavity and deflectors for collaborations
New designs for improved assembly
Cold copper halves design
Compact damping waveguides in rectangular disks
Improved components
Xboxes supports and modifications
Tooling, measurements etc.
W. Wuensch et al.

## Slide 25: High-field vacuum arcs understanding the physics
Data from T. Higo
ArcPIC simulations, K. Sjoebaek
Vacuum arcs – the formation of plasma accompanied by large electron currents - occur in many devices and applications.
What’s so special about us?
Very high surface electric fields, over 200 MV/m
Opportunity to test over 20 rf structures and over 40 pulsed dc electrodes combined with significant theoretical and simulation effort.
We believe that we see processes which give fundamental field limits for copper.

## Slide 26: Breakdown rate dependence on parameters – a physical model
W. Wuensch, MeVArc 17
Regularly observed dependence:
K. Nordlund, F. Djurabekova, Defect model for the dependence of breakdown rate on external electric fields, Phys. Rev. ST Accel. Beams 15, 071002 (2012)
Data taken in XBox-2 with TD26CC structure, T. Lucas
Physical model based on defect formation

## Slide 27: Breakdown rate understanding the physics
We operate a pulsed system, CLIC is 50 Hz, and the breakdown rate must be of the order 10-7 in the collider.
Data from T. Higo
W. Wuensch, MeVArc 17

## Slide 28: Recent test results
W. Wuensch, MeVArc 17

## Slide 29: CLIC Technology – applications overview
Beam manipulation and diagnostics:
Energy spread linearizers and deflectors
XFEL
Thompson/Compton scattering source
Medical
Advanced acceleration
W. Wuensch et al.

## Slide 30: High efficiency klystron research
Collaborative effort guided and coordinated by I. Syratchev
2
J. CAI, CERN
C. Marrelli, ESS
A. Baikov, MUFA
D. Constable, Lancaster U
V. Hill, Lancaster U
G. Burt, Lancaster U
R. Kowalczyk, SLAC
High Efficiency International klystron activity 2
Since 2013
I. Syratchev et al.

## Slide 31
difficulty
Efficiency, %
Common tubes, 95% of the market
Ultimate(space charge – free) limit
Depressed collector
High efficiency! How high it could/should be!?
Igor’s outlook and challenges in efficiency reach with single beam klystron amplifiers.
Reducing perveance
‘best’ existing tube
We still might do it?
New bunching technology
Multi Beam technology. Reduced voltage and perveance. Cost and efficiency.
Gated Cathode (triode gun). No HV switches. Modulator cost and efficiency.
SC or PPM solenoid. Overall efficiency.
Complementary technologies
MBK
I. Syratchev et al.

## Slide 32
High efficiency! How high it could/should be!?
Pulsed, 0.7 GHz,
92 MW
-9.3 M€
-10.7 M€
Excessive electricity bill, M€
1 year
Efficiency, %
FCC e+e- at 50 Euro/MWh and 5000 hours/year:
Efficiency impact on operation cost
37 MW, more than twice the overall cryogenic power needs
I. Syratchev et al.

## Slide 33
Energy storage
switch
HV transformer
RF circuit (=0.7)
Cathode
Collector
Modulator (=0.9)
180 kV
Solenoid 4 KW
20 MW, 50 Hz, 150 sec
150 kW
CLIC 20 MW L-band Multi-beam pulsed klystron.
150 kW + 88 kW
60 KW
Total = 0.62
Permanent Magnets:
- No power consumption
- Potential cost reduction
Vs. SC solenoid:
- More expensive solution
New klystron RF circuit (=0.9)
(+) Reduced Collector dissipation (16 kW)
New/advanced technology
Total = 0.95
Lower (<60kV) voltage:
- 40 mini-cathodes
No oil tank (cost)
Shorter tube (cost)
Faster switching (efficiency/cost)
Gated mini-cathode:
No switches (cost)
Modulator efficiency ~1.0
(+) Improved stability
Power from grid:
290 190 MW
Depressed collector (=0.5)
I. Syratchev et al.

## Slide 34
Klystron efficiency vs. perveance
73.5%
RF measurements with directional coupler.
23.04.2017
MBK TH1803
State of the art.
Commercial MBK (low perveance) tubes with high efficiency.
Recommended by industry
Optimised at CERN
After many decades of development the klystron technology was considered to be saturated. The experimental results from hundred’s of different devices have shown that higher efficiency is associated with lower perveance. Accounting for technological and cost reasons (K>0.2), the 75% efficiency was expected to be the utmost limit.
10 beams
21 MW
1.0 GHz
I. Syratchev et al.

## Slide 35
To saturate the bunch, peripheral electrons should receive much stronger relative phase shift than the core electrons: non monotonic bunching. In the COM method the Core of the bunch experiences periodical Oscillations due to the space charge forces, whilst the peripherals approach the bunch centre monotonically. COM method requires very long length to achieve full bunch saturation.
COM tubes with different numbers of stages:
K=0.26
Bunch saturation issues.
Reaching high efficiency requires that ALL the electrons entering the output cavity should populate the bunch (useful part of RF period) leaving anti-bunch empty.
bunch
anti-bunch
Optimised by 1D code KlypWin
I. Syratchev et al.

## Slide 36
Bunch saturation issues.
Example of the ‘fully’ saturated bunch in COM tube (Tesla 2D code)
I. Syratchev et al.

## Slide 37
133.8 kV, 12.55 A, 1.4 MW at 0.8 GHz, 80(+)%
High efficiency klystrons.
New bunching technologies on one slide.
Core Oscillations Method (5.75 m)
Bunching Alignment Collecting, 2.44 m
Core Stabilization Method
COM
BAC
CSM
High Efficiency International klystron Activity
igor.syratchev@cern.ch
CSM_23B1, 1.72 m
CSM_2L3B3, 1.88 m
I. Syratchev et al.

## Slide 38
From the klystron text book:
“For the bunch entering output cavity, the good bunching (i.e., a high fundamental harmonic of the beam current) can only yield high conversion efficiency when the energy spread in stream is small.”
(1)
Power conversion efficiency issues.
Example: power extraction efficiency from the bunched beam with I1/I0=1.75 and E min=E0 (monochromatic bunch) at the output cavity entrance. The beam and cavity parameters were taken from FCC COM tube.
Output cavity F/Q Loaded phase space. Fully saturated bunch 1D simulations with CERN in-house code (J. Cai)
85.3%
Unstable area: bouncing/ reflected electrons
F0
Bunch deceleration in the output cavity F=1.00025xF0
85.3%
Equation (1)
Modulation depth, I1/I0
Power conversion efficiency
Fully saturated bunch
Simulations (J. Cai)
In a ‘classical’ approach, the highest power conversion efficiency with fully saturated bunch does not exceed 87%.
Fully saturated ‘rectangular’ bunch
Gaussian ‘classical’ bunch
Ez in the cavity
83.3%
Zoom
accelerated electrons
I. Syratchev et al.

## Slide 39
Ultimate high power conversion efficiency conditions:
To avoid migration of the electrons from bunch to anti-bunch during deceleration in the output cavity, the incoming bunch with non-zero length should have certain velocity dispersion: Congregated Bunch, when the leading electrons are slower than the tailing ones.
For the full deceleration, the congregated bunch should be gradually transformed at the cavity exit into monochromatic bunch with least velocity.
Power conversion efficiency issues.
89.4%
Modulation depth, I1/I0
Power conversion efficiency
I1/I0=1.75
‘classical’
saturated
congregated
Equation (1)
bouncing electrons
quick optimisation
I. Syratchev et al.

## Slide 40
Power conversion efficiency. Limiting factors.
Applegate diagrams for the electrons emitted at different radius:
r=0
r=0.5 R beam
r=0.9 R beam
Bouncing (re-accelerated) electrons
Harmonic current (bunch length) at different radii.
Example of HE CSM tube (full 3D CST simulations).
BRS is an effect when the bunch length shows radial dependence.
It appears as a result of intrinsic radial imbalance between cavities RF impedance and the space charge forces of the beam.
In 2D simulations this effect is the major source of reflected electrons generation that are not predicted in 1D simulations.
We are not inefficient (2D vs. 1D), we simply cannot go higher – the reflected electrons collapse power generation.
Efficiency 80%
Bunch Radial Stratification
I. Syratchev et al.

## Slide 41
COM tube. 8_04_XX series of 10 optimised tubes.
Cavity 7 Volts
Cavity 8 Volts
Klys2D (Thales), 81.6%
Frequencies scattering
Drifts scattering
8_04_08; Eff. = 84.62%
08_04
08_04_08
MAGIC (PIC)
Replacing cylindrical beam by hollow beam efficiency is further increased up to 86%
BRS effect is almost mitigated!
I. Syratchev et al.

## Slide 42
85.7%
CSM tube. Second Generation. Tube length 1.72 m at 0.8 GHz.
Saturation curve (MAGIC 2D)
I. Syratchev et al.

## Slide 43
0.8 GHz, 133.9 kV, 12.551 A, K=0.263
0.704 GHz, 110 kV, 15.272 A, K=0.42
Expected efficiency reduction (AJDisk) 1.9%.
Length 1.72 m
Length 1.4 m
GSP/PSP
We have developed special procedure (GSP/PSP) which allows to scale the frequency, power, perveance, voltage, number of beams etc., and to preserve the bunching quality of the original tube:
I. Syratchev et al.

## Slide 44: HL-LHC: Crab Cavities for SPS test
2017, A year of milestones
  2 bare cavities: Processed & RF validated at 2K
  2 dressed cavities: Preparation & cleanroom assembly
  Cold test of dressed cavity at 2K
  Cleanroom string assembly of 2 dressed cavities
  Crab LLRF functionality: Validation at 2K with BE-RF-FB
  Complete refurbishment of SM18_M7 test bunker
  Cold test of SPS cryomodule in M7 (with limited RF)
R. Calaga, A. Macpherson et multi al.

## Slide 45: HL-LHC: Crab Cavities for SPS
Preparation
Bare Cavity Validation
String Assembly
Cryomodule Cold Test
Dressed Cavity Testing
R. Calaga, A. Macpherson et multi al.

## Slide 46: HIE ISOLDE cavities, cryomodules and linac commissioning for 2017 physics run
Breakthrough! Seamless Cavities
CM4 assembled and ready for installation in HIE ISOLDE
HIE ISOLDE 2017
physics run with 3 CM
12 RIB experiments done 8 MeV/u achieved
Excellent SRF availability
20 QWR produced, qualified and installed in the 4 HIE ISOLDE CMs
Chart: Beamtime [hours]
| 2015 | 2016 | 2017
RIBs | 142.7 | 685 | 1512.65
Stable | 163.25 | 152 | 515.25
Courtesy BE-OP
W. Venturini, K. Schirm et al.

## Slide 47: Nb3Sn sputtered films for SRF
High critical temperature
Low BCS resistance
Stoichiometry control (Sn At% 19-26 %) [1]
Requires high temperature treatment
Limited range of annealing temperatures
Substrate importance
Advantages
Challenges
Tc | Nb3Sn ~ 18.3 K
 | Nb ~ 9.3 K
RBCS @ 4.2K and 500MHz | Nb3Sn ~ 0.4 nΩ
 | Nb ~ 45 nΩ
[1] J. Charlesworth, I. MacPhail, and P. Madsen, J. Mater. Sci. 5, 580 (1970).
K. Ilyina et al.

## Slide 48: Coating by magnetron sputtering
Annealing temperatures | 600 - 800oC
Annealing time | 24 h… 72 h
Coating temperatures | 600 - 735oC
Alternative Additional Annealing | 24 h… 72 h
Reacted During Coating
Reacted After Coating
48
07-Dec-2017
Reacted During Coating
Reacted After Coating
07-Dec-2017
Reacted During Coating
Reacted After Coating
Coating parameters:
Coating gas: Ar or Kr
Coating pressures:
7·10-4 mbar … 5·10-2 mbar
Composition:
Sn 20 At% to 27 At%,
K. Ilyina et al.

## Slide 49: Results: films reacted after coating
A15 phase formation. XRD analysis & Morphology
100 nm
100 nm
A15 phase confirmed by the presence of Nb3Sn characteristic peaks of (200), (210), (211) … (332)
Absence of non-superconducting phases NbSn2, Nb6Sn5
K. Ilyina et al.

## Slide 50: Results: films reacted during coating
A15 phase confirmed by the presence of Nb3Sn characteristic peaks of (200), (210), (211) … (332)
Absence of non-superconducting phases NbSn2, Nb6Sn5
200 nm
Cu
Nb3Sn
Pt
FIB
100 nm
SEM
K. Ilyina et al.

## Slide 51: Results: Critical temperature
[2] A. Godeke. Supercond. Sci. Technol., 19 (2006) R68-R80
How to increase ?
Composition
Films of Nb3Sn on copper substrate
Reacting AFTER /DURING coating
High temperature treatment duration
Additional Annealing
K. Ilyina et al.

## Slide 52: Proposed improvement: intermediate layer
Idea:
Works as “buffer” layer to reduce residual stresses in the films (to solve cracking problem for the films reacted AFTER the coating)
Decrease lattice mismatch, i.e. improving crystalline lattice order (to avoid depression) [4]
Diffusion barrier layer (to prevent copper interdiffusion into Nb3Sn layer)
Possible candidates – Nb, Ta, Al2O3
[4] Hein. The A15 story. The Science and Technology of Superconductivity, pp 333-372
K. Ilyina et al.

## Slide 53: Preliminary results with Ta layer: encouraging
K. Ilyina et al.

## Slide 54: Summary
The RF R&D at CERN is very diverse
A large part reflects the necessity to go beyond present-day performance of existing accelerators – for the LHC and its injectors in particular this means larger intensity to reach higher luminosity.
There is a clear trend visible to replace vacuum tubes by solid-state wherever possible.
Preparing the future of accelerator-driven High-Energy Physics requires intensive R&D on new technologies (CLIC technology for high-gradient normal-conducting linacs operating in pulsed mode, superconducting RF for circular colliders running in continuous mode)
Thank you very much!