## Slide 1: Progress of the European Spallation Source
Roger Ruber
Uppsala University
Thanks to all colleagues for materials
Jülich, 1 February 2018

## Slide 2: Presentation Outline
Reminder of neutron science
Overview of the ESS machine
Technical highlights
  Science instruments
  Target system
  Accelerator
Outlook
  Fundamental physics at ESS
  Financing and time schedule

## Slide 3: Material Science & Innovation
Society’s progress has been determined by the development of new materials
Wood, glass, stone, bronze, iron, steel, concrete, plastics, silicon…
ferroelectrics, superionic conductors, giant magnetoresistance, semiconductors, liquid crystals, fullerenes carbon allotropes, high Tc superconductors and more…
“The Stone Age didn’t end for lack of stone”
Ahmed Zaki Yamani
We have to build the best facilities
with the best instruments
if we are to develop, understand, and harness New Materials

## Slide 4: Why to use neutrons?
Neutral charge
  deeply penetrating except for some isotopes
Nuclear interaction:
  cross section depending on isotope (not Z), sensitive to light elements.
Spin S = 1/2
  probing magnetism
  unstable n → p + e + νe with life time τ ~ 900s , I = I0 e- t/τ
Thermal energies result in non-relativistic velocities
  mass: n ~p; E = 293 K = 25 meV, v = 2196 m/s , λ = 1.8 Å
X-rays
Neutrons
Light
Light
X-rays
Neutrons

## Slide 5: How to produce neutrons
Nuclear Spallation
→ accelerator
Nuclear Fission
→ reactor

## Slide 6: Usable Neutron Brightness
Fission
1.2 x per decade
Spallation
4 x per decade

## Slide 7: Long Pulse Performance
4
time (ms)
Brightness (n/cm2/s/sr/Å)
x1013
ISIS TS1
128 kW
ISIS TS2
32 kW
SNS
1-2 MW
JPARC
0.3-1 MW
ILL 57 MW
ESS 5 MW
2015 design
0
1
2
3
15
5
10
λ = 5 Å
Possibilities of pulse shaping
ESS 2 MW
2015 design

## Slide 8: ESS Basic Design Principles
High Power Accelerator
Ultimate energy: 2 GeV
Repetition rate: 14 Hz
Pulse length: 2.89 ms
Peak power: 125 MW
Instruments
15-22 Instruments in construction budget
(depending on scenario)
Target Station
Ultimate power: 5 MW
He-gas cooled
Rotating W-target
42 Beam ports
Ion Source
Protons
Current: 62.5 mA

## Slide 9: European Spallation Source (ESS)
1993
Proposal for a European spallation source
2003
First European design effort completed
2009
Decision that ESS will be build in Lund
2012
Design update completed
2014
Construction starts
2020
First beam on target
First neutrons
2023
Start of user program
30 years !
2025
Construction complete

## Slide 10
April 2017
Klystron Gallery
Cryo Compressor
Building
Central Utility
Building
Distribution
Substation
Primary
Substation
Target
Monolith
Exp. Hall
E01
Active
Cells
Front End
Building
High Energy
Loading Bay

## Slide 11: Accelerator and Klystron Gallery
Accelerator Tunnel and Klystron Gallery

## Slide 12: Target Buildings

## Slide 13
December 2017
Experiment Hall

## Slide 14: First 15 Neutron Science Instruments
ESS Instrument Layout (September 2017)
ESS In-Kind Partners also collaborate on sample environment, data management systems etc.
ODIN
DREAM
NMX
MIRACLES
T-REX
MAGIC
BIFROST
HEIMDAL
FREIA
LOKI
VESPA
ESTIA
SKADI
+
+
C-SPEC
+
Nuclear Physics Institute
BEER
Test Beam Line
Monolith
Neutron beam extraction
Offers 42 neutron beam ports
Allows instruments to view either upper or lower moderator position

## Slide 15: Length and Energy Scales
SANS = small angle neutron scattering
Notes: Small-angle neutron scattering (SANS): uses elastic neutron scattering at small scattering angles to investigate the structure of various substances at a mesoscopic scale of about 1–100 nm.
Neutron reflectometry is a neutron diffraction technique for measuring the structure of thin films.
Neutron diffraction or elastic neutron scattering is the application of neutron scattering to the determination of the atomic and/or magnetic structure of a material.

## Slide 17: The ESS Target
Target wheel
Proton beam window
Moderator and reflector plugs

## Slide 18: The Target Building
Utilities and cooling plant
Helium cooling of target wheel
Water cooling of moderators, plugs and shielding
Intermediate water loops between primary circuits and conventional facility utilities
Helium cryoplant for refrigeration of cold moderator system
Nuclear grade HVAC system
130 m
22 m
37 m
High bay
Transport hall
Remote handling systems
Large active cells for safe storage and processing of spent radioactive target components
Shielded casks for transfer of spent components from monolith to active cells
Beam expander hall
Target monolith
Utilities block
Active cells

## Slide 19: The Target Station
Helium cooling of target material
Mass flow 3 kg/s
Pressure 11 bar
Temperature inlet/outlet 40 °C/240 °C
proton beam
proton beam window
proton beam instrumentation plug
Moderator and reflector
target wheel
neutron beam extraction port
monolith vessel
target monitoring plug
Rotating solid tungsten target
36 sectors
Mass, total 11 tonnes, whereof 3 tonnes of W
Rotates 23.3 rpm, synchronized with pulsed proton beam 14 Hz
Moderators
Provisional locations of moderators above and beneath the target wheel, i.e. monolith centre
1st MR plug exploits the upper space, offering:
  Cold, 30 mm high, liquid H2 moderators, 17 K
  Thermal, 30 mm high, H2O moderator, 300 K
Diagnostics and instrumentation
Controlled and integrated commissioning and operation of the accelerator and target
Fluorescent coating of PBW and target front face
Optical paths, grid profile monitor, aperture monitor
Wheel monitoring including position, temperature, vibration, as well as internal structure
Target Safety System
Monitors target coolant flow, pressure and temperature, monolith pressure, & target wheel rotation
Prohibit beam on target if parameters are outside specified limits

## Slide 20: The Target Wheel
Tungsten depth in proton beam direction is 45 cm
The range of a 2-GeV proton in tungsten is 74 cm
Brick dimensions: 10 W x 30 D x 80 H mm3
190 bricks per sector, 6840 bricks in total
Helium flows
  radially outward above and below the cassette,
  reverses direction at the wheel rim,
  and returns through the tungsten
48 cm
proton beam
20
Tungsten bricks
Cassette
Each 10° sector is loaded with a tungsten-filled cassette

## Slide 21: Moderator and Reflector Systems
Moderate neutrons to low energies, thermal and cold,
  useful for the neutron scattering
Cooling the radiation heat in liquids and solid metal bodies

## Slide 22: The Bunker Design
~ 7000t of steel
~ 300t of Borated HDPE
~ 750t of virgin HDPE/LDPE
~ 620t of concrete
~ 970t of heavy concrete
~200t of construction steel
Each bunker side measures approx. 40m long x 26m wide x 5m high
~ 10,000 tones total mass
~1400 wall & roof blocks

## Slide 23: 1996 ESS Design: Feasibility Study
5 MW beam power
1.334 GeV H- Linac
  synchrotron option discarded
    to complex for E <3GeV
  normal conducting linac
    SC linac under consideration
  6% duty cycle
  107 mA, 0.6 ms pulse
  2 x 70 mA sources
    not yet achieved at time of proposal
2 accumulator rings → 2 targets
  1 µs pulse compression (from 2 injection pulses)
  10 Hz and 50 Hz target operation
PAC97 - 9W013: Status of the European Spallation Source Design Study
ESS A Next Generation Neutron Source for Europe, Volume 3, The ESS Feasibility Study, March 1997.
coupled cavity

## Slide 24: 2009 ESS Accelerator Design Update
SC linac option (5 MW)
  1 GeV, 150 mA, 16⅔ Hz
Simplify the linac design and increase reliability
  proton pulse length ≥ 1 µs, energy ≥ 1 GeV (and ≤ 3 GeV)
  synergies with CERN Linac4 + SPL development work
  decrease the current to 75 mA
    single source
    can increase cavity gradient to 15 MV/m
  increase the energy from 1 to 2.2 GeV
  increase the repetition rate to 20 Hz
  decrease pulse length to 1.5 ms from 2 ms
PAC09 - TU6PFP083: Conceptual Design of the ESS-Scandinavia

## Slide 25: 2013 ESS Accelerator Design
Design Drivers:
High Average Beam Power
  5 MW
High Peak Beam Power
  125 MW
High Availability
Key parameters:
2.86 ms pulses
2 GeV
62.5 mA peak
14 Hz
Protons (H+)
Low losses
Minimize energy use
Flexible design for mitigation and future upgrades
Spokes
Medium β
High β
DTL
MEBT
RFQ
LEBT
Source
HEBT & Contingency
Target
2.4 m
4.6 m
3.8 m
39 m
56 m
77 m
179 m
75 keV
3.6 MeV
90 MeV
216 MeV
571 MeV
2000 MeV
352.21 MHz
704.42 MHz
First beam
  90 MeV during Summer 2019
  571 MeV during Fall 2020
5 MW capacity after 2025
RF sources for HB part are
scope contingency for accelerator
IPAC13 - THPWO072: Design Options of the ESS Linac

## Slide 26: The ESS Accelerator
 | Length [m] | No. Cavities | β | No. Magnets | No. Steerers | No. Sections | Power [kW]
LEBT | 2.38 |  |  | 2 Solenoid | 2 x 2 | 1 | 
RFQ | 4.6 | 1 |  |  |  | 1 | 1600
MEBT | 3.83 | 3 |  | 11 Quad | 10 x 2 | 1 | 15
DTL | 38.9 | 5 |  | PM-Quads | 15 x 2 | 5 | 2200
LEBT + Spoke | 55.9 | 26 | 0.50 | 26 Quad | 26 | 13 | 330
Medium Beta | 76.7 | 36 | 0.67 | 18 Quad | 18 | 9 | 870
High Beta | 178.9 | 84 | 0.86 | 42 Quad | 42 | 21 | 1100
HEBT | 130.4 |  | (0.86) | 32 Quad | 32 | 15 | 
DogLeg | 66.2 |  |  | 12 Quad + 2D | 14 |  | 
A2T | 46.4 |  |  | 6 Quad + 8 Raster |  |  | 
 | 604.21 | 155 |  |  |  |  | 

## Slide 27: ESS Accelerator Collaboration
27

## Slide 28: Ion Source & Low Energy Beam Transport
Nominal performance achieved in INFN-Catania.
Start installation in January 2018.
First Plasma from the ESS Ion Source
M. Lindroos, TAC 14, Oct. 2016
ESS Ion Source
M. Lindroos, TAC 14, Oct. 2016
CERN Courier, May 2006

## Slide 29: Double Spoke Resonators
DOUBLE-SPOKE CAVITY | 
Frequency [MHz] | 352.21
Beta_optimum | 0.50
Operating gradient [MV/m] | 9.0 (8.8)
Temperature (K) | 2
Bpk [mT] | 61
Epk [MV/m] | 38
G [Ohm] | 133
r/Q [Ohm] | 427
Lacc (=beta optimal x nb of gaps x λ /2) [m] | 0.639
Bpk/Eacc [mT/MV/m] | 6.8
Epk/Eacc | 4.3
P max [kW] | 335

## Slide 30: Medium & High Beta Elliptical Cavities
 | MEDIUM-β | HIGH-β
β | 0.67 | 0.86
# cells/cavity | 6 | 5
# CM | 9 | 21
Cav. /CM | 4 | 4
# Cav. | 36 | 84
CM L [m] | 6.584 | 6.584
Sector L [m] | 77 | 179
Prototype cryomodule with 4 medium β 6 cell elliptical sc cavities in CEA (Saclay) test place
Medium-β prototypes
P. Michelato et al, IPAC2017 & SRF2017
Notes: All cavities chemically treated with BCP
Three cavities reach the ESS specification
Very good Q0 at low field for CEA cavities, very good accelerating gradient for LASA cavity
Origin of this Q drop is not fully understood, but probably due to field emission and secondary emission effect inside inner cells (triggered by surface quality obtained after chemical treatment)

## Slide 31: Beam Raster Scanning on Target
5:4 pattern
Raster system sweeping beam in 2D pattern @ target
8 colinear magnets, individually powered
Crosshatch pattern (fx/fy, ϕxy, ax, ay) within 2.86 ms pulse

## Slide 32: outlook
Overview of the ESS organization, time schedule and ideas for the future

## Slide 33: Fundamental Physics at ESS
Four proposals
ANNI
  precise measurements of
    neutron beta decay,
    hadronic weak interaction (input to theory),
    electromagnetic properties: dipole moment, CP-violation.
UCN
  ultra-cold neutron source
NNbar/HiBEAM
  neutron-antineutron oscillations search
    aims at least a factor of 1000 greater sensitivity to the oscillation probability than similar ILL experiment (after 3 years of operation)
ANNI
HIBEAM

## Slide 34: ESSnuSB Proposal for a Neutrino Super Beam
Study neutrino oscillations (CP-violation)
  neutron program must not be affected
  if possible synergetic modifications.
Linac modifications:
  double rep. rate: 14 Hz → 28 Hz (4% to 8% duty cycle)
  add accumulator ring (Circ~400 m)
    to compress proton pulses to few μs, affordable by the magnetic horn (350 kA, power consumption, Joule effect)
  H- source (instead of protons)
    space charge problems to be solved.
~300 MeV neutrinos.
  target station (EUROν) & underground detector (LAGUNA)
Short pulses (~μs) allow decay-at-rest experiments using the neutron target
EU Design Study for ESSnuSB approved by EU in December 2017 for 2018-2021

## Slide 35: Financing and In-kind Contributions
Host Countries of Sweden and Denmark
Construction 47,5%
Operations 15%
In-kind Deliverables ~ 3%
Cash Investment ~ 97%
Non Host Member Countries
Construction 52,5%
Operations 85%
In-kind Deliverables ~ 70%
Cash Investment ~ 30%

## Slide 36: Partner Institutes
Aarhus University
Atomki - Institute for Nuclear Research
Agder University
Bergen University
CEA Saclay, Paris
Centre for Energy Research, Budapest
Centre for Nuclear Research, Poland, (NCBJ)
CERN, Geneva
CNR, Rome
CNRS Orsay, Paris
Cockcroft Institute, Daresbury
DESY, Hamburg
Delft University of Technology
Edinburgh University
Elettra – Sincrotrone Trieste
ESS Bilbao
Forschungszentrum Jülich
Helmholtz-Zentrum Geesthacht
Huddersfield Univesrity
IFJ PAN, Krakow
INFN, Catania
INFN, Legnaro
INFN, Milan
Institute for Energy Research (IFE)
Institut Laue-Langevin (ILL)
Rutherford-Appleton Laboratory, Oxford (ISIS)
Kopenhagen University
Laboratoire Léon Brilouin (LLB)
Lodz University of Technology
Lund University
Nuclear Physics Institute of the ASCR
Oslo University
Paul Sherrer Institute
Roskilde University
Tallinn Technical Univesrsity
Technical University of Chemnitz
Technical University of Denmark
Technical University Munich
Science and Technology Facilities Council
(STFC)
University of Tartu
Uppsala University
WIGNER Research Centre for Physics
Wroclaw Univesrity of technology
Warsaw University of Technology
Zurich University of Applied Sciences
(ZHAW)

## Slide 37: Updated Schedule (Oct. 2017)

## Slide 38: Civil Construction Status (Dec. 2017)

## Slide 40: Summary
Construction is on track for the start of the user program in 2023 with 2 MW of beam power,
  the 570 MeV accelerator will start late in 2020
  instrument commissioning start in 2021
All ESS staff will move to the construction site in 2018
Thanks to all colleagues for the material
  special thanks to Colin Carlile, Roland Garoby, Mats Lindroos