## Slide 1: Increasing Demand for High Efficiency RF Power Sources
Erk Jensen
CERN
ARIES Workshop on Energy Efficient RF
Ångström Laboratory, Uppsala universitet
18 – 20 June 2019 – Uppsala, Sweden

## Slide 2: Outline
Introduction – global context
Definition of “Energy Efficiency”
The Demand for High Efficiency RF Power
Trends
  IOT’s
  Klystrons
  Magnetrons
  Solid State RF Power Sources
Summary

## Slide 3: Why does energy efficiency matter?
Scarcity of fossil energy – problematic nuclear power
Volatile & unpredictable energy costs
Increasing environmental concerns (global warming, El Niño, CO2 emission)
Awareness for 50 years (Club of Rome 1968, Oil crisis 1973)
Political – societal imperative: must go towards sustainable energy!
Also particle accelerator facilities must be conceived/built/operated with this in mind! … in fact – they should give a good example and incite R&D!

## Slide 4: Energy Efficiency and Strategy
Quote from www.iea.org:
  Energy efficiency is one of the cornerstones of any strategy to guarantee sustainable and inclusive economic growth. It remains one of the most cost-effective ways to enhance security of energy supply, to boost competitiveness and welfare, and to reduce the environmental footprint of the energy system. Not only can the growth of carbon emissions be tempered by the more efficient use of energy but energy efficiency can also improve local pollution and contribute to reducing the millions of air-pollution related premature deaths each year, and keep consumers energy bills in check.
  UN’s “Sustainable Development Goal 7.3” is the measurable improvement (decrease) of global energy density, defined as primary energy supply per GDP.
Particularly relevant since large colliders are quite gourmand for energy

## Slide 5: Orders of magnitude
M. Seidel/PSI
generation | consumption | storage
1d cyclist „Tour de France“ (4h x 300W): 1.2 kWh | 1 run of cloth washing machine: 0.9 kWh | Car battery (60 Ah): 0.72 kWh BEV*) Battery (Lithium-ion): 100 kWh
1d Wind Power Station (avg): 12 MWh | 1d SwissLightSource 2.4 GeV, 0.4 A: 82 MWh | All LHC magnets @ 8.33 T: 3 MWh ITER superconducting coil: 12.5 MWh
1d nucl. Pow. Plant (e.g. Leibstadt, CH): 30 GWh | 1d CLIC Linear Collider @ 3 TeV c.m. 14 GWh 1d FCC-hh @ 100 TeV c.m. 14 GWh | All German storage hydropower: 40 GWh
1d Earth/Moon System E-loss: 77 TWh | 1d electrical consumption mankind: 53 TWh | Energy stored in all BEVs*): O(0.5 TWh) World storage hydropower: O(1 TWh)
1d sunshine absorbed on Earth: 3,000,000 TWh = 3 EWh (Exa ) | 1d total consumption humankind: 360 TWh | Energy storage seems not to scale up!
generation | consumption | storage
1d cyclist „Tour de France“ (4h x 300W): 1.2 kWh | 1 run of cloth washing machine: 0.9 kWh | Car battery (60 Ah): 0.72 kWh BEV*) Battery (Lithium-ion): 100 kWh
1d Wind Power Station (avg): 12 MWh | 1d SwissLightSource 2.4 GeV, 0.4 A: 82 MWh | All LHC magnets @ 8.33 T: 3 MWh ITER superconducting coil: 12.5 MWh
1d nucl. Pow. Plant (e.g. Leibstadt, CH): 30 GWh | 1d CLIC Linear Collider @ 3 TeV c.m. 14 GWh 1d FCC-hh @ 100 TeV c.m. 14 GWh | All German storage hydropower: 40 GWh
1d Earth/Moon System E-loss: 77 TWh | 1d electrical consumption mankind: 53 TWh | Energy stored in all BEVs*): O(0.5 TWh) World storage hydropower: O(1 TWh)
 | 1d total consumption humankind: 360 TWh | Energy storage seems not to scale up!
Accelerators are in the range were they become relevant for society and public discussion.
Desired turn to renewables is an enormous task; storage is the problem, not production!
Fluctuations of energy availability, depending on time and weather, will be large!
*) Battery Electric Vehicle

## Slide 6: Power flow in Accelerators
Electricity grid
Accelerator
Radio Frequency
Magnets
Vacuum etc.
Auxiliary systems
Cryogenics
Conv. cooling, AC etc.
Instruments
E.g. particle detectors
Computing
conversion to secondary radiation (beam collisions, targets, undulators …)
direct beam application:
p-therapy
Isotope production
secondary radiation
Exotic particles, e.g. Higgs, B-mesons
Photons (synchrotron radiation)
Neutrons
Muons
Possible figures of merit:
Number of physics events, secondary particles, X-rays on sample … per kWh consumed
beam
Eventually all converted to waste heat !
M. Seidel/PSI

## Slide 7: Efficiency , definition
Smaller efficiency
Larger efficiency
consumed energy
rejected energy
(normally heat)
useful energy
=
consumed energy
useful energy
=
consumed energy
consumed energy
rejected energy
(normally heat)
Definition as a ratio makes sense only for an energy-converting sub-system.
For an accelerator facility, we need other figures of merit!
Note:
larger means less energy consumed,
less energy wasted and smaller installation!
outcome
outcome

## Slide 8: Adapted definition
For High-Energy Physics: Instantaneous luminosity per gid power used … or better:
Integrated luminosity per primary energy supplied, measured in units of
.
Using the integrated definition illustrates how system availability and energy management enter the equation:
  In case of failure, no luminosity is produced but energy continues to be supplied.
  In case of failure, transients on the supply grid may occur and must be managed.
.

## Slide 9: RF power generators – typical efficiencies
 | Tetrodes (and diacrode) | IOTs (Inductive Output Tubes) | Conventional klystrons | Solid State PA | Magnetrons
range: | DC – 400 MHz | (200 – 1500) MHz | 300 MHz – 1 GHz | DC – 20 GHz | GHz range
class (CW): |  |  |  | 1 kW @ low | 
typical : | 85% - 90% (class C) 65% - 78% (class B) *) | 70% | 50% | 60% | 90%
Remark | Broadcast technology, widely discontinued |  | new idea promises significant increase | Requires combination of thousands! | Oscillator, not amplifier!
 | Tetrodes (and diacrode) | IOTs (Inductive Output Tubes) | Conventional klystrons | Solid State PA | Magnetrons
 | DC – 400 MHz | (200 – 1500) MHz | 300 MHz – 1 GHz | DC – 20 GHz | GHz range
 | 85% - 90% (class C) 65% - 78% (class B) *) | 70% | 50% | 60% | 90%
Remark | Broadcast technology, widely discontinued |  | new idea promises significant increase |  | Oscillator, not amplifier!
M. Jensen: EnEfficient RF Sources, 2014, Daresbury
Thales RS 1084 CJ
< 30 MHz, 75 kW
(class B)
CTF3 klystron
, , , ,
*) Electronic efficiency, not including heater & input power.

## Slide 10: Recent Multi-beam IOT program (1/2)
In order to provide an alternative to klystrons, ESS launched a R&D program for Multi Beam IOT.
Two prototypes were delivered and tested.
The goal was 1.3 MW @ 704 MHz pulsing up to 3.5 ms – 14 Hz
CERN contributed building a test place and performing tests.
Program concluded in 2018.

## Slide 11: Recent Multi-beam IOT program (2/2)
Chart: @ 704.42 MHz
| 300 | 400 | 600 | 800 | 1000 | 1200 | 1300 | 1400
YL1530 @ 200 MHz | 44 | 50 | 59 | 66 | 70 | 72 | 71.5 | 69
Chart: @ 704.42 MHz
| 300 | 400 | 600 | 800 | 1000 | 1200 | 1300 | 1400
YL1530 @ 200 MHz | 40 | 45 | 54 | 60.5 | 65 | 68 | 69 | 69
Chart: @ 704.42 MHz
| 300 | 400 | 600 | 800 | 1000 | 1200 | 1300 | 1400
YL1530 @ 200 MHz | 40 | 45 | 54 | 60.5 | 65 | 68 | 69 | 69
Operating point
RF/DC efficiency = 70 %
Operating point
RF/DC efficiency = 72 %

## Slide 12: Average RF power needs of large HEP Projects
CLIC 3 TeV: Pulsed, 1 GHz,
FCC-ee: CW, (0.4 & 0.8) GHz,
ILC 0.25 TeV: Pulsed, 1.3 GHz, *)
*): Estimated value from https://arxiv.org/abs/1903.01629
TDR values for 500 GeV: (68…92) MW, depending on region.

## Slide 13: Example FCC-ee : orders of magnitude
Grid to DC: 90%
RF power generation!
RF distribution!
losses in cavities
RF to beam
Eventually, all is converted to waste heat!
Figure of merit: physics results per MWh!
… or:
Note: largest impact by RF power generation
P. Lebrun

## Slide 14: Higher Efficiency Klystrons
… more details in following session (“Energy Efficient Vacuum Tube Devices”)

## Slide 15: The value of increased , e.g. 70%  80%
 | klystron 70% | klystron 80% | Difference
RF power needed (e.g. FCC-ee) |  |  | 
DC input power |  |  | 
Waste heat |  |  | 
Annual consumption (5500 h assumed) |  |  | 
Annual cost (60 CHF/MWh assumed) |  |  | 
Electricity installation dimensioned for |  |  | 
CV installation dimensioned for… |  |  | 
 |  |  | Difference
RF power needed (e.g. FCC-ee) |  |  | 
DC input power |  |  | 
Waste heat |  |  | 
Annual consumption (5500 h assumed) |  |  | 
Annual cost (60 CHF/MWh assumed) |  |  | 
Electricity installation dimensioned for |  |  | 
CV installation dimensioned for… |  |  | 
All the above gains are significant!
R&D on increasing the useable efficiency is worth every penny/cent invested!
Potential saving: 1.04 TWh in 10 years 63 MCHF in 10 years

## Slide 16: How does a klystron work?
A continuous electron beam is accelerated by a DC voltage and guided by magnets,
A small power RF input causes an RF voltage in the input gap, where the velocity of the electrons will be modulated with the RF.
Passing though a subsequent drift tube, this velocity modulation will lead to density modulation (bunching).
The density modulation causes an RF component of the current which will excite large power in the output gap.
With just input cavity and output cavity, the maximum possible efficiency of a klystron is 58%.
Additional cavities (near the operation and possibly at harmonics) will help the bunching process.
The best efficiency reached this way is around 70%.
Space charge effects limit the efficiency – they can be reduced using many small beams rather than one big (Multi-beam klystron – MBK)
From A.S. Gilmour, Jr. “Microwave Tubes”, Artech House 1986, who took this from Microwave Tube Manual by Varian Associates, Air Force Publication Number T.0.00-25-251, 1979

## Slide 17: MBK developments for CLIC
Frequency: 1 GHz
Peak power: 20 MW
Pulse length: 150 sec
Rep. rate: 50 Hz
Efficiency: >67%
Recommended by industry
Optimised at CERN
Simulated klystron efficiency vs. perveance
I Syratchev/CERN

## Slide 18: A promising new concept (2013)
RF=78.0%
Useful RF phase
Normalised velocity
Normalised velocity
RF period, rad
RF=89.6%
Normalised velocity
RF period, rad
Bunch phase
Bunch phase
0
0
2
2
Output cavity
Output cavity
http://ieeexplore.ieee.org/xpl/articleDetails.jsp?arnumber=7194781
‘’Classical” bunching
New bunching with core oscillations (COM)
I Syratchev/CERN

## Slide 19: Comparison of the two bunching methods
RF extraction efficiency: 86.6%;
N beams = 8
V = 180 kV
I total = 128 A
COM
conventional
10 MW ILC
20 MW CLIC
20 MW CLIC
8 beams
1 beam
I Syratchev/CERN

## Slide 20: Magnetrons

## Slide 21: Magnetrons (?)
Magnetrons are oscillators, not amplifiers, which is a problem (unless you can operate your whole accelerator with one).
… but they promise very high efficiencies, which makes them attractive. Consumer electronics magnetrons are very cheap (e.g. microwave ovens)
A possibility: injection-locking!
Adler’s formula: .
To make this work, you will tune the magnetron free oscillation frequency close to your operating frequency ().
… and then you also need to adjust the phase!
Adler, R., "A Study of Locking Phenomena in Oscillators," Proceedings of the IRE , vol.34, no.6, pp. 351-357, June 1946

## Slide 22: Electronic efficiency – klystrons vs. magnetrons
1.09 GHz
1.09 GHz
2.45 GHz
1.5 GHz
500 MHz
352 MHz
11.5 GHz
industrial empirical limit for conventional klystrons
Magnetrons
Klystrons
High efficiency klystrons (I. Syratchev)
H. Wang, IPAC 2019, Melbourne, WEXXPLS1

## Slide 23: Tune by trimming the magnetic field
Trimming the field to adjust close to zero, an acceptable spectrum can be obtained.

## Slide 24: Combining the power of 2 magnetrons
Y. Zhang et al.: https://ieeexplore.ieee.org/document/8032501

## Slide 25: Solid-State Power Amplifiers

## Slide 26: Definitions
Drain efficiency (or collector efficiency):
“Total efficiency”:
Power added efficiency:
Normally,

## Slide 27: LDMOS SSPAs
LDMOS transistors have made their appearance as replacements for vacuum electronic devices, at least at the 1-kW-level.
Advantages: Operation at lower voltage, no heater, better lifetime, rugged, modularity allows system design for graceful degradation.
Disadvantages: not forgiving overdrive, modularity requires power combination of very many devices (thousands), moderate efficiency!
Recent examples: ESRF 350 MHz (left), CERN 200 MHz (right).

## Slide 28: Overdrive (1/3)
Chart: Grid tubes
| 0 | 0.14857142857142858 | 0.29428571428571426 | 0.45 | 0.61428571428571432 | 0.79285714285714282 | 1 | 1.3142857142857143 | 1.8871428571428572 | 3.2142857142857144 | 6.4285714285714288 | 0.54545454545454541 | 0.61818181818181817 | 0.72727272727272729 | 0.83636363636363631 | 0.98181818181818181 | 1 | 1.1272727272727272 | 1.3090909090909091 | 1.509090909090909 | 1.7636363636363637 | 2.0363636363636362 | 2.3636363636363638 | 2.4727272727272727 | 3.676408537275877E-2 | 0.16810482465774959 | 0.30804216967959258 | 0.44534997545593652 | 0.59379996727458195 | 0.75953918166077616 | 0.999381782168974 | 1.2091871815897948
Grid tubes | 0 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.1667 | 1.3333 | 1.5 | 1.6667
Operating point
Including overhead
for LLRF and margin for availability
Operating point
RF/DC efficiency = 70 %
Possibility of short power excursions for LLRF
only for gridded tubes (possible for SSPA at a cost
of an overdesigned system)
Eric Montesinos, Proton Driver Efficiency Workshop, PSI 2016

## Slide 29: Overdrive (2/3)
Chart: Grid tubes, Klystrons
| 0 | 0.14857142857142858 | 0.29428571428571426 | 0.45 | 0.61428571428571432 | 0.79285714285714282 | 1 | 1.3142857142857143 | 1.8871428571428572 | 3.2142857142857144 | 6.4285714285714288 | 0.54545454545454541 | 0.61818181818181817 | 0.72727272727272729 | 0.83636363636363631 | 0.98181818181818181 | 1 | 1.1272727272727272 | 1.3090909090909091 | 1.509090909090909 | 1.7636363636363637 | 2.0363636363636362 | 2.3636363636363638 | 2.4727272727272727 | 3.676408537275877E-2 | 0.16810482465774959 | 0.30804216967959258 | 0.44534997545593652 | 0.59379996727458195 | 0.75953918166077616 | 0.999381782168974 | 1.2091871815897948
Grid tubes | 0 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.1667 | 1.3333 | 1.5 | 1.6667
Klystrons | 0.593 | 0.67 | 0.763 | 0.876 | 0.979 | 1 | 1.092 | 1.219 | 1.284 | 1.312 | 1.311 | 1.282 | 1.275
Operating point
Including overhead
for LLRF and margin for availability
Operating point
RF/DC efficiency = 70 %
Possibility of short power excursions for LLRF
only for gridded tubes (possible for SSPA at a cost
of an overdesigned system)
klystrons saturate, but tolerate overdrive
Eric Montesinos, Proton Driver Efficiency Workshop, PSI 2016

## Slide 30: Overdrive (3/3)
Chart: Grid tubes, Klystrons, SSPA
| 0 | 0.14857142857142858 | 0.29428571428571426 | 0.45 | 0.61428571428571432 | 0.79285714285714282 | 1 | 1.3142857142857143 | 1.8871428571428572 | 3.2142857142857144 | 6.4285714285714288 | 0.54545454545454541 | 0.61818181818181817 | 0.72727272727272729 | 0.83636363636363631 | 0.98181818181818181 | 1 | 1.1272727272727272 | 1.3090909090909091 | 1.509090909090909 | 1.7636363636363637 | 2.0363636363636362 | 2.3636363636363638 | 2.4727272727272727 | 3.676408537275877E-2 | 0.16810482465774959 | 0.30804216967959258 | 0.44534997545593652 | 0.59379996727458195 | 0.75953918166077616 | 0.999381782168974 | 1.2091871815897948
Grid tubes | 0 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.1667 | 1.3333 | 1.5 | 1.6667
Klystrons | 0.593 | 0.67 | 0.763 | 0.876 | 0.979 | 1 | 1.092 | 1.219 | 1.284 | 1.312 | 1.311 | 1.282 | 1.275
SSPA | 0.025333 | 0.16667 | 0.33333 | 0.5 | 0.66667 | 0.83333 | 1 | 1.0833
Operating point
Including overhead
for LLRF and margin for availability
Operating point
RF/DC efficiency = 70 %
Possibility of short power excursions for LLRF
only for gridded tubes (possible for SSPA at a cost
of an overdesigned system)
SSPAs do not tolerate overdrive!
Eric Montesinos, Proton Driver Efficiency Workshop, PSI 2016

## Slide 31: GaN SSPAs
Using gate pulsing, high efficiencies are currently possible with 150 V GaN HEMTs (up to 85% at 1 kW, 1 GHz).
Gate pulsing implies relatively short pulses and low duty cycles ().
Even without gate pulsing, efficiencies of 80% seem possible.
1 GHz Si LDMOS transistor
1 GHz GaN HEMT
J. Cluster, G. Formicone, J. Walker: https://ieeexplore.ieee.org/document/7492071 and https://ieeexplore.ieee.org/document/7777488

## Slide 32: Summary
Future HEP installation require RF powers . To satisfy these requests, high efficiency is imperative!
Concerning present-day technologies:
  Using novel bunching techniques, klystrons have recently made a technology leap forward in terms of efficiency.
  Magnetrons look interesting once sufficient phase stability can be reached.
  SSPAs, notably based on GaN HEMTs, show significant potential.
Investment into R&D towards higher efficiency RF power sources promises excellent return! … not only in financial savings, but also for the community!
In addition to electronic efficiency, energy management and system availability are equally key to overall energy efficiency.

## Slide 33: Spare slides

## Slide 34: Making best use of RF power

## Slide 35: Optimum beam loading: vs. gradient
Full beam loading – optimum efficiency
(operating point for CLIC drive beam)
Choice for CLIC 3 TeV
: RF to beam efficiency
Choice for CLIC 380 GeV

## Slide 36: Real of cryogenic He refrigeration
P. Lebrun/CERN
930
230
COP: Coefficient of performance: To extract at , one needs at .

## Slide 37: The operating for superconducting cavities
At lower , the cavity increases, so the dynamic loss decreases.
On the other hand, the cryogenic efficiency gets worse at lower .
Trading these two effects off leads to an optimum operating
Red:
Blue:
Example: 800 MHz 5-cell cavity for 18 MV, is the cryogenic power at ambient temperature. Thanks: R. Calaga, S. Claudet, P. Lebrun!
F. Marhauser, IPAC 2014, “Cost Rationales for an SRF proton Linac”

## Slide 38: State of the art: High , N2 doping
A. Grasselino, SRF2013 & M. Liepe SRF2015

## Slide 39: Recent results with Nb3Sn coated cavities
Daniel Hall, SRF 2015, Whistler, CDN

## Slide 40: Figure of merit for proposed lepton colliders
Chart: 
| 0.25 | 0.5 | 1
ILC | 1.0465 | 1.118 | 1.7193
CLIC | 0.89286 | 1.0165 | 1.0017
FCC-ee | 177.6062 | 20.2166 | 6.0284 | 0.91176
MAP-MC | 0.004 | 0.5787 | 1.913 | 4.4444
Disclaimers:
This is not the only possible figure of merit
The presented numbers have different levels of confidence/optimism; they are still subject to optimisations
(2 IPs)
Numbers for baseline proposals

## Slide 41: Figure of merit for proposed proton colliders
HL-LHC: , ,
FCC-hh: , ,