## Slide 1: Design study for the High Efficiency X-band Klystrons at CERN
Jinchi Cai Fellow, CERN
Igor Syratchev Staff, CERN
KlyCv4

## Slide 2
S-band/Industry
XL5
50 MW
X-Toshiba
6 MW
X-CLIC
8 MW
X-CLIC
50 MW
L-FCC
1.3 MW
UHF-LHC
0.4 MW
Established empirical limit
XP4
75 MW
L-MBK ILC
10 MW
L-MBK CLIC
20 MW
‘Ultimate’ technical limit (IJZ)
UHF-LHC
0.3 MW
Designed at CERN (PIC & KlyC)
Industrial tubes
The new klystron bunching technologies have been established and evaluated.
The computer code KlyC/2D and special scaling procedures have been developed.
A number of high efficiency klystrons has been designed (yet on paper).
S-Toshiba
6 MW
First HE industrial prototype (stability issues)
High efficiency klystron development at CERN

## Slide 3: Outline
Background and design goal for 8MW Klystron
RF circuits design
Beam optics & RF launcher design
Summary & Cost effective design
Latest progress on 50MW X-band Klystron

## Slide 4: Toshiba E37113
FCI simulation: 47%, measured saturated efficiency ~43%
Large beam aperture to accommodate large current
Multiple (3) cells output coupler.
Y. Okubo, et al. Development of an X-band 6MW Pulsed Klystron
In operation at X-box 3
As of 01.11.2018

## Slide 5: 6 MW tube. Roadmap for the new design
Beam voltage, current are not changed. Electron gun design is preserved. (3)
COM method adopted for X band. The beam-wave interaction design should be re-done. (1)
Collector should be re-designed to accommodate the updated spent beam. (2)
Magnetic system should be adjusted to guide the beam through longer transmission. (3)
Performance evaluation of entire device. (4)

## Slide 6: Outline
Background and design goal for 8MW Klystron
RF circuits design
Beam optics & RF launcher design
Summary & Efforts to improve…
Latest progress on 50MW X-band Klystron

## Slide 7: Coupled modes theory implanted into KlyC/2D
 | F1 | F2 | F3
Coupled theory | 11.7704+0.0406j | 12.0114+0.1308j | 12.1735+0.0364j
HFSS eig. | 11.7710+0.0377j | 12.0051+0.1325j | 12.1722+0.0378j
CST MWS | 11.77111+0.0382j | 12.00470+0.1325j | 12.17316+0.0376j
3cells structure. KlyC vs. CST/3D benchmarking
Monochromatic bunch.
Congregated bunch
1
2
3
Paper submitted to IEEE TED

## Slide 8: Preliminary Design Process (KlyC)
1D with artificial output cavity(M=0.9): 73%
2D with artificial output cavity—64%
Initial opt.
Check
2D with real output cavity—48%
Opt.
2D with real output cavity(M=0.5): 54%
Emax>200MV/m

## Slide 9: Output coupler evolution
Gap length
eff.
Emax
2mm
Efficiency can’t reach 60% level with a single cell design
Maximum E field is much larger than 100MV/m when eff>50%
Multiple cells structure should be adopted to increase the efficiency and to keep a reasonable surface Emax
Type | fake | 1cell_1mm | 1cell_2mm | 2cell | 3cell | 4cell
efficiency | 67.6% | 54.9% | 54.3% | 59.0% | 59.5% | 60.4%
Min(ve/c) | -0.23 | -0.03 | -0.02 | 0.03 | 0.03 | -0.05
EmaxMV/m | ~ | 330MV/m | 232MV/m | 87MV/m | 80MV/m | 82MV/m
For the fixed gap of 2mm and period of 4mm (0.9mm fillet radius), couplers with different number of cells were analyzed. The frequencies, locations, Qext were optimized to find optimum eff. for the given bunching circuit.
4-cell design was benchmarked with CST; eff=58.5%
Efficiency degradation

## Slide 10: Optimization of the entire tube
Use max eff. as the target. Optimization is done by adjusting the frequencies and positions of all the cavities.
The maximum surface E-field is not a constraint yet in this optimization.
One more gain cavity is added to the RF circuit to increase power gain without efficiency degradation.

## Slide 11: Optimized design with 4-cell coupler (KlyC)
62.8% efficiency (Emax=90MV/m)

## Slide 12: PIC CST/3D benchmarking
Phase space movie in CST
KlyC reference
60.5% efficiency with Bz=2.5Br
~100MV/m
This is high efficiency design. The maximum surface field is not well addressed
~0.1% beam power interception

## Slide 13: Optimization of the coupler
Emax reduced by 20%, eff. dropped by 2%.
The bandwidth curve and power transfer curve is almost the same
More uniform field distribution
Pin=80W
f=11.994GHz
eff=60.2%
Emax=70MV/m
eff.~58%, Emax~82MV/m

## Slide 14: RF circuit design. Short summary.
Nominal output power=8MW
-1dB bandwidth>60MHz
Surface field Emax ~ 80MV/m
No instabilities observed with parameter swept
Beam radius does not affect saturation efficiency

## Slide 15: Outline
Background and design goal for 8MW Klystron
RF circuits design
Beam optics & RF launcher design
Summary & Cost effective design
Latest progress on 50MW X-band Klystron

## Slide 16: CST/3D. Solenoid design.
90
380
Bz=0.38T
Design is scaled from the Toshiba’s original solenoid. Magnet is larger to ensure uniform 0.38T along 0.3 m section.
Magnetic field distributions near The gun and collector are not yet optimized.
1.8kW to 5.9kW
0.32T to 0.38T
150mm to 300mm

## Slide 17: Collector design by TRK simulation
Fast simulation by MATLAB code, which is benchmarked by CST TRK, dP/dS<50kW/cm2
Bz=0T
Fake DC gap
40% Vg
100% Vg
40% Vg
Vg spread=0.4
dP/dS< 40kW/cm2; 150kW/cm2 for diode mode

## Slide 18: Gun Design with bucking coil (Bz=0.38T)
Export/import interface
SC limit TRK model
PIC model
Bz profile/ Final design
Geometry from Cannon

## Slide 19: PIC RF simulation with Gun and collector
DC: stable without oscillation
RF: Stable amplification signal
Eff.=58.6%

## Slide 20: Single waveguide coupler design
1
2
1- coaxial waveguide for input
2- double WR for output
Field axial symmetric is good, but not convenient for fabrication
Single WR coupler should be substituted without much perturbation to Qext and field symmetry
0.36mm
0.64mm
Input cavity
Output cavity
R=2.5mm
(Emax-Emin)/Eaver/2=1.6%
(Emax-Emin)/Eaver/2=4.9%

## Slide 21: Other realistic features
10MW
34kV/mm
100W
0.07kV/mm
Coupler to WR90
Transition section guarantees the reflection less than -30dB
All the intermediate cavities are rounded by 1mm at the nose
The frequencies of all the cavities should be adjusted little a bit to compensate the lower coupling caused by rounding
KlyC simulation is done before final verification by CST PIC

## Slide 22: Outline
Background and design goal for 8MW Klystron
RF circuits design
Beam optics & RF launcher design
Summary & Cost effective design…
Latest progress on 50MW X-band Klystron

## Slide 23
KlyC optimization is done with the field from real cavity design
Eff=58.5%
Min(ve/c)=0.045
Emax=73kV/mm
CST model is re-tuned accordingly with every feature included
SW+TW

## Slide 24
100W
8MW
154kV,90A
All in one simulation is done in CST
22 million mesh cells
2 million particles
~ 1 day on 2-cores GPU
~1 month on CERN server
Min(ve/c)=-0.059
Eff.=58.1%
Bz field imported from solenoid system
57dB
Emax=85MV/m
250W
27kW

## Slide 25: Performance summary
60MHz
9MW Max.
Well consistent with CST

## Slide 26: Cost effective design effort in collaboration with CANON
Tapering the tunnel of output cell to avoid beam interception in output gap
Optimize the output cell gap to avoid very strong surface field
Optimize of the frequencies, positions, Qext are done in KlyC
Shorter length means less solenoid power, less fabrication cost
COM for inner layer, Classic for outer layer
Whole tube optimization is done
Eff=57.5%, Emax=86kV/mm for KlyC simulation

## Slide 27: Original long tube 4 cell output structure design
Eff.~58.5%
Emax~73kv/mm
Ve/c~-0.03
-1dB bandwidth~[-30MHz,10MHz]
Pin=130W
L~300mm
Rc after circuit~4.0mm
Eff.~57.4%
Emax~87kv/mm
Ve/c~-0.08
-1dB bandwidth~[-20MHz,15MHz]
Pin=80W
L~140mm
Rc after circuit~4.2mm
Updated short tube 3 cell output structure design

## Slide 28
Beam interception occurs after the output structure, ~17kW
Decrease input power by 10% will lead to 6kW beam interception with 0.5% efficiency dropping down
Bz=0.38T
Stable tube without reflected electrons
Minimal velocity is -0.071c, which is consistent with KlyC
Emax~95kV/mm
Occurs at the last but one cell
Coupled modes operated
CST verification
Eff.=56.5%
Further polishing in PIC simulation is still necessary

## Slide 29: Outline
Background and design goal for 8MW Klystron
RF circuits design
Beam optics & RF launcher design
Summary & Cost effective design
Latest progress on 50MW X-band Klystron
I. Syratchev
J. Cai
A. Jensen
B. Weatherford
J. Neilson
V. Dolgashev

## Slide 30
50 MW HEX tube progress
The 6 cell coupler was digitized for KlyC (cell frequencies, fields and coupling matrix). In KlyC, the RF power generation efficiency when excited with idealized bunched beam was 70%+ and surface E field ~90 MV/m, similar to CST/3D results.
The RF bunching circuit was scaled from 8MW HE klystron and re-optimised using artificial and efficient cavity. The 70% efficiency was predicted KlyC/2D.
Whole tube optimization (L<400mm) in KlyC is done. CST benchmark is undergoing.
Status
V0=400kV, I0=190A
Tapered 6 cell coupler
Congregated bunch
Monochromatic bunch

## Slide 31
Thanks! Questions?