## Slide 1: SOLEIL Long Term SSPA Operational Experience
ARIES Workshop on Energy Efficient RF
Ångström Laboratory, 18-20 June 2018
Massamba DIOP
On Behalf of the RF & LINAC Group

## Slide 2
SOLEIL Booster first SSPA (Pnom = 35 kW @ 352 MHz) :
Pmod ≈ 300 W ; n1 = 8  2.4 kW ; n2 = 8  19 kW ; n3 = 2  146 RF modules (128 Ampli + 18 Pre-A)  Pout ≈ 38 kW
Combining in // a number of elementary amplifier modules (or pallets) of a few 100 W (up to ~ 1 kW)
Few kW unit
x kW
- MOSFET (Vd = 30 - 50 V)  No HV & Low phase ripple
- Circulator & its load to ensure a good isolation (even a small residual VSWR can affect the MOSFET power capability !!)
 Modularity & Redundancy inherent to such a design
Few 100 kW unit
≈
≈
≈
≈
1:n3
n3:1
x 10 kW
x 10 kW
Driver
ampli
⇔
≈
≈
≈
≈
n1 Ampli modules
1:n1
n1:1
Pre-
ampli
x 10 kW
≈
≈
≈
≈
x n2
1:n2
n2:1
x kW
x kW
Few 10 kW unit
⇔
Pre-
ampli
The number of pre-ampli depends on the module gain
SSPA Principle
x n3

## Slide 3
~ 77 000 running hours over 14 years and only one single trip from the SSPA, in August 2016,
due to a loose connection on a monitoring cable (down time ~ 2.10-5 and MTBF ~ 38 000 hours)
~ 1 module failure / year, without impact on the operation, thanks to the modularity and redundancy
300 W CW - 352 MHz amplifier module
VDMOS D1029UK05 from SEMELAB
(G = 11 dB, ƞ = 62 %)
600 W - 280 / 28 V dc
power converter
Power combiner
(8 x 8 x 2)
8 dissipaters of
16 + 2* modules
* Pre-amplifiers
35 kW
Circulator
8 x 300 W
All amplifier components were designed in house and the mass production contracted to industry
In 2005, world record for a SSPA
Booster Original 35 kW SSPA
Notes: 146 modules of 300 W @ 352 MHz & individual power supplies, mounted on 8 water cooled dissipaters

## Slide 4
A new 60 kW SSPA for the Booster
Upgrade plan :
Former spare cavity installed in one straight section of the Bo ring and powered with 60 kW (VRF = 1.8 MV)
New 60 kW - 352 MHz SSPA, identical to a standard tower of our SR amplifiers
(10 dissipaters of 16 modules, built from 160 RF modules of 400 W with BLF574XR transistors and their dc-dc converters made available by the SR SSPA refurbishment)
SSPA and its associated LLRF & control (replica of the actual one) inside the Bo RF room
Increase VRF of the existing plant from 1 MV up to 1.2 MV  PRF ~ 30 kW (Pbeam ~ 0)
Booster RF system was originally designed for standard operation
The 35 kW amplifier drives a 5-cell copper cavity => VRF = 1 MV (Pdiss = 20 kW ; Pbeam = 5 kW  Ptot = 25 kW)
But low-ɑ operating mode suffered from a low injection efficiency (15-20%) due to the long BO bunches
 Heavy safety radiation constraints
 Prevents more beam lines to join this operating mode
2nd RF station installed to increase VRF from 1 MV up to 3 MV in winter 2017-2018
Shorter bunch length  SR injection efficiency improved by a factor of ~ 2 in low-ɑ operation
‘Upgraded’ Low-ɑ operating mode available for users since October 2018
with VRF = 3 MV (SR injection efficiency = 35% instead of 18% before).
+ power savings and redundancy in all other operating modes

## Slide 5
Same principle as the BO one but extended to 4 towers of 45 kW:
  10 dissipaters of 18 modules per tower
  726 modules / amplifier x 4 cavities  16 towers & ~ 3000 modules
Amplifiers 1 & 2 (2 x 4 towers)
powering the 2 cavities of
Cryomodule 1
600 W - 280 Vdc / 28 Vdc
LDMOS LR301 from POLYFET
G : 13 dB, η : 62 %
Combiners
Splitters
A1
A2
Still a world record for SSPA?
Soleil SR 180 kW SSPA’s

## Slide 6
Top transistor currents
Bottom transistor currents
Pi & Pr
2.5 kW combiner
Multiplexing (I x 2 x 680 mod. + Pi & Pr x 80)  single µcontroller for 1 complete amplifier (4 towers)
Tower T4 of
Amplifier 2
SR SSPA Control

## Slide 7
Equipment | MTBF | Downtime | Comments
a) 4 x RF amplifiers | ~ 12 500 h | ~ 1 10-4 | Failures from preamplifiers and 1st stage combiners
b) 4 x 500 kVA thyristor-based 230 Vac / 270 Vdc rectifiers | ~ 8 000 h | ~ 4 10-4 | Single rectifier per amplifier
a) + b) 4 x RF transmitters | ~ 5 000 h | ~ 5 10-4 | 
MTBF & beam downtime, cumulated by the 4 SR SSPA’s over ~ 70 000 running hours in ~ 13 years
Already excellent MTBF and operational avaibility
  But still perfectible
  - providing some more redundancy
  1) in the ac-dc power conversion, which originally
  consists in a single 500 kW rectifier per SSPA
  2) in the preamplifier stage, a failure of one of them
  switching the RF off automatically
  - improving the power capability of the 1st stage combiners
   Cures for these “weaknesses” in our new design
SR SSPA’s Operational Results

## Slide 8
180 kW SSPA’s Refurbishement
The failure rate of our original LR301 transistors remains significant, stabilized ~ 2% a year from 2012-2013.
2 types of failures identified: - Transistor breakdown
- Damaged soldering due to thermal fatigue
 Since 2013, on going refurbishment
LR301 replacement by 6th generation BLF574XR (Vd = 50V instead of 30V with better performances)
More robust transistor and lower thermal stress  longer lifetime  less maintenance
 failure of a single « new » transistor (~ 6 years of operation)
+ 7 dB transistor gain  160 modules & their dc PS are got back for the new BO SSA
Pmod increased : 315 W  450 W
Electrical power savings (efficiency : 50 %  60%) compensate the investment cost in < 3 years

## Slide 9
1
80
24W
190kW
3W
300W
24kW
1
80
24W
190kW
3W
300W
2.4kW
300W
24kW
Present config : each pre-ampli drives 80 modules; if one of them fails the amplifier is stopped
Pre-ampli
Upgrade
Thanks to the combiner-divider, the failure of a pre-ampli does not affect the functioning anymore
Cure the lack of redundancy in the pre-amplification stage  develop a “combiner-divider”
180 kW SSPA’s Refurbishement
Modification of the 2.5 kW combiners (welded  screwed connections) to increase their power capability

## Slide 10
12 of the 16 towers already refurbished (~ 2400 modules)  rate of 5 towers a year until 2020 with SOLEIL and external resources
Storage Ring RF upgrade Status
Present : Now we can store 450 mA with 3 running SSPA’s or 500 mA with 3 running cavities
In 2020 (end of refurbishment) : Possibility to store 500 mA with 3 running SSPA’s / cavities or 450 mA with a single cryomodule, combining 2 SSPA’s per cavity
180 kW SSPA’s Refurbishement

## Slide 11
P1
P2
P2
P1
P2
P1
P1+P2
P1
P2
P3
P4
P3+P4
P1+P2
OR
depending on the post configuration
Connecting 2 Magic Switches
CM2
CM1
Waveguide network layout to power one or the other CM with 300 kW / cav from the 4 SSPA’s, combined by pairs
« Magic Switch »
Modification of the waveguide network to combine the power from two amplifiers into one cavity  Possibility of storing the full beam current using a single CM
Toward storing 450 mA using a single CM
The 2 Magic Switches implemented and waveguide distribution completed in end-2018

## Slide 12
SOLEIL SSPA R&D
Scientific Collaborations
and Technology Transfers

## Slide 13
SOLEIL R&D with 352 MHz SSPA’s
Development of new RF modules, based on 6th generation LDMOS (Vd = 50V)
Pmod ~ 700 W, G ~ 20 dB,  > 70% at 352 MHz
[ With original LR301 (28V), Pmod = 315 W, G = 13 dB,  = 62 % @ 352 MHz ]
 Huge improvement : Pmod x 2.2 , better performance (G ,  , linearity) & strong reduction in thermal stress (ΔT : - 60 °C)  longer lifetime
ESRF project of partly replacing its 1 MW klystrons by 150 kW SSPA’s (1 per cavity)
 2009, SOLEIL transfer of technology with ELTA-AREVA
 7 SSPA’s of 150 kW, built by ELTA under SOLEIL license
BO : 4 x 150 kW SSPA’s in use since January 2012
2 trips in 7 years of operation  refill postponed
SR : 2 x 150 kW SSPA’s in use since October 2013
(3rd one stopped after few months due to cavity leak)
3 trips in 5 years of operation  beam loss (youth problems fixed)
BO + SR : ~ 1 820 transistors and not a single failure !
DC-to-RF efficiency of 58%, dc-dc converters included
With new ac-dc converters   (overall ac to RF) > 60%
ESRF 150 kW 352 MHz SSPA from ELTA/SOLEIL
2 towers of 75 kW ↔ 260 RF modules of 700 W

## Slide 14
LNLS – SOLEIL Collaboration
April 2010 in Campinas-Brazil : the SOLEIL - LNLS team, after successful tests of the amplifiers
Two SSPA’s of 50 kW @ 476 MHz for LNLS (Brazilian LS) SR * with components designed by SOLEIL (400 W modules with BLF574)
* A 2.5 kW 476 MHz SSA had already been built for the LNLS Booster

## Slide 15
LNLS 50 kW RF plants
The two 50 kW SSPA’s of the LNLS SR have run satisfactorily for > 8 years
 Use of SSPA’s @ 500 MHz in SIRIUS, the new LS under construction

## Slide 16
Experience feedback 
* + 10 pts in efficiency lead to electrical power savings over 10 years of operation ≈ full amplifier cost
  Modular dc-dc converters + single power rectifier replaced by modular 230 Vac / 50 Vdc converters, in 2 kW units, 96% efficiency, voltage remote control
   optimized efficiency for any operating power :
  56% (overall) @ Pmax and 50% @ 0.6 Pmax
RF output power, Pn : 650 W CW
Input return loss : - 40 dB at Pn
Unconditional stability (K >10 dB)
Gain : 17 dB at Pn (1 dB compression)
Efficiency ≈ 62 % at Pn
Gain dispersion : +/- 0.2 dB at Pn
Phase dispersion : +/- 5° at Pn
New 650 W - 500 MHz modules using 6th generation (Vd : 50V) LDMOS BLF578 from NXP
Modularity brought in the preamplification stage by inserting the « divider-combiner »
2 kW unit
controller
Increase effort on the modularity/redundancy and the efficiency *
Moderate power for long lifetime (thermal stress  soldering degradation)
R&D with 500 MHz SSPA at SOLEIL
Mandatory for good combining efficiency  Components for gain and phase adjustments

## Slide 17
500 MHz SSPA for ThomX(1) & SESAME(2)
ThomX 50 kW SSPA
(6 x 16 RF modules + 3 x 15 PS)
(1) ThomX : Compton X-ray source under construction in Orsay, France
(2) SESAME : Jordan Synchrotron light source
For SESAME SR : 4 x 80 kW SSPA  1st one built by SOLEIL as a demonstrator
 3 others on the same model by SigmaPhi Electronics (SPE), SOLEIL licensee since 2014
Status : all in operation (first pair since end 2016 and 2nd one since May 2017)
The ThomX 50 kW SSPA is also completed ; it is now being commissioned on site
  Fully modular 50V power supplies
  230 Vac / 50 Vdc converters,
  in 2 kW units, 96% efficiency, with voltage remote control for efficiency optimization
  Change from the tower to cabinet assembly, better suited with the new power supplies
Control upgrade  stand-alone, self-protected and more modular
(1 µcontroler per dissipater)
SESAME 80 kW SSPA
(10 x 16 RF modules + 5 x 16 PS)

## Slide 18
1.3 GHz SSPA for LUCRECE*
RF Power Source requirements for LUCRECE: 20 kW CW SSPA @ 1.3 GHz (SOLEIL - SPE collaboration)
Comparison between GaN and LDMOS technology
* RF R&D program for the French FEL project LUNEX5
Chart: Gain and Efficiency vs Pout
| 0.56115000000000004 | 1.1556040000000001 | 2.4446319999999999 | 5.206671 | 11.016477999999999 | 22.837921999999999 | 45.161327999999997 | 84.883118999999994 | 150.24931599999999 | 178.793645 | 194.37178599999999 | 211.49771200000001 | 228.45988700000001 | 248.50824800000001 | 270.47577699999999 | 293.99310300000002 | 319.14723900000001 | 346.17151799999999 | 375.09783499999998 | 403.27713899999998 | 430.92197099999998 | 453.93225000000001
Gain New Gen GaN | 20.2387 | 20.3882 | 20.6489 | 20.9396 | 21.1805 | 21.3068 | 21.2405 | 20.912 | 20.3194 | 20.0531 | 19.9093 | 19.7649 | 19.636 | 19.4889 | 19.3417 | 19.1916 | 19.0378 | 18.8845 | 18.7265 | 18.5416 | 18.3313 | 18.0805
Gain Old Gen GaN | 15.6194 | 17.1854 | 16.6027 | 16.486 | 16.371 | 16.2346 | 16.1069 | 15.9681 | 15.8031 | 15.6183 | 15.3946 | 15.1506 | 14.8754 | 14.525 | 14.1167 | 13.8493
Gain New Gen LDMOS | 7.6043 | 8.1196 | 8.9184 | 9.8944 | 11.1098 | 12.4372 | 13.8401 | 15.2929 | 16.4601 | 17.421 | 18.1782 | 18.3271 | 18.4671 | 18.5961 | 18.7061 | 18.8144 | 18.9097 | 19.0231 | 19.0802 | 19.1213 | 19.1371 | 19.1147 | 19.0514 | 18.9336 | 18.7395 | 18.4794 | 18.1611 | 17.7262 | 17.3516
Eff New Gen LDMOS | 0.51501 | 0.77562 | 1.2028 | 1.7986 | 2.7103 | 4.0363 | 6.057 | 9.2264 | 13.2446 | 18.5145 | 25.3686 | 27.2658 | 29.2588 | 31.3588 | 33.5781 | 35.8872 | 38.3138 | 41.8144 | 44.368 | 47.0165 | 49.6272 | 52.0001 | 54.2575 | 56.2419 | 57.777 | 58.8798 | 59.5919 | 60.113 | 60.3528
Eff New Gen GaN | 2.1135 | 3.4938 | 5.3406 | 8.0354 | 11.9158 | 17.2027 | 24.0776 | 32.3975 | 41.8607 | 45.1879 | 46.7701 | 48.4514 | 50.0354 | 51.8164 | 53.6837 | 55.5664 | 57.4243 | 59.3899 | 61.3539 | 63.1358 | 65.0278 | 66.2888
Eff Old Gen GaN | 0.18884 | 4.7623 | 21.1143 | 23.2292 | 25.527 | 28.3499 | 31.1606 | 34.087 | 37.1874 | 40.4271 | 44.022 | 47.4007 | 50.5722 | 53.3598 | 55.669 | 56.6772
 | Old Gen GaN | New Gen GaN | New Gen LDMOS
Vd (V) | 50 | 50 | 42
Pout (W @ 1 dB comp.) | 71.2 | 150.2 | 459.7
Pout (W @ 3 dB comp.) | 425.9 | 430.9 | X
Gain (dB) | 14.11 | 18.33 | 18.16
Efficiency (%) | 55.6 | 65 | 59.6
Efficiency (%)
Transistor performance measurements
X: not measured

## Slide 19
Other SOLEIL activities on SSPA’s
The 150 kW-500 MHz SSPA is already in the SPE catalogue
 2 x 75 kW (2 x 8 dissipaters of 16 modules) combined by
means of a wave guide to coaxial combiner, the WaCCo
R&D on VHF e-gun for LUNEX5
2 SSPA of 60 kW @ 176 MHz
800 W - 176 MHz RF modules
(compact 800 W - 176 MHz circulators developed
in collaboration with VALVO Bauelemente )
SOLEIL upgrade towards DLSR
6 & 7 BA / cell lattice  z < 100 pm
Main RF: Pbeam = 250 kW at 352 MHz  Re-use of our actual refurbished 180 kW SSPA’s (or part of them) + converter and control upgrade?
Harmonic system (n=4): adaptation of LUCRECE SSPA if the system is active
WaCCo
2 x 80 kW
WaCCo

## Slide 20
Summary & Conclusions
SOLEIL has pioneered the use of SSPA’s in particle accelerators
35 kW + new 60 kW in the BO and 4 x 180 kW in the SR with outstanding operational MTBF >> 1 year
BO RF upgrade  redundancy + SR injection efficiency improvement in low-ɑ operating mode (~ factor of 2)
2013: start of original transistor replacement by 6th generation LDMOS (Vd = 50 V instead of 30 V), much more robust and with higher gain and efficiency  Drastic reduction in module failures, higher power capabilities and efficiency + available components for the new 60 kW BO SSPA
SR SSPA refurbishment + “Magic switches” (+ Upgraded cavity couplers)  Additional redundancy
Possibility to store full Ibeam using either a single CM or 2 CMs with only 3 running amplifiers/cavities
SOLEIL R&D on SSPA  improvement of the original design in compactness, reliability and efficiency
Overall (plug to RF) efficiency ~ 65% at 352 MHz or lower frequencies, ~ 56% at 500 MHz and ~ 50% at 1.3 GHz
Scientific collaborations & technology transfers to the industry (ESRF, LNLS, ThomX, SESAME, LUCRECE, ...)

## Slide 21
Thank you for your attention