## Slide 1
Energy Efficiency of Accelerators
EUCARD-2 and ARIES WPs
Workshop on efficient RF Sources, Uppsala 2019
Mike Seidel (PSI)
E.Jensen, F.Gerigk (CERN), R.Gehring (KIT), C.Marchand (CEA), A.Lundmark (ESS), J.Stadlmann, P.Spiller (GSI), M.Wohlmuther (PSI)

## Slide 2: the energy problem
climate change causes critical reflections on the use of fossile energy carriers; nuclear power has other problems and is disputed; renewable energy sources are on the rise but have problems due to fluctuations
legitimate but often emotional discussions; impacts politics
 improving efficiency is a strategy in many countries, affects also research facilities
source Wikipedia:
„school strike for climate“
includes all carriers, today ≈ 18TW

## Slide 3: Example: PSI Facility, 10MW
Ring Cyclotron 590 MeV
loss  10-4
SINQ
spallation source
2.4 mA /1.4 MW
proton therapie center [250MeV sc. cyclotron]
dimensions:
120 x 220m2
Muon production targets
50MHz resonator

## Slide 4
public grid ca. 10MW
RF Systems 4.1MW
Magnets
 2.6MW
aux.Systems
Instruments
 3.3MW
Beam on targets
1.3MW
heat  to river, to air
neutrons
muons
cryogenics
example: PSI Facility, 10MW
n: per beamline:
1013s-1@ 10eV ≈ 20µW
+: per beamline
5·108s-1 @ 30MeV/c
≈ 300µW
similar conversion processes:
synchrotron radiation/FEL
muon/neutrino source
colliders, e.g. Higgs production

## Slide 5
Projects Eucard-2 and ARIES, co-funded by EC
Eucard-2: European Coordination for Accelerator Research, 2013…2017
www.psi.ch/enefficient:
task 1: energy recovery from cooling circuits, Th.Parker, A.Lundmark (ESS)
task 2: higher electronic efficiency RF power generation, E.Jensen (CERN)
task 3: short term energy storage systems, R.Gehring (KIT)
task 4: virtual power plant, J.Stadlmann (GSI)
task 5: beam transfer channels with low power consumption, P.Spiller (GSI)
ARIES: Accelerator Research and Innovation for European Science and Industry, 2017…2021
Efficient Energy Management: www.psi.ch/eem
task 1: High Efficiency RF Power Sources (C.Marchand / CEA, R.Ruber / Univ.Uppsala)
task 2: Increasing energy efficiency by increasing the efficiency of the spallation target station (M.Wohlmuther / PSI, L.Zanini / ESS)
task 3: High Efficiency SRF power conversion (F.Gerigk / CERN)
task 4: Efficient operation of pulsed magnets (P.Spiller, S.Haberer / GSI)

## Slide 6: Targets, or Conversion to Secondary Radiation
measure | gain
Zr cladding instead steel | 12%
more compact rod bundle | 5%
Pb reflector | 10%
inverted entrance window | 10%
total gain factor | 1.42
color code: neutron density on same scale
(MCNPX)
old
new
beam
beam
Example: neutron production target at PSI

## Slide 7: ARIES task: improving neutron flux per beam power
D2 Cold Source
p beam
Simulation of Spatial Neutron Flux Distribution in D2 cold source with MCNP
6 – 8 Å
4 – 6 Å
3.9 – 1 Å
[n/p/cm2]
Neutrons are produced by a 1MW p-beam impinging on a Pb-Target
Neutrons must be moderated to low energies (eV) using deuterium with low capture cross-section
M.Wohlmuther, PSI; L.Zanini, ESS

## Slide 8: Heat Recovery Workshop, Lund [Th.Parker, E.Lindström, ESS]
DESY, ALBA, SOLEIL, ESS, MAX-4, PSI, DAFNE, ISIS (institutes)
E.ON, Kraftringen, Lund municipality
lab survey on consumption and heat recovery
heat recovery works for many facilities; high temperatures beneficial
Heat pumps can be used to convert power to higher temperature level
new facilities MAX-4 and ESS foresee heat recovery on large scale
talks: http://indico.esss.lu.se/indico/event/148/

## Slide 9: Lab Survey: Energy Consumption & Heat [Master Thesis, J.Torberntsson, ESS]
Chart: Electricity consumption (GWh/y)
| 1.PSI | 2.ESRF | 3.ISIS | 4.KVI | 5.INFN | 6.ALBA | 7.GSI | 8.CERN | 9.SOLEIL | 10.DESY | 11.ESS | 12.MAX IV
 | 125 | 64 | 70 | 4.175 | 25 | 20 | 60 | 1220 | 36.768 | 150 | 270 | 65.625
10 in operation
2 under Construction
Energy consumption
Cooling methods
Energy related costs

## Slide 10: Low Power Accelerator Magnets
Workshop on Special Compact and Low Consumption Magnet Design,
CERN: indico.cern.ch/event/321880/
study: Ph.Gardlowski (GSI), systematic comparision of beam transport options
permanent magnets Pro: no power required, reliable, compact | Con: tunability difficult, large aperture magnets limited, radiation damage
optimized electromagnet Pro: low power, less cooling (+vibrations) | Con: larger size, cost
pulsed magnet Pro: low power, less cooling, high fields | Con: complexity, field errors
s.c. magnet Pro: no ohmic losses, higher fields | Con: cost, complexity, cryo installation
high saturation materials Pro: lower power, compactness, weight | Con: cost, gain is limited

## Slide 11: Permanent Magnet Quad Design for CLIC
NdFeB magnets with Br = 1.37 T
4 permanent magnet blocks
gradient = 15.0…60.4 T/m, stroke = 0..64 mm
Pole gap = 27.2 mm
Field quality = ±0.1% over 23 mm
Stroke =
0 … 64 mm
Tunable high-gradient permanent magnet quadrupoles, B.J.A. Shepherd et al 2014 JINST 9 T11006

## Slide 12: Pulsed Quadrupole Magnet [P.Spiller et al, GSI]
 | Prototype Quadrupole
Gradient | 80 T/m
Length | 0.65 m
Pulse length | 90 ms (beam 1 ms)
Peak current | 400 kA (35 kA)
Peak voltage | 17 kV (5 kV)
Energy @17 kV | 65 kJ (5.6 kJ)
Inductivity | 535 nH
Capacitor | 450 mF
Forces | 200 kN
Engineering model of the prototype quadrupole magnet incl. support
low average power; high field; energy recovery in capacitive storage possible for periodic operation (ongoing ARIES study)
complexity added by pulsing circuit; field precision potentially challanging

## Slide 13: superconducting structures for CW operation
voltage, dissipated power and cryogenic efficiency:
new developments:
N2 doping, high Q, low Pdissip
Nb3Sn cavities, high Q at 4.5K, thus better c
Systematic studies on flux expulsion (CERN, FNAL)
FNAL N2 doping
[S.Posen et al, FNAL]
Nb3Sn coated cavities
[M.Liepe et al, Cornell, IPAC19]

## Slide 14: Flux trapping workshop @ CERN, 8-9 Nov 2018
64 participants from the North America, Asia & Europe.
Supported by ARIES. Milestone: MS18, report
https://indico.cern.ch/event/741615/overview

## Slide 15: Proposed HEP Projects and Grid Power Consumption
 | ECM [TeV] | L / IP [cm-2s-1] | PGrid [MW] | major power driving effect
ILC | 1 | 4.9×1034 | 300 | beam power: 13.6 MW/beam, cryogenics
CLIC | 3 | 5.9×1034 | 582 | beam power: 14 MW/beam
FCC-ee (Z) | 0.091 | 2.3×1036 | 259 | SR Power: 50MW/beam
FCC-ee (t) | 0.365 | 1.5×1034 | 354 | SR power: 50MW/beam
FCC-hh | 100 | 3.0×1035 | 580 | SR power: 2.4MW/beam @ 50K, cryogenics
 col. | 6 | 1.2×1035 | 270 | advantages, least developed, cycling!, 1.6MW/drive beam (parameter example)
Energy consumption is critical not only for cost reasons, but more so for the perception of our field in the public.
Sustainability is a very high ranking topic in politics and public discussion
important scalings:

## Slide 16: cost volatility indicates huge fluctuations in supply and demand
Germany

## Slide 17: Energy Storage for Strategic Energy Management
LIQuid HYdrogen & SMES
development by KIT for general purpose:
hybrid SMES/LH2
[M.Sander, R.Gehring, KIT]
large power 10..100 MW
capacity to 70 GWh
SMES to 10 GJ
synergy with existing cryogenics
≈1.9k€/kW, ≈8.25 k€/MWh (≈1B€/500MW ??)
Large capacity technology:

## Slide 18: Dynamic operation simulation for CLIC
thoughts for CLIC: standby during high load
[Andrea Latina, CERN]
result of CLIC model with 2 standbys during day:
cost example France
high: Winter, 8-10am: 14c/kWh
low: Summer, 0-6am: 2c/kWh
factor 7

## Slide 19: EUCARD/ARIES Workshops
November 28-29, 2019 - 5th Workshop Energy for Sustainable Science at Research Infrastructures hosted by PSI, Switzerland https://indico.psi.ch/event/6754
September, 2-5, 2019 - Efficient Neutron Sources hosted by Paul Scherrer Institut, Switzerland https://indico.psi.ch/event/7274
June 18-20, 2019 - ARIES Workshop on Energy Efficient RF hosted by Ångström Laboratory, Stockholm, Sweden https://indico.uu.se/event/515/
November 8-9, 2018 - TTC/ARIES topical workshop on flux trapping and magnetic shielding hosted by CERN https://indico.cern.ch/event/741615/
November 23-24, 2017 - 4th Workshop Energy for Sustainable Science at Research Infrastructures hosted by ELI-NP, Romania http://www.eli-np.ro/4ess/
February 29 - March 2, 2016 - Workshop on Efficiency of Proton Driver Accelerators hosted by PSI, Villigen, Switzerland http://indico.psi.ch/event/Proton.Driver.Efficiency.Workshop
October 29-30, 2015 - III. Workshop on Energy for Sustainable Science at large Research Infrastructures hosted by DESY, Hamburg, http://erf.desy.de/energyworkshop ,
session storage systems: https://indico.desy.de/conferenceOtherViews.py?view=standard&confId=11870
April 21-24, 2015 - EuCARD2 2nd Annual Meeting Dedicated EnEfficient session: https://indico.cern.ch/event/364085/session/25/?slotId=0#20150423
November 26-28, 2014 - Workshop on Compact and Low Consumption Magnet Design for Future Linear and Circular Colliders hosted on CERN, https://indico.cern.ch/event/321880/
June 3-4, 2014 - Workshop on EnEfficient RF Sources, hosted at Cockroft Institute in Daresbury https://indico.cern.ch/conferenceDisplay.py?confId=297025
April 28-29, 2014 - Workshop on heat recovery, held at MAX IV in Lund, Sweden https://indico.esss.lu.se/indico/conferenceDisplay.py?confId=148
February 3, 2014 - Workshop Session Energy Efficiency Aspects of the CLIC Project under the frame of activities for EnEfficient/Eucard-2 https://indico.cern.ch/sessionDisplay.py?sessionId=9&confId=275412#20140204
October 23-25, 2013 - 2nd Workshop on Energy for Sustainable Science hosted at CERN, Geneva, Switzerland https://indico.cern.ch/event/245432/

## Slide 20: EnEfficient: Dedicated Studies
Cooling Related Inventory, Del. Report, J.Torberntsson et al (ESS)
  https://edms.cern.ch/file/1325126/4/EuCARD2-Del-D3-1-Final.pdf
Pulsed Quadrupoles, Del. Report, C.Tenholt (GSI)
  https://edms.cern.ch/file/1325127/4/EuCARD2-Del-D3-2-Final.pdf
Review of Energy Storage Systems, Del. Report, J.Eckoldt (DESY), R.Gehring (KIT), M.Seidel (PSI)
  https://edms.cern.ch/file/1325129/2/EuCARD2-Del-D3-4-final.docx
Comparison of Beam Transport Options, Del. Report, Ph.Gardlowski (GSI)
  https://edms.cern.ch/file/1325128/3/EuCARD2-Del-D3-3-Final.pdf
Energy Management Report, S.Leis, D.Batorowicz (Uni Darmstadt)
  https://edms.cern.ch/file/1325135/2/EuCARD2-Mil-MS19-Final.pdf
  [extended thesis version]
Virtual Power Plant at Science Facilities, Del. Report, J.Stadlmann (GSI)
  https://edms.cern.ch/file/1325130/2/EuCARD2-Del-D3-5-Final.docx
Review of Proton Driver Accelerators, Report, M.Seidel (Editor)
  https://www.psi.ch/enefficient/PastEventsList/pdriver-efficiency-summary_compilation_V6.pdf
Analysis of PSI High Intensity Accelerator, A.Kovach (PSI)
  https://www.psi.ch/enefficient/DocumentationEN/Analysis_and_Optimisation_of_HIPA_Power_Consumption-20161214.pdf

## Slide 21: Summary
Energy Efficiency & Sustainability are important for accelerator projects and for the perception of our field in the public; Eucard-2 and ARIES provide networking, R&D on this topic
R&D efforts must be strengthened, even matured technologies have surprising potential
e.g. RF generation, low loss s.c. cavities, low power & permanent magnets, energy storage, target efficiency
comprehensive energy management, taking into account the grid load, may become important aspect for very large facilities (utilizing energy storage, dynamic operation)
Documentation past workshops: www.psi.ch/enefficient
Ongoing program: www.psi.ch/aries-eem