## Slide 1: Technologies for the DFH, supply strategy and schedule
Vittorio Parma
Technology Department
MSC-CMI Section
UU-CERN-RFR meeting for the DFH collaboration project for HL-LHC,
CERN 20 June 2018

## Slide 2: Technologies
Cryogenic pressure equipment device:
  Inner helium pressure vessel integrated in an outer vacuum insulating vessel
  Thermal insulation by vacuum, radiation shielding (MLI) and low thermal conduction supports (typically in G10/11 composite materials)
  Interfaces to other systems (cryogenic, vacuum, electrical): ISO K flanges and elastomeric seals, Conflat™ flanges and metal seals, all-welded welds
  Thermal contraction compensation elements (bellows, flexible hoses)

## Slide 3: Technologies
Materials:
  Sheet-metal work, stainless steel grades, compatible with cryogenic temperatures
  Machined parts (e.g.flanges), stainless steel grades, compatible with cryogenic temperatures
  Composite materials (G10/11, other low conducivity materials)
  Copper materials
  Multilayer insulation materials (MLI)
Assembly technologies:
  Mechanical close fittings, bolted assemblies
  All-welded stainless steel assemblies (TIG orbital/manual) compatible with PED requirements
  Weld orbital cutting machines
  Sealed assemblies (organic and metallic seals) for vacuum applications
  Leak-tightness of assemblies to better than 10-6 mbar.l/s (helium mass spectrometry)
  Wire routing and mounting of feed-through flanges (to be confirmed)

## Slide 4: Technologies
Assembly and Quality testing area:
  Facility with all necessary services and infrastructure (e.g. Handling devices)
  LN2 shock and pressure tests area
  Helium spectrometry leak-detection area (vented to reduce He back-ground)
Quality Control & Testing:
  Metrology and dimensional checks and measurements
  X-rays of welds
  LN2 shocks of welded assemblies
  Pressure testing
  Leak-tight testing (helium spectrometry)
  Electrical tests of instrumentation wiring (continuity, insulation) (to be confirmed)

## Slide 5: General strategy for DFH
Engineering design done by CERN
CERN remains liable for functional performance (e.g thermal performance)
CERN provides UU with CERN’s technical specification and specification drawings
UU is in charge of the procurement of the DFH based on CERN’s specs
Understanding that RFR will be contracted by UU for the construction of the DFH, based on UU’s specifications and (presumably) CERN’s drawings,
RFR will be in charge of the construction, qualification testing and supply to CERN of the equipment and all the relevant documentation
CERN reserves the right of introducing hold points at intermediate and final steps of the construction of the pre-series and series units. This will be part of the technical specification to UU
The construction follow-up will be led by UU. CERN remains available for support

## Slide 6: Schedule
Pre-series
Series