## Slide 1: FREIA Laboratory Facility for Research Instrumentation and Accelerator Development
Overview of Activities
Roger Ruber for the FREIA Team
ESS, 14 September 2018

## Slide 2: Uppsala Accelerator History
1477: Uppsala University, oldest in Scandinavia
25'000 students, 7'000 staff
historical profiles: Linné, Rudbeck, Celsius, Ångström, Svedberg
1940's: The(odore) Svedberg builds a cyclotron
Gustaf Werner synchro-cyclotron (1947 - 2016)
  nuclear physics & oncology
CELSIUS ring (1984 - 2005)
  nuclear & particle physics
2000's: External projects
CTF3/CLIC (since 2005)
FLASH/XFEL (since 2006)
ESS (since 2009)
2010's: New ventures
FREIA laboratory (est. 2011)
Skandion clinic (est. 2015)

## Slide 3: FREIA
cryogenics
- liquid helium
- liquid nitrogen
control room
- equipment controls
- data acquisition
radio-frequency (RF) power sources
3 bunkers
with test stands
horizontal cryostat
vertical cryostat
State-of-the-art Equipment
Facility for Research Instrumentation and Accelerator Development
Funded by KAWS, Government, Uppsala Univ.
Competent and motivated staff
collaboration of physics (IFA) and engineering (Teknikum).

## Slide 4: Accelerators & Instrumentation
High Intensity Proton Beams
Ultra Bright Electron Beams
SC Cavities & Magnets
RF Generation & Control
Advanced Instrumentation
Cryogenics

## Slide 5: Cryogenics
Helium liquefaction
  150 l/h at 4.5K (LN2 pre-cooling)
  2000 l LHe dewar/buffer, 3+1 outlets
  cryostats connected in closed loop
Gas recovery
  100 m3 gasbag
  3x 25 m3/h compressor
  10 m3 200 bar storage
2K Pumping
  ~3.2 g/s at 10 mbar
  ~4.3 g/s at 15 mbar
  110(90)W at 2.0(1.8)K
Liquid nitrogen
  20 m3 LN2 tank
Sub-atmospheric pumping station
Helium gas recovery system

## Slide 6: “HNOSS” Horizontal Cryostat
HNOSS = Horizontal Nugget for Operation of Superconducting Systems
Test of superconducting cavities/devices
  3240 x ø1200mm inner volume
  up to two cavities simultaneously,
  each equipped with helium tank,
Low or High power RF testing
  fundamental power coupler (top, bottom, side)
  (cold) tuning system
Operation in the range 1.8 to 4.5K.
Available as ARIES
Trans National Access Facility

## Slide 7: “Gersemi” Vertical Cryostat
Under commissioning
Test of SC cavities & magnets
  3.2m x ø1.1m total volume
  2.65m x ø1.1m below lambda plate
    design includes joint for lambda plate
Operation in the range 1.8 to 4.5K
Three operation modes
  vacuum
  liquid bath
  pressurized bath with 2K heat exchanger
Available as ARIES
Trans National Access Facility

## Slide 8: Test Activities
Hélène single spoke cavity (IPNO)
  antenna, low power
  self-excited loop (SEL)
  RF calibration procedures
Germaine double spoke (IPNO)
  antenna and cold tuner, low power
  cryogenics: cooling, heat load
  LLRF, SEL
  Q0, gradient, microphonics
Romea cavity package (IPNO)
  power coupler and tuner, nominal gradient
  Q0 and gradient, microphonics, fill time, Lorentz force detuning
  tuner operation
RF Station 352 MHz (2x)
  acceptance and functional test
    including RF distribution components
  soak test
  pulsed and CW operation on cavity
RF Station 704 MHz
  acceptance & operation of modulator
High-β elliptical cavity package (CEA)
  FPC conditioning ok
  under test
ESS Cryomodules
  prototype, arrived August 2018
  13 series during 2019 - 2020

## Slide 9: High Power RF Amplifiers
352 MHz Tetrodes
2x 400 kW, 3.5 ms, 14-28 Hz
  combined output 2 tetrodes TH595
50 kW CW
  on loan from CERN
  tetrode TH571b
  352 or 400 MHz output cavity
704 MHz Klystron
1.1 MW, 3 ms, 14 Hz
  on loan from ESS
  Ampegon/PPT modulator
  Toshiba klystron
CERN 50 kW CW

## Slide 10: Solid State RF Development
SSA development
  single ended RF power amplifier
  based on BLF188XR
  1250 W and 70% efficiency
SSA demonstrator
  10 kW, 8 modules
Compact Combiners
  compact cavity combiner 100 kW
  planar Gysel combiner 10 kW

## Slide 11: Controls and Measurement
Slow Controls & Safety Interlock
  connecting different sub-systems: cryogenics, cryostats, powering, ...
  Siemens PLC, Nat.Instr. cRIO
  EPICS interface with data archiver
LLRF
  Self excited loop 352/704 MHz
    pulsed or CW operation
  Nat. Instr. PXI and LabVIEW
    digital phase control for SEL
    extended RF measurements
  Lund Univ/ESS µTCA system
    timing, external signal generators
Fast Magnet Quench Monitoring
  Nat.Instr. PXI and LabVIEW
    based on CERN developments
Software
  EPICS and archiver
  LabVIEW code
    klystron auto conditioning
    power coupler auto conditioning
      pulse length, power level, repetition rates
    SEL control and data acquisition
    cavity frequency shift tracing
    dynamic Lorentz force detuning

## Slide 12: Research Projects
*) FEL = Free Electron Laser
ESS Superconducting Linac
HiLumi LHC
CLIC
ESS Neutrino Super Beam
FELs
Ultrafast Electron Diffraction
High Brilliance Electron Beams
High Brilliance Proton Beams

## Slide 13: Summary
Uppsala University & FREIA Laboratory actively developing accelerator and instrumentation technology
Development, verification, and testing
cavity (package)
high power RF
RF solid-state and power combiners
LLRF
Controls
Research
high brilliance beams
superconducting RF
vacuum/RF breakdown
Academic Teaching