## Slide 1: Testing of Series Superconducting Dipole Magnets for the SIS100 Synchrotron
P. Aguar Bartolome et al.
GSI Helmholtzzentrun für Schwerionenforschung GmbH, Darmstadt, Germany
3rd International Workshop of the Superconducting Magnets Test Stands, 11th-12th June

## Slide 2: Outline
Introduction
  - FAIR @ GSI
  - Heavy Ion Synchrotron SIS100
SIS100 Dipole Magnets
  - Design
  - Testing Strategy
GSI Test Facilities for SIS100 Magnets
  - Infrastructure
  - Measurement Systems
Test Status for SIS100 Series Dipoles
Summary and Outlook

## Slide 3: Facility for Antiproton and Ion Research
Existing GSI facility
FAIR facility
International project
SIS100
High intensity ion and antiproton beams for experiments in nuclear, atomic, plasma physics and material science.
Existing facility UNILAC/SIS18 will provide ion-beam source and injector for FAIR.
SIS18
UNILAC
p-LINAC

## Slide 4: Heavy Ion Synchrotron SIS100
SIS100 = Schwerionensynchrotron 100 [Tm] = Heavy ion synchrotron (beam rigidity 100 [Tm]*)
Accelerator tunnel SIS100
Service tunnel
Hexagonal, circumference 1083.60 m
Operational modes:
  Ultra High Vacuum (10-11 mbar)
    - Adsorption by cold vacuum chamber (10 - 15K)
    - Superconducting (magnet) accelerator
  Fast-ramp machine ~0.5 sec. to maximum field
*Beam rigidity 100 [Tm] = Bending dipole field 1.9 [T] × Bending radius 52.632 [m]

## Slide 5: SIS100 Dipole Magnets: Design
Cryo-dipole module
350 mm
140.1 mm
266 mm
68
Magnet cross section
Main parameters |  | 
Number of the magnets in SIS100 | 110 | 
Effective length Leff | 3.062 | m
Usable aperture | 60 x 120 | mm x mm
Bending angle | 3 1/3 | deg.
Bending radius | 52.632 | m
Nominal Field | 1.9 | T
Field homogeneity ∆B/Bmain x104 | < ± 6 | units
Ramp rate | 4 @1Hz | T/s
Nuclotron cable
1 - Cooling tube CuNi
2 - SC wire NbTi
3 - CrNi wire
4 - Kapton tape
Super ferric magnets
Curved magnet
SC coil (4 turn per pole)
Nuclotron type cable
Cooling with 2-phase He @ 4.5K
≈ 3000 mm
Cold mass with beam chamber

## Slide 6
At GSI site:
SIS100 Dipole Magnets: Testing Strategy
Quality inspections on different production steps
(e.g. yoke geometry for half yokes before and after welding, after assembly with the coil)
Functionality tests @ 300K
  components of assembly
  assembled magnet
Factory Acceptance Test (FAT)
  measurement protocols
  quality certificate (summary of single tests)
At contractor site:
Standard Test Program for 100% of magnets:
  documents control
  quality controls
  functionality tests @ 300K (after delivery, after cold tests)
  functionality tests @ 4.5K including magnetic field measurements (DC, AC mode)
Series dipoles are manufactured at Bilfinger Noell GmbH, Germany

## Slide 7: Site Acceptance Test (SAT): Scope
  Yoke geometry
  Process lines
  Instrumentation check
  Electrical integrity
  Quench performance
  Static heat load and AC losses
aperture height (precise)
sag and twist
positioning
pressure and leak
massflow rate
positioning
HV
continuity
turn-to-turn insulation
Quality assurance (including safety)
About 30 parameters to control
About 110 steps to follow
Duration ~ 3 weeks
Machine control
  Integral B-field
  Harmonics
  Load line
For each dipole magnet:

## Slide 8: Site Acceptance Test (SAT): Sequence
Reception
  visual inspection
  document check
SAT @300 K (Incoming)
  instrumentation
  electrical insulation
  geometry
  pressure and leaks, massflow rate
Mounting on the test bench
  Installation of the MF-probe
  electrical integrity magnet+current leads
  pumping 24 h
  cool down 76 - 90h
SAT @ 4.5K
  electrical integrity and insulation
  magnet training
  inductance
  magnetic field
  static and AC losses
Warming up and dismounting
SAT @ 300K (Outgoing) 1- 2 days
~ 5 days
2 - 3 days
3 - 4 days
4 - 5 days

## Slide 9: GSI Test Facilities for SIS100 Magnets
Series Test Facility (STF)
Cryo-plant 1.5 kW – commissioned Q2/2015
Power converters 2 x 20 kA (66 V) –commissioned Q1 & Q3/2016
14 kA DC HTS Current Leads (CL) – commissioning Q3/2015 – Q1/2017
QD / Magnet protection system
687m2 total area
4 test benches for cold tests
6 preparation benches
Calibration chain for MF-probe
1
2
3
4
5
5
Test benches for superconducting magnets: 1 - end box, 2 - feed box, 3 - distribution box, 4 - power switch, 5 - preparation bench
Full readiness for operation August 2017

## Slide 10: GSI Test Facilities for SIS100 Magnets
Prototype Test Facility
Cryo-plant 0,6 kW – commissioned 2007
Power converters 20 kA (66 V) – commissioned Q3/2013
14 kA DC HTS Current Leads (CL) – commissioning Q3/2013, Q4/2014
QD / Magnet protection system
150 m2 total area
1 test benches for cold tests SIS100 dipole
1 universal cryostat
1 - power converter, 2 - feed box for testing of SIS100 magnets, 3 - First of series dipole for SIS100, 4 - power switch, 5 - Universal cryostat for cryogenic tests of small components.
1
1
2
3
4
5

## Slide 11: Main Measurement Systems
6 capacitive sensors CSH1,2FL(20)-CRm 4,0 from Micro - Epsilon GmbH& Co.KG
Linear encoder WDS-100-P 115-CR
from Micro-Epsilon GmbH& Co for reproducible
positioning of the carriage along the magnet
absolute precision 15µm
relative precision < ± 3µm
System for high precision gap height measurement
In combination with a laser tracker, the
system provides data regarding the yoke’s sag and twist.
@ 300K
2
1
2
3
4
1 - carriage, 2 - capacitive sensors, 3 - wheels,
4 - holder for spherically mounted retroreflectors.

## Slide 12: Main Measurement Systems
System for magnetic field measurements
rotated ferro fluidic feed througth
The measuring probe is designed and built in collaboration with CERN
motor unit
5 measuring heads – tangential coils
3 pick up coils per head, 600 mm length
Effective surface 1.67 m2
Ti-alloy bellows – interconnection between segments and to align the heads along the beam axis
SiN ball bearings for rotation motion
Ceramic supporting blocks for transverse positioning in the gap
3600 mm
Cross section of the measuring head (3 tangentinal coils)
SiN ball bearing
620 mm
measuring head
supporting block
Ti bellow
Field measurements in vacuum @ 4.5K

## Slide 13
Test Status for SIS100 Series Dipoles
The measurement results reveal an excellent performance of the chosen design and high production quality.
The magnetic field shows very low variation in terms of the field integral and the low harmonic content is satisfactory for the beam physics requirements.
Quench performance verifies a high stability of the coil structure in the yoke.
46 | 42
Dipole magnets delivered
Dipole magnets tested

## Slide 14: Summary and Outlook
The series production of the SIS 100 dipole magnets started in August 2016
The first series dipole was delivered to GSI at the end of September 2017
Quality control and functionality tests at contractor and GSI site are defined
High precision measurement systems were developed for magnet evaluation
Excellent performance of the chosen design and high production quality.
Almost 50% of the series dipoles successfully tested.
Dipole series production is ongoing with a delivery rate of approx. one magnet per week.

## Slide 15: SAT Team
Test coordinators
Survey & alignment
Electrical integrity
Field measurement
Quench detection
Cryoplant operators
Transport and installation
Quality assurance
DAQ, control and software
GSI departments
SCM, QA, TRI, CRY, EN-MG, EPS, VAC, BB, RHV
Support on demand – MEWE, KB, ENG

## Slide 16
Thank you for your attention

## Slide 17
Backup 1

## Slide 18
 | unit | Main Dipole | Main Quadrupole | Chromaticity sextupole (h/v) | Steerer (nested h/v) |  | Multipole corrector (nested) |  | 
 |  |  |  |  |  |  | Quadrupole | Sext.(skew) | Octupole
Design |  | Super-Ferric | Super-Ferric | Super-Ferric | Cosθ |  | Cosθ | Cosθ | Cosθ
Number of Magnets |  | 108 | 166 | 42 | 83 |  | 12 | 12 | 12
Magnetic field strength | T/mn-1 | 1.9 | 27.77 | 232 | 0.372 | 0.366 | 0.91 | 31.8 | 446
Effective length | m | 3.062 | 1.264 | 0.383 | 0.403 | 0.410 | 0.62 | 0.59 | 0.56
Usable aperture | mm | 133x65 | 133x65 | 135x65 | 135x65 |  | 133x65 |  | 
Ramp time to Max. | sec. | 0.5 | 0.5 | 0.175 | 0.2 |  | 0.175 |  | 

## Slide 19: SIS100 Superconducting Magnet System
Main Quadrupole Magnets
Main Dipole Magnets
yoke cross section
with coil
cold mass
with beam chamber
Super-Ferric 1.9T @ 13.2 kA
Window frame, curved magnet R 52.632 m
Nuclotron cable
fast ramped
cooling with 2 phase He
108 Magnets
Super-Ferric 10 kA , 27.7 T/m
Nuclotron cable
cooling with 2 phase He
166 Magnets
1 - Cooling tube CuNi
2 - SC wire NbTi
3 - CrNi wire
4 - Kapton tape
5 - Glasfiber tape
Nuclotron cable:

## Slide 20: SIS100 Superconducting Magnet System – Corrector Magnets
Insulated Sc. strands connected in series
Chromaticity sextupole:
Super-Ferric 232 T/m2
Nuclotron cable
Nested (horisontal and vertical correction)
42 Magnets
Steering magnet:
Cos-Θ
Nuclotron cable
with insulated strands
Nested (horizontal and vertical correction)
83 Magnets
Multipole corrector magnet:
Cos-Θ
Nuclotron cable
with insulated strands
Nested (B2, A3, B4) correction
12 Magnets
250A × 27 Strands = 6.75kA

## Slide 21: Main Measurement Systems
Calibration of the magnetic field measuring probe
calibration @ 300K in NC dipole
surface calibration –> precise measurement B1,
angular displacement of the head relative to the reference one i.e., the middle segment –> direction B1, higher order harmonics
lengths of the interconnection areas between the segments –> precise measurement
02/02/2018
13/03/2018
30/05/2018
16/08/2018
segm.1
segm.2
segm.3
segm.4
segm.5
1.002
1.003
1.004
1.005
1.006
1.007
gain
segm.1
02/02/2018
13/03/2018
30/05/2018
16/08/2018
segm. 2
segm.3
segm.4
segm.5
-0.02
0.04
0.03
0.01
0
-0.01
Angle [rad]
0.02
0.05
dose the warm calibration work for the cold measurements?
yes, it works and is precise enough for qualifying of the SIS100 dipoles.
Required precision < 4×10-3
mechanic of the MF-probe is not affected by thermal cycles. The calibration stays stable

## Slide 22: Test Results for SIS100 Series Dipoles
acceptance criteria from SIS100:
with
measured on 15 magnets:
ΔBL/BL = 4.1 ×10-4
measured on 15 magnets:
ΔBL/BL = 4.1 ×10-4
Integral Field
[units]
-3
-2
-1
0
1
3
2
-3
-2
-1
0
1
3
2
5
4
5
4
7
6
-4
6
8
3
2
5
4
7
6
Harmonic Nr.
3
2
5
4
7
6
Harmonic Nr.
Simulation
average bn
average an
single magnets
Simulation
average bn
average an
single magnets
I = 13200 A
I = 1500 A
Field homogeneity
with
< ± 6 units @ = 30mm
acceptance criteria:
measured on 15 magnets:
magnet data acceptable for synchrotron operation
good agreement with expectation exept:
- b3 systematic → correctable
- a2 under investigation
high repruducibility ( except …)

## Slide 23
nominal current (nc) to be reached:
  at 3rd quench in first cycle
  at 1st quench in further
de-training limited to 5 % of nc (compared to previous quench)
quench current has to stabilize at 110 % of nc at least (14.5 kA)
nc reached at 2nd quench at least
no significant de-training observed
results for 22 magnets
stable operation for all tested magnets
Magnet training
specified:
Test Results for SIS100 Series Dipoles
Outstanding quench performance!
Training close to the short sample limit of the cable (17.8 kA) -> high stability of the coil structure in the yoke.
short sample limit of the cable 17.8 kA

## Slide 24: Test Results for SIS100 Series Dipoles
required:
well within specification on average for each magnet
very good reproducibility
  negligible
example
tilt
(→ an, bn)
aperture height
(→BL)
spot welding of lamination to outer frame
Z
• Aperture heigth
• Tilt
hspec = 68.13 mm
Aperture heigth h – hspec (µm)
02
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
26
27
36
37
-50
50
150
0
100
Magnet Nr.
Gap geometry