## Slide 1: News from the LASA test facility
Marco Statera
on behalf of the LASA team
INFN Milano - LASA
Uppsala, June 11th 2019

## Slide 2: Outline
LASA cryogenic system
SC cavities test facility
SC magnets test area
  High current and variable temperature
  HL-LHC HO corrector magnets
  FCC activity
conclusion

## Slide 3: LASA overview
aaa
power supplies
10 kA line
vertical cryostats
30 kA line
fast DAQ and slow control
SC cavities
Test area
Neutron test area
high field solenoids

## Slide 4: Cryoplant layout
a
operation 1-2 k h/year
DISCORAP cryostat
3000l
450 l dewar
constraints
100 Nm3/h compressors
100 m3 recovery balloon
DISCORAP

## Slide 5: Cryoplant Upgrades
a
warm helium
Automation ongoing
2019
SC cavities
HeII refiller
study ongoing
SC magnets
HL-LHC correctors
HTS @ variable T
He liquefier
Update or
New machine

## Slide 6: SC Cavities Testing Facility
Bunker with vertical cryostat, f 700 mm, 4500 mm depth, can hold large SC cavities as 500 MHz
Sub-cooling system for superfluid helium, up to 1.5 K. Cooling power 41 W a 2.0 K
2 Cold inserts for cavity testing
RF generators: 700 MHz, 1.3 and 3.9 GHz
Associated infrastructures
ISO4 clean room (9 m2)
High Pressure Rinsing facility
Slow pumping Slow venting system
UP water production plant (100 l/h)
  European Spallation Source – ESS
  Proton Improvement Plan II – PIP-II FNAL
Courtesy of R. Paparella

## Slide 7: SC Magnet Test Area
Small Magnets test cryostat
  HO correctors protoypes
    6P MCSXFP (MCSXF/MCSSXF)
    8P MCOXFP (MCOXF/MCOSXF)
    10P MCDXFP (MCDXF/MCDSXF)
High Current Test Station
  DISCORAP and HTS magnets
  HO correctors
    12P MCTXFP
    4P MQSXFP
  HiLumi HO correctors series
MAGIX
D 480 mm
h 1200 mm
4.2 K and 2.17 K
500 A
DISCORAP
D 695 mm
h 7200 mm
4.2 K
10 kA
HiLumi
D 515 mm
H 2950 mm
4.2 K
500 A

## Slide 8: HL-LHC HO Correctors
Cryostat for testing MCTXFP1 (12P), MCQSXFP1 (4P) and series magnets
4 K operation
515 mm inner diameter
Hosted within DISCORAP cryostat (which acts as a support)
About 3 m high
Up to 4 magnets (3 possible configurations)
New power supply and IGBT switch
Ordered end 2017
Delivery April 2018
Test MCTXFP1 (12P) 2018/09
Test MCQSXFP1-01 (4P) 2019/02
Test MCQSXFP1-02 (4P) 2019/06 ongoing
Mag.meas.
Safety
Valve and disk
CL
2+4
He inlet
Mechanical interface with dicorap cryostat

## Slide 9: Measurements
Data Acquisition Architecture
QDS (MSS Magnet Safety System)
Initiates a fast discharge or switches off the power supply incase some voltage thresholds on the magnet or on its electrical connection are exceeded. Includes a capacitor bank for firing quench heaters.
Fast Acquisition
Records voltages across the magnet under test with 1 kHz sampling frequence, in coincidence with a fast discharge
Current Control & Slow Control
Two different functions, implemented in the same hardware & software system.
Slow acquisition monitors and records most important data (temperatures, current, voltage along critical items) from the cooldown to the operation. Data are avalilable to the operator and recorded at about 1 Hz
HO correctors’ measurements at 4 K
Stability 1h @ ultimate
One magnet at a time
Field quality at 4K (1 magnet per cooldown)

## Slide 10: Quench Protection
Each HO corrector
1 common CL + bus bar
1 dedicated CL + bus bar
3 voltage taps
Cross check magnet connection before powering by AC signal

## Slide 11: Test configurations
Prototypes
Single magnet test
Series production
3 batches
  18 magnets
  2X12P 2X4P
  5 cooldowns
Automatization of the cooldown and warmup by a Nitrogen heat exchanger 2019
600
12P
4P
2350
LHe max

## Slide 12: Magnetic Measurement
Shaft from CERN (at LASA)
Measurement at LASA
Dedicated shaft for series HO correctors
feedthrough
CERN design
machined at LASA
designed and machined at LASA
by N. Lusa
designed and machined at LASA
MCQSXFP1 magnetic measurement in collaboration with CERN (L. Fiscarelli) 2019

## Slide 13: LASA High Current Test Station
DISCORAP cryostat for HTS magnets test
Mechanical interface redesign ongoing
Zero uplift filler delivered
Fast switch commissioned
Electrical connections integration ongoing
Temperature control design ongoing
Cryocooler procurement ongoing
Magnetic field measurement integration designed
f 0.695 m
7.2 m
3.4 m
1.4 m3 ethylene-vinil acetate disks
10 kA leads
HTS magnet
ballast
HTS magnet
10 kA test station
Three 6V 10 kA power supplies
10 kA current leads
7.2 m cryostat

## Slide 14: 10 kA Protection
1.2 ms to open
220 ms opening time
water cooling 17 kW
Power supply 10kA – 30 kA
Power line 10 kA
Disconnector/fast switch 10 kA 1.2 ms
Line clamp
Dump resistor
M. Quadrio and A. Paccalini
10 kA lead
Discorap test

## Slide 15: Working Principle
Low helium consuption
Good temperature control
Low temperature gradient (Ghe)
Note
The cryostat is not in vacuum
The vessels have to allow the gas to flow in/out for cleaning
Shell design by R. Pengo
We introduce the cryocooler
GAS He
30-100 K
AIR
HEATER
Vacuum insulation
+ LN2
Vacuum
10-50 K
Liquid He
(optional)

## Slide 16: Thermal Balance Scheme
Current leads
  Gas He from a 450 l Dewar
  Updated CL design (no UHV welding on Cu)
  1-2 W @ I=0 and 7 W @ 10 kA
Mechanical support
Integration ongoing
G He
CURRENT LEADS
CRYOCOOLER
FIRST STAGE 20W @ 30K and 120 W @100 K
SECOND STAGE 9W @ 10 K

## Slide 17: Magnet Temperature
Simplified model
Additional L-He consuption 1-10 l/h
Temperature homogeneity 1K
300 K
4 K
3.4 m
40 K
20 K
LHe
77 K
Magnet screen

## Slide 18: FalconD
Cable Parameter | Value
Cu/SC | 1
Strand number | 2x19
Strand diameter (mm) | 1
Height (mm) | 20
Inner width (mm) | 1.72
Outer width (mm) | 1.895
Keystone angle | 0.5°
Twist pitch (mm) | 100
INFN activity, co-founded by CERN, to develop a Nb3Sn cos-theta dipole demostrator for 14 T (2 m long)
Magnet Parameter | Value
Bore field (T) | 14
Operation on Load Line | 86% (block 3)
Current (A) | 22975
Jcu (A/mm2) | 1540

## Slide 19: INFN-LASA furnace for Nb3Sn winding heat treatment
The activity will require an investment to puchase a furnace for Nb3Sn reaction
Financial support already obtained, the activity to launch the tender in starting
Geometry and load: | 3 m with option for extension
Commissioning | 2020/2021
Installation area | 9 x 3.5 m
Length (uniform Temp/total) | 3 m
Performance | 
Max. operation temperature | 900°C
Temperature uniformity | ±3°C
Circulation fan / turbulent flow | 1 Fan/vertical axis
Process atmosphere | Argon
Vacuum level | 10-2 hPa
Oxygen monitoring | down to 1 ppm

## Slide 20: Status of Installation
AAA
Discorap cryostat
HiLumi cryostat
10 kA line
Nitrogen
heat exchanger
pumping station
4pole test

## Slide 21: Conclusion
Updates on the activity of the LASA magnet test station
Updating cryoplant
Commissioning of the system for HiLumi HO correctors
  Test the ‘long’ HO prototypes
  Test the HO corrector series magnets
HTS magnets at variable temperature
Furnace for Nb3Sn reaction for a 14T demonstrator: FalconD

## Slide 22
THANK YOU
LASA team
F. Alessandria, G. Bellomo, F. Broggi, N. Lusa, S. Mariotto, A. Paccalini, D. Pedrini, A. Leone, M. Quadrio, A. Pasini, M. Prioli, M. Sorbi, M. Statera, M. Todero, C. Uva
Ph. by G. Fornasier