## Slide 2: Energy Extraction Systems and CLIQ at CERN Test Areas
Bozhidar Panev – 11 June 2019

## Slide 3: Outline
EE systems at CERN
Switching technologies involved in the EE systems at CERN
Semiconductor based EE systems in CERN test benches
  High current systems (2÷30)kA
  Low current systems (up to 2kA)
Vacuum based EE systems (HL-LHC)
CLIQ unit

## Slide 4: EE systems at CERN
LHC
  13kA EE systems (RB/RQ circuits)
  600A EE systems (corrector circuits)
Superconducting test benches
  EE facilities – (0.6÷30)kA
13kA EE system
600A EE
systems
2kA vacuum switches
EE system
2kA IGBT
EE system
7.5kA IGBT
EE module
20kA
thyristor switch
EE system

## Slide 5: Switching technologies involved in EE systems at CERN
Electromechanical high-speed circuit breakers – up to 20ms opening time
Semiconductors as a solid state switch - up to 1ms opening time
Vacuum interrupters – up to 5ms opening time
IGBT
IGCT
Electro-mechanical
circuit breakers
Vacuum
interrupter

## Slide 6: IGBT based EE systems for superconducting test areas at CERN
Solid state switch development project started several years ago
IGBT was selected as a switching device
7.5kA module was developed, produced and installed
Some details:
4 IGBTs share the current of 7.5kA
Special care paid in the busbar and heatsink design
Three snubber capacitor stages
NI-Compact RIO based control system

## Slide 7: Performance of 7.5kA IGBT based EE system
Main features:
Compact design
Ultra fast operation
  Current transferred in the resistor for less than 1ms
Possibility of paralleling the racks up to 30 kA
Maintenance free
I=7.5kA
L=3mH
R=60mOhms

## Slide 8: SM18 – EE systems at cluster-D
Two IGBT based EE systems (15kA each) installed and commissioned in 2016
  Each system consist of 2 modules 7.5kA each
Maximum current: Imax = 30kA
Resistors: modular design allowing different configurations: (6.67240)mΩ
  Rated energy: 6MJ
Successful operation is registered
Expected service life: 20 years
Resistors
IGBT switch modules

## Slide 9: SM18 – EE systems at cluster-G (HFM)
Two IGBT based modules compose the EE system (the same as for cluster-D)
  Each module rated to 7.5kA
Maximum current: Imax = 15kA
Resistors: modular design allowing different configurations (6.67240)mΩ
  Rated energy: 6MJ
Commissioning planned for summer 2019
Expected service life  20 years
Dump Resistor
IGBT EE system for 15kA (2 x 7.5kA)

## Slide 10: 2kA IGBT based EE systems for HL-LHC (1)
Design and development started in 2017
A modular approach is applied in the design
A single module commutates bidirectionally 1000 A
Two modules connected in parallel for 2kA operation
1kA module
housed in a 6U chassis
2 modules
In parallel

## Slide 11: 2kA IGBT based EE systems for HL-LHC (2)
Details from the design:
  Dump resistor 300mΩ (2 x 600mΩ in parallel)
  Bipolar operation of each 1kA module
  ~2.5V voltage drop (still significant)
  Redundancy achieved through 2kA triggerable fuse
    250us reaction
    Low ohmic losses (200uOhms)
180 cm
90 cm
60 cm
triggerable fuse
Back up protection
with triggerable fuse
1kA module
configuration
Dump resistors

## Slide 12: Control electronics of IGBT based EE system
Some details of the control electronics
  sbRIO controller
  Two FPA boards
  Hardware interlock board
  Power supply board
NI – sbRIO controller
(single-board)
28 digital I/O
16 analogue inputs
etc.
3U control chassis
housed the electronic boards
FPA and PSU boards

## Slide 13: 2kA IGBT based EE systems for HL-LHC (3)
Semiconductor based (IGBT) bipolar, compact and complete EE system to be used with the Hi-Lumi corrector magnets (MCBXFA & MCBXFB) at the vertical test bench in SM18
Two systems (final version) fully tested were send for installation in SM18
Two more systems ordered in the industry – expected in Sep19
System under test
In SM18
Performance at 2kA – U_DUMP
730 μs

## Slide 14: Vacuum switches based EE systems
New development for HL-LHC
  28 EE systems required
    8 for 2kA
    20 for 600A
Prototypes fully tested
2kA EE system
2 system for 600A
Long service life vacuum switch
Control electronics

## Slide 15: Performance of vacuum switches based EE systems
2kA system installed and commissioned in SM18 for protection of MCBXFB – 15.03.19
2kA vacuum switches EE system in real operation
Pre-series  ordered
  4 systems for 2kA
  4 systems for 600A
EE operation during a training quench of MCBXFB at 1.5kA (15.03.2019) SM18
Circuit current transferred to resistor for ≈1.8ms
Vacuum switches EE systems are selected to be used for HL-LHC magnet circuits protection
  MCBXFA: 8 systems (2 kA)
  MCQSXF: 4 systems (600 A)
  MCBRD: 16 systems (600 A)

## Slide 16: CLIQ
Coupling-Loss Induced Quench (CLIQ) is an innovative quench protection method based on a capacitor discharge resulting in high inter-filament and inter-strand coupling losses
Complement of the Quench Heater systems for the HL-LHC new Inner Triplet magnets protection
Two prototype versions designed at CERN
CLIQ v2 successfully manufactured and tested by the industry
CLIQ v3 prototype ongoing (1000 VDC, 40 mF capacitors)
CLIQ v2 units
Courtesy to David Carrillo

## Slide 17: CLIQ
CLIQ v1 used on a 14-m-Long Full-Scale LHC dipole magnet. E. Ravaioli et al.
Testing of new trigger card for CLIQ v3
CLIQ v2 units manufactured and tested by the industry
Courtesy to David Carrillo

## Slide 18: A glimpse into the CLIQ v2 unit
Courtesy to David Carrillo

## Slide 19: Thank you!