## Slide 1: Magnet safety system and supervision in FREIA
3rd International Workshop of the Superconducting Magnets Test Stand
Kévin Pepitone
Uppsala, June 11-12, 2019

## Slide 2: Outline
Magnet safety
  Equipment connected to the magnets
  Acquisition systems
  Magnet protection at FREIA
Supervision
  Control system architecture
  Subsystems
  Services and user interfaces
  Safety system – PLC
  Cryogenics supervision software
  Power converters EPICS interface

## Slide 3
Magnet safety
Magnet safety
Equipment connected to the magnets
Acquisition systems
Magnet protection at FREIA
Supervision
Control system architecture
Subsystems
Services and user interfaces
Safety system – PLC
Cryogenics supervision software
Power converters EPICS interface

## Slide 4: Equipment connected to the magnets

## Slide 5: Equipment connected to the magnets
Computers for interlocks and acquisition
Measurements: 4-wires multimeter
oscilloscope (200 MHz BW and 2GS/s)
Safety systems: Matrix and PotAim cards 1kVdc insulation
Patch panels
Acquisition systems:
PLC
DAQ (16 bits) | HF | MF | LF
Maximum number of channels to be recorded | 48 | 48 | 72
Maximum differential input voltage | 1 kVdc | 1 kVdc | 1 kVdc
Acquisition frequency | 5 - 200 kHz | 1 - 5 kHz | 1 kHz
Bandwidth of the system | 600 Hz |  | 
Thresholds / delays per signal | 0 – 1 V / 0 – 1 s |  | 

## Slide 6: Acquisition systems – Fast acquisition
Quench detected by the matrix
=> Triggers fired
Look at the differential voltages to find where is the quench
Find the segment(s) where the quench occurs

## Slide 7: Acquisition systems – Long acquisition
“Plateau” -> Splices measurements
Ramp rate -> Inductances measurements
Quench

## Slide 8: Magnet protection at FREIA
Vthreshold
tValidation
System delay
36 Vtaps that can be connected to the magnets
16 Vtaps on the splices and current leads
Sensors and interlocks:
  GHe flow (current leads to gaz bag)
  Temperature on magnet and insert (49 sensors below the λplate, 18 above)
  Level (2 sensors below the λplate, 1 above)
PotAim cards and matrix:

## Slide 9
Supervision
Magnet safety
Equipment connected to the magnets
Acquisition systems
Magnet protection at FREIA
Supervision
Control system architecture
Subsystems
Services and user interfaces
Safety system – PLC
Cryogenics supervision software
Power converters EPICS interface
Courtesy Konrad Gajewski

## Slide 10: Control system architecture
Why EPICS?
Has all features that we need at FREIA
Mature, well maintained system
Will be used at ESS
EPICS drivers and device support for many commercial instrumentation
Easy integration with PLCs
Very wide users base and helpful community
EPICS (Experimental Physics and
Industrial Control System) based
3 Layer architecture
Top layer: Application programs (GUI, data browser, alarm manager,…)
Middle layer – Input/Output controllers (IOC)
Front end (PLC, ADCs, intelligent peripherals, etc…)
Common services:
Archiver (archive appliance)
Alarm manager (BEAST)
IOC
IOC
ChannelAccess
Internet
Archiever
Alarm Manager

## Slide 11: Subsystems @ FREIA connected to EPICS
Services:
Cryogenics (controls based on PLC)
Vacuum (pumps, valves, gauges)
Water cooling (valves, sensors)
Facilities:
RF power stations (anode PS, solid state amplifier...)
Horizontal cryostat
Vertical cryostat (PLC)
Machine protection system:
Fast interlocks (cRIO via LabView’s Epics IO-Server)
Slow interlocks (Siemens PLC)
Instrumentation:
Laboratory instrumentation (via LabView’s Epics IO-Server)
Timing system
Personnel protection system:
RF leak detector
Radiation monitoring
LLRF

## Slide 12: Control system services and user interfaces
Services:
Archiver (archive appliance)
Alarm manager (component of the Control System Studio)
Channel acces gateway
Electronic logbooks
User interfaces:
Control System Studio
  OPI builder (BOY)
  Data browser
  Alarm manager
Web browser
  Archive viewer
  FREIA status pages
  Logbooks

## Slide 13: Safety system - PLC
PLC
Current of power converters
Leads voltage
Minimum current for quench detection
Magnet temperature phase
Power converters
Energy extraction
Flash boxes
No quench detected (from safety matrix)
DAQ system OK
Power converter status
Energy extraction status
Current value (to cryo)
Quench signal (to cryo)
Slow/Fast power abort on power converters
Cables in parking or operation position
Thermo switches on leads
Cryo ok

## Slide 14: Cryogenics supervision software

## Slide 15: Power converters EPICS interface

## Slide 16: Conclusions
Expensive
Power converter
Cryogenics
Not to be broken, damaged, during transportation, installation and operation
PLC, safety system and many measurements on the magnet to be sure it is powered only when it is superconducting
Supervision and sensors to control pressure, temperature
MCBXF prototype

## Slide 17
Thank you for your attention

## Slide 18: Safety system - PLC
Par. (Quench to cryo; Magnet Phase)
6 ANALOG INPUTS + SPARES
(PC current; V leads)
27 DIGITAL INPUTS + SPARES
(DAQ OK; EE Status; PC Status; Leads Temperature)
17 DIGITAL OUTPUTS + SPARES
(PC Permit; Flash Boxes; Current to cryo; Quench to cryo)