## Slide 1: Online data analysis
Franco J. Mangiarotti
CERN – TE-MSC-TF
2019.06.12 – 3rd IWSMTS, Uppsala, SE

## Slide 2: Online vs Offline data analysis
Online data analysis:
  Right-away after an event
  Minimum data for operation (QI, quench location, etc)
  Required to continue testing
  Focus on speed instead of depth
Offline data analysis:
  A few hours, days or even years after the event
  Exhaustive analysis, comparison with other events

## Slide 3: Online data analysis tools

## Slide 4: DIAdem
Great data visualization and manipulation tool
Already discussed in the previous two workshops (link1, link2)
Main software used by TF section in SM18

## Slide 5: DIAdem tools: OAQ
Program to analyze a quench right after it happens
User interaction to select:
  quench time,
  quenched segments,
  quench antenna,
  test parameters, …
Outputs a text file with the main test results

## Slide 6: DIAdem tools: DMM-processor
Multi-purpose software to analyze slow-acquisition, high precision data:
  Splices resistance
  Inductance
  AC loss
  RRR
  Superconducting transition
Outputs images and text result files

## Slide 7: DIAdem tools: QH analysis
Goal: comparing a QH discharge with a baseline
  Use V, I, R and τ
Manual (QH verificator)
  Visually compare curves with baseline
Automatic (QH analysis)
  Verify if deviations are within acceptable window
  Calculate parameters at given times

## Slide 8: Carpenter and other offline tools
Result text files uploaded to Carpenter database
  Carpenter info: link1, link2
Other programs use this data to do more analysis

## Slide 9: Online data analysis examples
IWSMTS

## Slide 10: Broken strands in MBRDS1
Slow training and limit in one location
“Inverse” precursor
Atypical ramp rate dependency
Decaying voltages during flat-top
Probably conductor damage in coil exit
  By-pass coil and retest
Probable location of damage

## Slide 11: High quench integral in MCBRDP1
Quench-back not as effective as expected
Tried multiple energy extraction devices
  QI < 23 kA2s
  Vmax < 450 V
Fast cycle time required fast software
Final workaround: 2x EE racks (Vmax < 900 V)

## Slide 12: Heater discharges in MBHSP109
First ~60 discharges: manually analyzed
  Check the curves look OK before continuing
Next ~70 discharges: automatically analyzed
  QH analysis software
  LabVIEW program
  PLC

## Slide 13: Current cycles in MBHSP109
~200 cycles from 5 to 11.85 kA every day
How to verify the magnet does not degrade?
  Quenches
  VI measurements
Analysis:
  Current cycles: no degradation
  Thermal cycles: ~0.5% degradation
5-11.85 kA cycles
VI measurement
Quench

## Slide 14: Summary
Online analysis is critical to magnet testing
  Validation of the test
  Early troubleshooting
  Permission to continue testing
Sharing tools and procedures between labs will help us get more out of the testing