## Slide 1: HL LHC IT STRING TEST
Marta Bajko CERN
11-12 June 2019 Uppsala Sweden FREIA

## Slide 2: CONTENT
The LHC STRING : the past experience @ CERN
The HL-LHC STRING
  Motivation
  Goals
  Configuration
  Main Components
  Experimental program in a nutshell
The STRING in the SM18
The time line of the project
Summary

## Slide 3: Previous experience @ CERN
STRING-1 (1994-1998)
One half LHC cell:
  3 MB (10 m) + 1 MQ
Validation of:
  Cryogenics (6 CD’s)
  Vacuum
  Quench (172) and protection
  Powering and energy extraction
STRING-2 (2000-2004)
One full LHC cell
  6 MB (15 m) + 2 MQ + correctors
Validation of:
  Cryogenics,
  Vacuum
  Quench and protection
  Powering
  Accelerator relevant operation (e.g.tracking of MQ and MB)
String-1 in SM-18
String-2 in SM-18

## Slide 4: The HL-LHC IT STRING MOTIVATION
LHC
In the HL-LHC configuration, the Inner Triplet (IT) region of IR1 and IR5 of the present LHC will be heavily modified.
In particular the Q1-Q2-Q3-D1 magnets will be completely different from the present LHC magnets, mainly due to the new technology they are based.
HL-LHC
Powering cables or BB and disconnections

## Slide 5: The HL-LHC IT STRING MOTIVATION
In the HL-LHC configuration, the Inner Triplet (IT) region of IR1 and IR5 of the present LHC will be heavily modified.
HL-LHC
Powering cables or BB and disconnections
D1 magnet will be superconductor instead of normal conductors as is today in the LHC.

## Slide 6: The HL-LHC IT STRING MOTIVATION
LHC
In the HL-LHC configuration, the Inner Triplet (IT) region of IR1 and IR5 of the present LHC will be heavily modified.
HL-LHC
Powering cables or BB and disconnections
In addition, the aperture will be much larger, the cold mass configuration will be completely different and the corrector package will be substantially modified as configuration and technology, too.

## Slide 7: The HL-LHC IT STRING MOTIVATION
In the HL-LHC configuration, the Inner Triplet (IT) region of IR1 and IR5 of the present LHC will be heavily modified.
HL-LHC
Powering cables or BB and disconnections
The IT quadrupoles (Q1-Q3) will use Nb3Sn instead of the Nb-Ti used by the present ones.

## Slide 8: The HL-LHC IT STRING MOTIVATION
In the HL-LHC configuration, the Inner Triplet (IT) region of IR1 and IR5 of the present LHC will be heavily modified.
HL-LHC
Powering cables or BB and disconnections
The powering of the magnets will be with higher current than the present LHC IR magnets
and will be made via a HT superconducting link and new generation superconducting current leads

## Slide 9: The HL-LHC IT STRING MOTIVATION
In the HL-LHC configuration, the Inner Triplet (IT) region of IR1 and IR5 of the present LHC will be heavily modified.
HL-LHC
Powering cables or BB and disconnections
The protection of the magnets based on Nb3Sn superconductor technology will be different from the present ones (ex. CLIQ and new QH) due to its particulate characteristics at low and medium field and the high magnetic energy stored ( 1.2 MJ/m, 2-4 x higher than in LHC) in the magnets in operational conditions.

## Slide 10
The HiLumi String will serve as a test bed for matters or conditions that either :
  (a) cannot be tested as a part of the components acceptance and characterization program, or
  (b) depend on the response of the integrated system.
The main motivation is to represent, as far as reasonably achievable in a surface, the various operation modes and make of the HL LHC IT STRING a test stand to STUDY and VALIDATE the COLLECTIVE BEHAVIOURE of the different systems: magnets, magnet protection, cryogenics for magnets and superconducting link, magnet powering, vacuum, and interconnections between magnets and superconducting link, alignment.
Ref. HL-LHC IT STRING Scope https://edms.cern.ch/document/1693312/1
The HL-LHC IT STRING GOAL
Alternative configurations are possible for tests, with dedicated cost and resources, but unforeseen failure modes may be missed

## Slide 11
P5L is the most complicated and coherent set up with the Sm18 installations and the tunnel is the smallest . We plan to reproduce the space allowed in that place of the tunnel for the interventions
Configuration of the HL-LHC IT STRING
There is an essential difference as in HL LHC STRING we do not reproduce the SLOPE of the LHC tunnel.
SPS
HL-LHC
P1
P2
P3
P4
P5
P6
P7
P8
SM18

## Slide 12
IP5
Q2a
Q2b
Q1
Q3
CP
D1
DFX
Prototype
Prototype
Prototype
Prototype
Series
Series
Series
BPM
BPM
Additional Instrumentation
and heaters in the BS possible
All components are “like series” (prototypes) or series and are owned by the WP
All infrastructure or components that can not be re-used in the HL-HC are owned by WP16
Operation temperature 1.9 K
Powering to I_ultimate
1 thermal cycle to room temperature
1 quench / day during operation
Cryogenics designed to allow max 400 W heat extraction
STRING defined between Q1 and D1, powered through Sc link
Additional instrumentation will be added only on prototypes
Common vacuum is an economic solution considered as baseline
Beam Screen only in Q1 and Q2a prototypes
DXF, DSH, DSL of 110 m : the first prototypes
Protection as in the HL-LHC ( CLIQ, QH, EE)
Powering as in HL-LHC
Prototype
Prototype
Main Steps
Main Components of the HL-LHC IT STRING

## Slide 13: Experimental Program
Installation
Inter-
connection
Cooling
HWC
Exp @ Inom
Training to Iultimate
Thermal Cycle
HWC to
Inom
Exp @ I nominal
Warm up
Chart: HWC+ TC HL LHC IT String aprox. 170 quenches
| 1 | 35 | 57 | 77 | 92 | 111 | 146 | 170 | 10%Inom | 40%Inom | 75%Inom | Inom | Iultimate | TC
Q1-Q3 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 5.8208 | 5.8208 | 5.8208 | 5.8208 | 5.8208 | 5.8208 | 5.8208 | 5.8208 | 20.4637 | 20.4637 | 20.4637 | 20.4637 | 20.4637 | 20.4637 | 20.4637 | 20.4637 | 36.38 | 36.38 | 36.38 | 36.38 | 36.38 | 37 | 38 | 39 | 40 | 41 | 42 | 42 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 0.3638 | 5.8208 | 5.8208 | 36.38 | 36.38 | 37 | 38
MCBXFb | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.016 | 0.016 | 0.016 | 0.016 | 0.016 | 0.05625 | 0.05625 | 0.05625 | 0.05625 | 0.05625 | 0.1 | 0.1 | 0.1 | 0.1 | 0.11664 | 0.11664 | 0.11664 | 0.11664 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.016 | 0.016 | 0.1 | 0.1 | 0.11664 | 0.11664
MCBXFa | 0.0022 | 0.0022 | 0.0022 | 0.0022 | 0.0022 | 0.0352 | 0.0352 | 0.0352 | 0.0352 | 0.0352 | 0.12375 | 0.12375 | 0.12375 | 0.12375 | 0.12375 | 0.22 | 0.22 | 0.22 | 0.22 | 0.25661 | 0.25661 | 0.25661 | 0.25661 | 0.0022 | 0.0022 | 0.0022 | 0.0022 | 0.0022 | 0.0352 | 0.0352 | 0.22 | 0.22 | 0.25661 | 0.25661
D1 | 0.0215 | 0.0215 | 0.0215 | 0.0215 | 0.0215 | 0.344 | 0.344 | 0.344 | 1.2094 | 1.2094 | 2.15 | 2.15 | 2.5078 | 2.5078 | 2.5078 | 2.5078 | 0.0215 | 0.0215 | 0.0215 | 0.0215 | 0.0215 | 0.344 | 0.344 | 2.15 | 2.15 | 2.5078 | 2.5078
HO | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001 | 0.001
all | 0.3895 | 6.216 | 21.8531 | 38.85 | 42.881 | 0.3895 | 6.216 | 38.85 | 40.881
Validation of the circuits and the protection systems powered as in HL-LHC ( first time for converters, Sc link and magnets)

## Slide 14: HL-LHC IT STRING in the SM18

## Slide 15
Summary
HL LHC IT STRING is foreseen to study the collective behaviour of the IT zone
The main components are: Q1-D1 with complete cold and warm powering
The test stand will be integrated into SM18 and will run
in the same time as the individual components test
Installation will start in 2020; Testing 2021 -2023
Infrastructure upgrade is ongoing
3 prototypes and 3 series magnets will be used
P5L will be reproduced without slope
180 quenches and up to 400 W heat
is planned to be possible to extract
ID CARD of the TEST STAND: HL-LHC IT STRING
TEST Facility LOCATION: SM18 (b. 2173)
TEST DATE: 2021-2023
OPERATIONAL TEMPERATURE: 1.9 K
OPERATIONAL CURRENT: Ultimate (108% Inominal = 18 kA )
MAGNETS: Q1, Q2a, Q2b, Q3, CP, D1
COLD POWERING: SC link ,HTS leads DFH and DFX,
WARM POWERING: 1 x PC for 18 kA + 3 Trim for Q1-Q3 + 6 x 2 kA + 1 x 12 kA + 9x 0.1 kA + WCC
PROTECTION: CLIQ and QH ; EE where is baseline