## Slide 1: News from the KEK test facility
Kento Suzuki on behalf of the CERN-KEK collaboration
3rd Magnet Test Stand in Uppsala, K. Suzuki, June 11

## Slide 2: Japanese Contribution to HL-LHC: D1 magnets
Beam separation dipole (D1) by KEK
  Design study of D1 for HL-LHC within the framework of the CERN-KEK collaboration since 2011.
  150 mm single aperture, 35 Tm (5.6 T x 6.3 m), Nb-Ti technology.
  Development 2-m long model magnets (3 units) at KEK
Deliverables for HL-LHC
  1 full-scale prototype cold mass (MBXFP)
  6 series cold masses (MBXF1-6)
7 units x 7-m long cold masses
MOU was contracted at MEXT, Japan on 6th July 2018

## Slide 3: Schedule
Bill opening for the Prototype and Series : 24th May
  Successful bidder : Hitachi Co. Ltd.
Prototype fabrication has to start before cold test of 3rd Model at Sep. 2019.
Production of Series 1 will start after the vertical test of Prototype.
Foreseen milestones: delivery date of cold masses
  MBXFP (for string test): Nov. 2020.
  MBXF1-4 (for the HL-LHC machine): April 2023.
  MBXF1-6 (all): June 2024.
Contract signed
Start of series production
Deadline of prototype
Deadline of series 4

## Slide 4: Test stand at KEK

## Slide 5: Bird’s eye view of KEK
Super KEKB (e- + e+)
Mt. Tsukuba (877m)
Hokkaido
Tokyo
Test stand at
Cryogenics Science Center

## Slide 6: KEK Test Stand
Previous reports can be found at :
  1st workshop
    https://indico.cern.ch/event/507584/contributions/2027926/attachments/1289830/1920459/20160613KEKTestStand_NakamotoFinal.pdf
  2nd workshop
    https://indico.cern.ch/event/704235/contributions/2931999/attachments/1651165/2640917/20180508KEKD1_TestStandWSFinal.pdf
Control room
7.5 m deep cryostat
20 t crane
MBXF header
Liquefier
(2400 L dewer)

## Slide 7: Vertical cryostat
Operating Temp.: 4.4 K to 1.9 K by HeII Sub-cooler (55 W for MQXA)
Capacity of 1.9 K bath: 7524 mm deep, 700 mm in a diameter.
  Can accommodate the prototype/series magnet
New header for the D1 (MBXF) in 2014
Anti-cryostat for field measurement: O.D. 141.3 mm
  Quench antennas: 11 arrays for 7 m long magnet
15 kA Current Leads
  HVWL: 1.5 kV

## Slide 8: Cold test of the model magnets
1st model
(MBXFS1, 1b)
2nd model
(MBXFS2)
While good training performance was achieved in the 2nd model,
Unacceptable offset in b3 at the magnet center in the 2nd model.
The coil possibly deforms due to the large pre-load
~20 unit
DC loop
at the magnet center

## Slide 9: Cold test of the model magnets
1st model
(MBXFS1, 1b)
2nd model
(MBXFS2)
~20 unit
DC loop
at the magnet center
The 3rd short model magnet production :
- FINAL model magnet
- 2nd model’s cross section, similar pre-load as well
- Check reproducibility
The cold test is planned to be held in this summer
Results will be reported at the next MT26
While good training performance was achieved in the 2nd model,
Unacceptable offset in b3 at the magnet center in the 2nd model.
The coil possibly deforms due to the large pre-load

## Slide 10: Readiness for production of the Prototype and Series

## Slide 11: Acceptance criteria for Prototype/Series
During fabrication, conformity tests have to be conducted for its quality assurance
Electrical test
  Coil to ground : 2.6 kV (Warm) / 1.3 kV (LHe)
  Coil to quench heater : 4.6 kV (Warm) / 2.3 kV (LHe)
Alignment / Field quality
  Magnetic center axis : within ± 5 mm
  Integrated field angle : within ± 5 mrad
  Deviation of local field center / angle : within ± 2 mm / 2 mrad
  Field integral : |b3| < 2.9 unit, |b5| < 1.5 unit, ..
By the warm field measurement
Performed at
the test bench

## Slide 12: Readiness for the electrical test
Feed-through
+HV
+HV
Electrical tests with the 2nd model magnets have been performed under the LHe (1.9 K) condition after the cold test
Coil-to-ground (1.3 kV):
  Applied through the current lead (CL)
  Leakage current increases linearly
Magnet
CL
heater line
Lead cable

## Slide 13: Readiness for the electrical test
Feed-through
+HV
Electrical tests with the 2nd model magnets have been performed under the LHe (1.9 K) condition after the cold test
Coil-to-heater (2.3 kV):
  Applied through the feedthrough of the header
  Breakdown before reaching 2 kV
Magnet
heater line
Lead cable
Breakdown

## Slide 14: Countermeasure for the weak channels
Individual insulation performance of the header was checked without the magnet
  Unacceptable weak insulation for both channels of coil-to-ground (CL) and heater-to-ground (feedthrough)
  He gas flowing through the CL hollow to avoid thermal penetration into the cryostat, resulting in frost around CL
  Some pin plugs were weakly connected to sockets of the feedthrough and partially exposed to ~1.5 atm He gas
ICE
Special cryogenic operation to eliminate the frost is established Improvement works for the pin-socket connection are underway
→ Large leakage current
Feedthrough of the
heater lines
Dry condition
→ Breakdown (Passien’s law)

## Slide 15: Countermeasure for the weak channels
Individual insulation performance of the header was checked without the magnet
  Unacceptable weak insulation for both channels of coil-to-ground (CL) and heater-to-ground (feedthrough)
  He gas flowing through the CL hollow to avoid thermal penetration into the cryostat, resulting in frost around CL
  Some pin plugs were weakly connected to sockets of the feedthrough and partially exposed to ~1.5 atm He gas
ICE
Special cryogenic operation to eliminate the frost is established Improvement works for the pin-socket connection are underway
Feedthrough of the
heater lines
Dry condition
→ Breakdown (Passien’s law)
Shortly ready for the Prototype / Series
→ Large leakage current

## Slide 16: Warm field measurement: SSW for Prototype/Series
Field angle with respect to fiducials (reference alignment points) will be determined by the warm field measurement with SSW (Single Stretched Wire).
The measurement system was already developed for SuperKEKB QCS magnet and is now available for the D1.
  The dedicated team joined the HL-LHC D1 project.
  Preparation of measurement for the 7m-long prototype cold mass is underway in Nikko-Exp. Hall at KEK.
Nikko-exp. hall for SuperKEKB
Area (15m x 5m) for MFM and survey for D1
SSW system of QCS magnet for SuperKEKB

## Slide 17: Warm field measurement: Rotating coil system for Prototype/Series
Local field angle/ magnetic center will be determined by warm field measurements with a rotating coil which is being designed for the 7-m long magnet
Our test stand can accommodate the overall measurement system (L~15m)
Preparation of instruments is ongoing in collaboration with the QCS SuperKEKB accelerator team
KEK Test stand
D1 Cold mass
Rotating coil system

## Slide 18: Summary
KEK will soon start the production of the Prototype
Readiness for the production
  Electrical test
    We have investigated performance and some improvements works are ongoing
  Field measurement
    Preparation for the measurement instrumentations in collaboration of the QCS SuperKEKB acceleartor team

## Slide 19: Supplement

## Slide 20: Design overview from D1 (MBXF)
 | A series production (7m) | MBXFS2 (2 m)
Coil aperture | 150 mm | 
Field integral | 35 T m | 9.5 T m
Field (3D) | Nominal: 5.60 T, Ultimate: 6.04 T | 
Peak field (3D) | Nominal: 6.58 T, Ultimate: 71.4 T | 
Current | Nominal : 12.047 kA, Ultimate 13.280 kA | 
Operating temperature | 1.9 K | 
Field quality | <10-4 w.r.t B1 (Rref=50 mm) | 
Load line ratio (3D) | Nominal: 76.5%, Ultimate: 83.1% at 1.9 K | 
Differential inductance | Nominal: 4.0 mH/m | 
Conductor | Nb-Ti: LHC-MB outer cable | 
Stored energy | Nominal: 340 kJ/m | 
Magnetic length | 6.26 m | 1.67 m
Coil mech. length | 6.58 m | 2.00 m
Magnet mech. length | 6.73 m | 2.15 m
Heat load | 135 W (Magnet total) 2 mW/cm3 (Coil peak) > 25 MGy | 
Radiation dose |  | 
19
13
8
4
4 blocks
44 turns
Technical challenges
・Large aperture： Management of coil size and pre-stress.
・Radiation resistance：Radiation resistant material for coil parts. Cooling capability.
・Iron saturation：Good field quality from injection to nominal current

## Slide 21: Cold test of the model magnets
1st model
(MBXFS1, 1b)
2nd model
(MBXFS2)
Training history so far
Good training performance
achieved in the 2nd model due to sufficient pre-load

## Slide 22: Issue in field of quality in the 2nd short model
q
-a
+a
dx
dy
Oval cross-section
Circular cross-section
Found offset (~20 units) in b3 which is not acceptable according to the requirement
Due to large pre-load (120 MPa at the magnet pole), oval coil deformation was possibly occurred during fabrication
Z scan
DC loop
a=0.4 mm

## Slide 23: Electronical insulation performance (cont’d)
Special study performed for eliminating the frost by our cryogenic technicians
  Stopping the He gas flow allows thermal penetration into the cryostat
  To reduce consumption of LHe, not only the test-stand liquefiers but primary ones (at different facility) are also operated cooperatively
ICE
1500 V applied to CL

## Slide 24: FINAL model magnet production: 3rd model
After yoking
Same magnetic cross section as that of the 2nd short model
  Similar pre-load is applied as well
To ensure effects from the coil deformation, the warm field measurement is being conducted for each fabrication step
  Very important feedback to the prototype design
Warm field measurement system
Cold test is planned to be held in this summer (August)
New results is expected to be reported at the next MT26

## Slide 25: Electronical insulation issue (Cont’d)
Also heater-to-ground (cryostat) withstand voltage was also limited to 1.8 kV while the target voltage is 2.3 kV (under LHe condition)
Some pin plugs were weakly connected to sockets of the feedthrough and partially exposed to ~1.5 atm He gas
Feed-through
Feedthrough for the
heater lines
Leakage current when
Heater-to-ground
voltage ramp to 2 kV
Breakdown voltage
Design improvement is underway for

## Slide 26
Manufactured by Toshiba in 2000 for vertical cold tests of LHC-MQXA magnets.
  19 LHC-MQXA (7m), 32 J-PARC SCFM (4m)
Applicable Law: Japanese High Pressure Gas Safety Act
  Operation at 1.9 K is exceptional. Category of “Designated Equipment”
Operating Temp.: 4.4K to 1.9K
Cooling
  300K to 40K by GHe, 40K to 4.4 K by LHe
  4.4 K to 1.9K by HeII Sub-cooler (55W for MQXA)
Capacity
  whole bath: 9020 mm deep, 700 mm in a diameter.
  1.9 K bath: 7524 mm deep, 700 mm in a diameter.
  Weight: 8.6 ton (MQXA). Need to check for D1.
He Cryogenic Plants (see next slide in detail)
New header for the D1 (MBXF)
  Manufactured in 2014, approval of the JHPG Safety Act in 2015.
  Anti-cryostat for field measurement: O.D. 141.3 mm
  Quench antennas: 11 arrays for 7 m long magnet
  Feedthrough: 48 poles x 10
  HVWL: 1.5 kV (present limit 0.5 kV.)
  15 kA Current Leads
    Manufactured by Fuji Electric in 2015. All copper base. (50L/h for a pair)

## Slide 27: HeII Sub-Cooler
Pre-heat exchanger
  Copper spiral tube (I.D. 12mm, Spiral Dia. 42 mm)
  Fine silver-plated copper balls
  Efficiency 88%
J-T expansion valve
Main heat exchanger
  Design: DT=30 mK at 80 W, 1.9 K.
  Required surface area: > 3.0 m2
  4.4 m long copper tubes: 3 x f 76.2 mm, 10 x f 12 mm.
Pumping system
  4 parallel lines
    2 x Roots pumps: 2 x 900 m3/h
      SHIMADZU MB-1400
    1 x Oil free pump: 630 m3/h
      TAIKO MDP-1015
  Note: Current performance is limited by cooling capacity of a water chiller (old!!).
    Only 2 pumiping lines are operational.

## Slide 28: Cryogenic Plants
Refrigerator/Liquefier for Test Stand
160 L/h, 2400 L dewar
Teisan / L’Air Liquide in 1987 for the TRISTAN-AMY detector
New cold box in 2007
Backup of the primary refrigerator for LHe supply.
Helium liquefying rate is sufficient to cover both supply for users and magnet testing.
Attention to GHe handling
  limitation in purification system
  difficulty to predict GHe recovery from KEK sites
Neighbor refrigerator (Primary)
350 L/h, 5000 L dewar
LINDE LR280 in 2014
Mandatory to supply LHe to KEK users.
20 m long LHe transfer line to the test stand.
  In linkage operation: 510 L/h max.

## Slide 29: Control System
CENTUM VP, Yokogawa Electric
  A distributed control system (DCS) as a platform for automated control and operation of the cryogenic plant.
  Programmed by KEK engineers.
  Interlock for 15 kA P/C (slow down or shutoff)
    Monitor: LHe level, CL status and refrigerator
  Historical trend data
Ex) display for main cryostat control
Ex) display of interlock for 15 kA P/C

## Slide 30: Power Converter
Manufactured by IDX in 1993 for SSC-SDC magnet development.
Nominal: 15 kA, 15V
Thyristor switch for prompt shutoff.
Dump resistor of 73 mW (grounding at middle point ) for the D1
  Available: 0, 12.5, 25, 50, 75 and 100 mW.
Water cooling: 150 L/min, 10 kg/cm2
Quench detectors
  2 x Balanced Voltage (Main)
  2 x Total Voltage
External 15 kA DCCT (Zero-Flux Current Transformer)
  Fully calibrated at CERN as a standardization of current.
  But unwanted shutoff caused by vibration during the excitation in May 2016.
  Performance degradation is concerned.
Note: some contact failures found in relays through the D1 model magnet testing.
  aged deterioration…
  Overhaul must be done be as soon as we can.

## Slide 31: Measurement System - Present -
Isolation Amp: NF P-62A, 76 ch
Fast DAQ:
  NI PXI 1643 (16bit, 250 kS/s/ch), 88 ch
    Voltage taps, quench antennas, P/C, etc.
Slow DAQ: GP-IB
  KEYSIGHT 3458A multimeter (8.5 digit) x 3
  Kyowa UCAM-60B for strain gauge measurement, currently 30 ch (80 ch max.)
Software: Labview (& KEYSIGHT VEE only for field measurement)
3 PCs: Fast DAQ, Slow DAQ, MFM.

## Slide 32: Field Measurement System
Vertical Measurement
Rotating coil in anti-cryostat (I.D. 108.3mm) at “warm” temperature.
  Printed-circuit board
  3 radial coils: B1 and analogue bucking
  Long (350mm) and short (80mm) arrays
  GN2 flow from the end to suppress thermal shrinkage of the pipe
7 m long GFRP shaft
  not long enough for the 7 m magnet, but it can be extended.
Encoder: HEIDENHAIN RON 255
Integrator: MetroLAB PDI-5025 x 3
Magnet scale: SONY LY51
Horizontal Measurement
For warm measurements of LHC-MQXA and J-PARC-SCFM cold mass.
But the system is dismantled for the time being…
  The system will come back for the D1 magnets.

## Slide 33: Operating Personnel
Operators for the cryogenic plant
  3 to 4 weeks for a test cycle.
  24 hours operation >> 3 shifts/day, 5 days/week.
  15 shifts/week: 1 shift for 8.75 hours
  10 shifts/week by outsourcing from 16:30 to 9:00 for safety reason.
  5 KEK staffs and 2 outsourcing workers
    They must be holders of “a high pressure gas production safety management”.
Operators for the magnet test
  Quench Tests: from 9h to 19h (sometimes 20h)
  Field measurement: mainly daytime, through nighttime if necessary.
  3 to 4 KEK staffs (not only dedicated to the test…)
* Staff of Cryogenics Science Center: 17 in total.
  Tsukuba: Researchers 6, Post-doc 2, Engineers 4
  Tokai: Researchers 2, Post-doc 1, Engineers 2
  Mandatory: LHe supply for users
  Projects: J-PARC (T2K neutrino, COMET, g-2, muon beam lines, etc.), HL-LHC upgrade, KAGURA (gravitational telescope)