## Slide 1: The CLIC Study Compact Linear Collider
Andrea Latina, CERN
Uppsala University – May 9, 2019
on behalf of the CLIC and CLICdp Collaborations
Notes: The Compact Linear Collider (CLIC) is a proposed TeV-scale high-luminosity linear particle collider that aims to explore the next energy frontier.

## Slide 2: The CLIC Study Compact Linear Collider
 Project overview
 Physics reach
 Accelerator technologies
 Outlook
on behalf of the CLIC and CLICdp Collaborations
Compact Linear Collider e+e– collisions up to 3TeV http://clic.cern/
Andrea Latina, CERN
Uppsala University – May 9, 2019

## Slide 3: Collaborations
CLIC detector and physics (CLICdp)
30 institutes from 18 countries
CLIC physics prospects & simulation studies
Detector optimization + R&D for CLIC
CLIC accelerator collaboration
~60 institutes from 28 countries
http://clic.cern/
CLIC accelerator design and development
(Construction and operation of CTF3)

## Slide 4: CLIC
FCC-ee

## Slide 5: Luminosity vs Energy
Center of mass energy [GeV]
Total luminosity [1034 cm-2s-1]
A. Blondel, F. Zimmermann, arXiv:1112.2518 (2011).
A. Blondel et al., arXiv:1208.0504 (2012).
A. Bogomyagkov, E. Levichev, and D. Shatilov, Beam-beam effects investigation and parameters optimization for a circular e+e− collider at very high energies, Phys. Rev. ST Accel. Beams 17, 041004 (2014).
K. Ohmi, N. Kuroo, K. Oide, D. Zhou, and F. Zimmermann, Coherent Beam-Beam Instability in Collisions with a Large Crossing Angle, Phys. Rev. Lett. 119, 134801 (2017).
D. Shatilov, FCC-ee Parameters Optimization, ICFA Beam Dynamics Newsletter #72 (2017).

## Slide 6: CLIC European Strategy Inputs
http://clic.cern/european-strategy
Submitted to CREB
Reports on design, technology, and implementation
Notes: A number of documents report on the CLIC accelerator and detector and physics status in advance of the European Strategy update 2018-2020, including the design, technology, and implementation aspects of the CLIC accelerator and the detector, and summaries of the physics potential of CLIC.

## Slide 7: CLIC European Strategy Inputs

## Slide 8: CLIC layout and power generation
Baseline electron polarisation ±80%
380 GeV c.o.m. energy
Notes: Two-beam acceleration scheme, in which
normal-conducting high-gradient
12 GHz accelerating structures are powered via a high-current drive beam.

## Slide 9: CLIC layout – final stage
Baseline electron polarisation ±80%
3 TeV c.o.m. energy

## Slide 10
CLIC parameters

## Slide 11
Mature CLICdet detector model; performance extensively validated:
CLIC detector

## Slide 12: Luminosity staging baseline
Baseline polarisation scenario adopted: electron beam (–80%, +80%) polarised in ratio (50:50) at √s=380GeV ; (80:20) at √s=1.5 and 3TeV
increased from
0.5+0.1ab–1 1.5ab–1 3ab–1
New!
Staging and live-time assumptions following guidelines consistent with other future projects: Machine Parameters and Projected Luminosity Performance of Proposed Future Colliders at CERN
arXiv:1810.13022, Bordry et al.
Electron polarisation enhances Higgs production at high-energy stages and provides additional observables
gg collider using laser scattering also possible Upgrades using novel accelerator techniques also possible

## Slide 13: CLIC Physics
H
n
n
W
W
e–
e+
H
H
Z
Z
H
e–
e+
H
H
tt at √s=3TeV
Issues not addressed by SM: origin of the weak scale interactions dark matter origin of matter/antimatter asymmetry
Many new studies focused on discovery prospects at CLIC Exploring the physics landscape as broadly as possible
The CLIC Potential for New Physics
Yellow Report in preparation

Precision Higgs

Precision top

Beyond Standard Model
New!

## Slide 14: Higgs coupling sensitivity
New!
Based on Eur. Phys. J. C 77 475 (2017) updated to new luminosity scenario
Each energy stage contributes significantly
Dl/l =
+11% –7%
complementary at 1.5TeV
lHHH
Z
Z
H
e–
e+
H
H
H
n
n
W
W
e–
e+
H
H
dominates
at higher √s
lHHH
Full GEANT-based simulation studies including beam backgrounds of many channels at all 3 stages –> global fit including correlations;
Precision <1% for most couplings
c/b/W/Z/g couplings significantly more precise than HL-LHC even after 380GeV stage
GH is extracted with 4.7 – 2.5% precision
Using M(HH) differential distribution:
New!
no assumptions on additional Higgs decays – unique to lepton colliders
Higgs self-coupling requires high energy
~
Notes: All results limited by 0.6% precision of gHZZ from s(HZ) measurement

## Slide 15: Top physics
Hadronic decays of high-energy top quarks do not lead to 3 separated jets –> identify substructure
e+e– -> tt -> qqqqbb
First study of boosted top production in e+e–
 FCNC decays  CP properties of ttH  cross-section and AFB -> resolved, semi-resolved, boosted
 couplings to Z and g  EFT interpretation
 observe 1S ‘bound state’, Dmt ~ 50 MeV
 Intending threshold scan around 350 GeV (10 points, ~1 year) as well as main initial- stage baseline √s=380GeV
 sensitive to top mass, width and couplings
√s=3TeV
–> initial and high-energy stages are very complementary
Polarisation provides new observables
arXiv 1807.02441: Top-quark physics at the CLIC electron–positron linear collider
in journal review
sin2f
Dsin2f
New!

## Slide 16: CLIC Accelerator
 Key technologies have been demonstrated  CLIC is now a mature project, ready to be built

## Slide 17: Key accelerator challenges
High-current drive beam bunched at 12 GHz
Power transfer + main-beam acceleration
100 MV/m high gradient in main-beam cavities
Produce, transport, and collide low-emittance beams
System integration, alignment and stability, engineering, cost, power …

## Slide 18
CLIC Test Facility (CTF3)
18
Uppsala - May 2019
Andrea Latina

## Slide 19: Accelerator challenges
Key challenges:
High-current drive beam bunched at 12 GHz
Power transfer + main-beam acceleration
~100 MV/m gradient in main-beam cavities
Low emittance generation
Alignment & stability
Drive beam arrival time
stabilised
to CLIC specification of 50fs:
28A
Drive beam quality: Produced high-current drive beam bunched at 12GHz
Current in combiner ring
Examples of measurements from CLIC Test Facility, CTF3, at CERN. CTF3 now the ‘CERN Linear Electron Accelerator for Research’ facility, CLEAR
3 GHz
x2
x3
12 GHz

## Slide 20: Accelerator challenges
31MeV = 145MV/m
Key challenges:
High-current drive beam bunched at 12 GHz
Power transfer + main-beam acceleration
~100 MV/m gradient in main-beam cavities
Low emittance generation
Alignment & stability
Demonstrated 2-beam acceleration

## Slide 21: Accelerator challenges
Key challenges:
High-current drive beam bunched at 12 GHz
Power transfer + main-beam acceleration
~100 MV/m gradient in main-beam cavities
Low emittance generation
Alignment & Stability
X-band performance: achieved 100MV/m gradient in main-beam RF cavities

## Slide 22: Accelerator challenges
The CLIC strategy:
Align components (10μm over 200m)
Control/damp vibrations (from ground to accelerator)
Measure beams well – allow to steer beam and optimize positions
Algorithms for measurements, beam and component optimization, feedbacks
Tests in existing accelerators of equipment and algorithms (FACET at Stanford, ATF2 at KEK, CTF3, Light-sources)
Key challenges:
High-current drive beam bunched at 12 GHz
Power transfer + main-beam acceleration
~100 MV/m gradient in main-beam cavities
Low emittance generation
2008
CLIC emittance at damping rings
Nano-beams

## Slide 23: Accelerator challenges
The CLIC strategy:
Align components (10μm over 200m)
Control/damp vibrations (from ground to accelerator)
Measure beams well – allow to steer beam and optimize positions
Algorithms for measurements, beam and component optimization, feedbacks
Tests in existing accelerators of equipment and algorithms (FACET at Stanford, ATF2 at KEK, CTF3, Light-sources)
2016
Key challenges:
High-current drive beam bunched at 12 GHz
Power transfer + main-beam acceleration
~100 MV/m gradient in main-beam cavities
Low emittance generation
CLIC emittance at damping rings
Nano-beams

## Slide 24
24
PACMAN, Marie Curie Action:
vertical RMS error of 11μm
i.e. accuracy is approx. 13.5μm
2) Beam-based alignment
Stabilise quadrupole
O(1nm) @ 1Hz
1) Pre-align BPMs+quads
accuracy O(10μm) over about 200m
3) Use wake-field monitors accuracy O(3.5μm) – CTF3
FACET
FERMI
Low emittance transport

## Slide 25
Final focus system
ATF2 @ KEK

## Slide 26: Towards industrialisation
Investigating paths to industrialisation
Baseline manufacturing technique: bonding and brazing
Alternatives: brazing as for SwissFEL machining halves
Target is structures that are low-cost & easy-to-manufacture

## Slide 27: SwissFEL – C-band linac
104 x 2m-long C-band structures
(beam  6 GeV @ 100 Hz)
Similar μm-level tolerances
Length ~ 800 CLIC structures
Being commissioned

## Slide 28: Power
Preliminary power consumption for 380GeV CLIC
Experimental area
Cooling & ventilation Safety systems Machine control & operational infrastructure
Included so far:
+~20–30%
( Klystron-based option: 142 MW + ~20-30% )
Final power estimate will be < 200MW (compared with 252MW in 2016)
Being updated for changes in design parameters, and using operating (not specification) values for RF power sources and magnet power supplies
Vacuum systems
RF and RF power systems Magnet & magnet powering systems Beam instrumentation Active alignment and stabilization in ML and BDS Electricity
To be added:
Total energy use will be updated once power consumption complete
2016 estimate
~

## Slide 29: 380 GeV Klystron option

## Slide 30: Cost
Machine has been bottom-up re-costed in 2018
Cost  ~5.9 BCHF for initial stage
(Finalised for ESU)
Project Implementation Plan 2018
Maintenance cost 116 MCHF per year.

## Slide 31: Schedule
Updated schedule: Construction + commissioning: 7 years
Year
Year
Year
Year
Year
Year
Year

## Slide 32: Schedule
Updated schedule: Construction + commissioning: 7 years, followed by 25–30 year physics programme

## Slide 33: CLIC roadmap

## Slide 34: Next phase
2020–2025 Preparation Phase:
Finalisation of implementation parameters Preparation for industrial procurement Drive Beam Facility & other system verifications Technical Proposal of the experiment Site authorisation
2026 Construction start

## Slide 35: CLIC technology applications
EoI to SPSC, autumn 2018: https://cds.cern.ch/record/2640784
Electron accelerator implementation at CERN
X-band based 70m LINAC to ~3.5 GeV in TT4-5
Fill the SPS in 1-2s (bunches 5ns apart) via TT60
Accelerate to ~16 GeV in the SPS
Slow extraction to experiment in 10s as part of the SPS super-cycle
Experiment(s) considered by bringing beam back on Meyrin site using TT10
–> Potential experiment e.g. LDMX Would fulfil many of CLIC accelerator next steps
INFN Frascati advanced acceleration facility EuPRAXIA@SPARC_LAB
Eindhoven University led SMART*LIGHT Compton Source
CLIC technology for different applications:
CompactLight: EU co-funded FEL design study
SPARC at INFN-LNF
Medical applications
CompactLight

## Slide 36: CLEAR
Main activities:
CLIC & high-gradient X-band
Instrumentation R&D
VESPER irradiation test station Electronic components for space applications (with ESA) Medical applications (VHEE) Electronic components for accelerators and detectors
Novel techniques: plasma focusing and acceleration, THz radiation, dielectric structures
Open to proposals for user experiments
80–220 MeV electrons Bunch charge 0.01–1.5 nC
CALIFES beamline
CLEAR started with beam in August 2017
CERN Linear Electron Accelerator for Research

## Slide 37: Summary
 CLIC is now a mature project, ready to be built
 The main accelerator technologies have been demonstrated
 The physics case is broad and profound
 The detector concept and detector technologies R&D are advanced
 The full project status is presented in a series of Yellow Reports
Thanks to all who provided material, including: Steinar Stapnes, Phil Burrows, Daniel Schulte, Walter Wuensch, Aidan Robson, Lucie Linssen, Andrea Wulzer, Roberto Franceschini, Jorge de Blas, Philipp Roloff

## Slide 38: CLIC workshop January 2019
215 participants