## Slide 1: Cryostats
Rocío Santiago Kern
On behalf of the FREIA team
FREIA Laboratory, Uppsala University
8th of May 2019

## Slide 2: Contents
Introduction and main concepts
Horizontal cryostat HNOSS
Vertical cryostat Gersemi
Double spoke cryomodule
Cold boxes

## Slide 3: Contents
Introduction and main concepts
Horizontal cryostat HNOSS
Vertical cryostat Gersemi
Double spoke cryomodule
Cold boxes

## Slide 4: What and Whom?
cryogenics
- liquid helium
- liquid nitrogen
control room
- equipment controls
- data acquisition
RF power sources
3 bunkers
with test stands
horizontal cryostat
vertical cryostat
Facility for Research Instrumentation and Accelerator Development
Competent and motivated staff
collaboration with physics (IFA), engineering (Teknikum), TSL
and Ångström workshop
Funded by KAWS, Government, Uppsala Univ.
State-of-the-art Equipment

## Slide 5: FREIA Collaborations
FREIA has collaborations to test the following:
  Superconducting (SC) double spoke cavity for ESS
  (done)
  Superconducting (SC) high beta elliptical cavity for ESS
  (done)
  Cryomodules housing two superconducting double spoke cavities for ESS
  (ongoing)
  Superconducting dipole magnets for CERN Hi-Lumi project
  (to start at the end of the year)
  Superconducting cold boxes for CERN (together with RFR Solutions)

## Slide 6: Superconductivity
  SC materials offer almost no electrical resistance  Lower heat disipation in the material
Cavities
Magnets
- Wires conduct much larger electric currents
- More intense magnetic fields
- Less heat to the cavity
- More power available for the beam
- Helium liquefaction plant
- Using LHe/GHe means a recovery system
Toperation = 2 K (31 mbar)
Superfluid He
Source: https://en.wikipedia.org/wiki/Superconductivity#/media/File:Timeline_of_Superconductivity_from_1900_to_2015.svg

## Slide 7: Cryostat Fundamentals
Cryogens in
Cryogens out
Main conversions
Pplug = 1 kW to generate 1 W cooling power at 4.2 K
VGHe at 293 K = 700 VLHe at 4.2 K
Minimise the amount of heat that reaches the cold parts, i.e. the device under test (DUT)
  Convection  vacuum
  Radiation  thermal shield, multilayer insulation
  Conduction  thermal anchors
LHe 4K Tank
Joule-Thomson Valve

## Slide 8: Cryostats: General Components
Vacuum vessel
  Main container, outermost component
  Under vacuum. A high vacuum (≤10-5 mbar) already reduces the heat into the cold parts by 90%
Thermal shield
  Blocks the thermal radiation
  Works as a thermal anchor or heat sink for the equipment connected to room temperature, like valves and cable instrumentation linking to equipment placed at lower temperatures
  Usually cooled via LN2 or GHe at a certain temperature
Multi layer insulation (MLI)
  Further reduces the radiation heat
  Might help in an event of vacuum insulation loss
  Wrapped around the thermal shield, the DUT, etc.
Magnetic shield
    Made of a high permeability material
    Reduces the effect of the earth’s magnetic field on the cavities
    Can be placed at any temperature
    Unless removable cannot be in place while testing magnets: saturation

## Slide 9: Contents
Introduction and main concepts
Horizontal cryostat HNOSS
Vertical cryostat Gersemi
Double spoke cryomodule
Cold boxes

## Slide 10: HNOSS
Purpose: test of superconducting cavities
Has two parts:
  Valvebox (VB): contains all the valves and tanks and most of the piping
  The cryostat itself (HCS): houses the cavities and the table
Both parts have:
  Magnetic shield (room temperature)
  Thermal shield (LN2 temperature)
Total volume ca. 7 m3

## Slide 11: Vacuum Vessel
Material: 304L
Flange types (high vacuum): ISO F, ISO K, ISO KF
Flange types (ultra high vacuum): ISO CF

## Slide 12: Thermal Shield
Material: Al (EN 573-3 AW6060T6 )
Other usual material: Cu (more expensive, more weight but better σth)
Cooling pipes: Aluminium (omega-type pipes)
Transition between Al (thermal shield) and SS (pipes from the valvebox)
Thermal shield not continuous

## Slide 13: Magnetic Shield
Made of several parts of mu-metal (high permeability material) welded together
The material is made into shaped and placed on a furnace following a certain procedure to activate the material
This material is very sensitive to further handling: those parts of the material exposed to work will lose the magnetic properties

## Slide 14: Transfer lines
Material: SS
Space between the transfer line and the cooling lines
LN2 and LHe line separated, not touching
Insulation material: multilater insulation (MLI)
Usually under vacuum

## Slide 15: Transfer Lines: Couplings
Swagelok VCR
Bayonet Female Male
For cryogen transfer (LN2, LHe)
CF gasket
Picture taken from Kurt Lesker
Swagelok VCR:
  Requires less space
CF connections:
  Only to be used if need to remove for every test
Bayonet:
  Lower heat leak (small sizes), thus more efficient in transfer
  Provide a vacuum insulated joint
  More expensive

## Slide 16: Contents
Introduction and main concepts
Horizontal cryostat HNOSS
Vertical cryostat Gersemi
Double spoke cryomodule
Cold boxes

## Slide 17: Purpose
To test superconducting magnets (max 2kA)
To test superconducting cavities

## Slide 18: Valvebox
Used to deliver the cryogens to the cryostat
Height: 2300 mm
Vacuum Vessel Material: SS
Thermal shield material: Cu
Flange types (high vacuum): ISO F, ISO K, ISO KF

## Slide 19: Vacuum Vessel and Thermal Shield
Vacuum Vessel Material: SS
Thermal shield material: Al
Thermal shield not continuous
Flange types (high vacuum): ISO F, ISO K, ISO KF
Vacuum port
Vacuum Vessel
Thermal Shield
Multi transfer line

## Slide 20: Pressure Vessel

## Slide 21: Contents
Introduction and main concepts
Horizontal cryostat HNOSS
Vertical cryostat Gersemi
Double spoke cryomodule
Cold boxes

## Slide 22: Purpose
The spoke cryomodule section at ESS will increase the protons beam energy from 90 to 216 MeV
This section
  Is supercoducting
  Is 56 m long
  Has 26 double spoke cavities
  In 13 cryomodules
Source: P. Duchesne et al. “Design of the 352 MHz Beta 0.50 double s
poke cavity for ESS”, Proceedings of SRF2013, Paris, France (FRIOC01)

## Slide 23: Components
It is a specialized version of HNOSS
Has two double spoke cavities inside
  hanging from tie-rods
  each has a magnetic shield around
Thermal shield made of Al, cooled via LN2
  Note: For ESS cooling is with GHe (no LN2 available)
The prototype has more instrumentation than the series cryomodules
Source: G. Olry et al. “Recent Progress of ESS Spoke and Elliptical
Crymodules”, Proceedings of SRF2015, Whistler, BC, Canada (TUAA06)
Source: P. Duthil et al. “Design and Prototyping of the Spoke
Cryomodule for ESS” Proceedings of HB2016, Malmö, Sweden, WEAM4Y01
Source: P. Duthil et al. “Design and Prototyping of the Spoke
Cryomodule for ESS” Proceedings of HB2016, Malmö, Sweden, WEAM4Y01

## Slide 24: Contents
Introduction and main concepts
Horizontal cryostat HNOSS
Vertical cryostat Gersemi
Double spoke cryomodule
Cold boxes

## Slide 25: Purpose
Interconnection (splices) and cooling of superconducting cables
Preliminary design, in collaboration with RFR Solutions
Courtesy of V. Parma
Courtesy of V. Parma
Courtesy of V. Parma

## Slide 26: Components
Courtesy of J. Dequaire and Y. Leclercq
The SC cable vessel
  Made of SS 316L
  Mass flow of helium below 17 K
  The design pressure is 4 bar
  Flanges : CF type
  Tube thickness : about 3 mm
Thermal shield
  Made of Al alloy or Cu alloy
  Half tube thickness : 2 mm
Courtesy of J. Dequaire and Y. Leclercq
Courtesy of J. Dequaire and Y. Leclercq
The vacuum vessel
  Made of SS (304L or 316L)
  Independently sliding parts to provide access to internal components
  Flanges : ISO-K, ISO-KF, CF type
  Tube thickness : about 6 mm

## Slide 27
THANK YOU
for your
ATTENTION

## Slide 28: Helium Vessel
The internal envelope of the DFH cryostat contains the superconducting cables in a gaseous mass flow of helium below 17 K. The design pressure is 4 bar.
The helium vessel is composed of a main vessel and several smaller vessels connected in between by flexible hoses. The smaller vessels are composed of double sleeves to allow access on either side.
Formed bellows ensures the compensation of thermal contractions
Material :
  Helium vessel : 316L (1.4404 or 1.4435)
  Bellows : 316L (1.4404 or 1.4435, Note: 316Ti not allowed)
  Flexible hoses with braids : 316L (1.4404 or 1.4435)
  Supports : Composite epoxy/glass fiber : G10
  Conflat flanges : 316LN 3D forged (CERN procurement)
  Fasteners : A4 degreased (silver plated for dedicated application)
  Conflat fasteners : A4-100 degreased
Leak tight welds :
  Welds shall be full penetration and qualified to the PED requirements
  TIG welds (141 or 142)
Flanges : CF type
Tube thickness : about 3 mm
Courtesy of J. Dequaire and Y. Leclercq

## Slide 29: Thermal Shield
Composed of three independent shields made in thermal conductive material.
Material :
  Thermal shield : Aluminum alloy to be defined or copper alloy
  Fasteners : A2, A4, Aluminum
Assembly:
  The shields must be half shelled
Half tube thickness : 2 mm
Courtesy of J. Dequaire and Y. Leclercq

## Slide 30: Equipment
Safety valves
  possible closed volumes (betwen valves)
  closed volumes (vacuum vessel)
Bellows
Cryogenic valves
  Depending on where they sit they should be thermalized
  For LHe used WEKA or VELAN
  For LN2 use SELFA
LHe level probes from American Magnetics Inc.
Temperature sensors
  From Troom to 30 K: normal Pt100
  From Troom to 1.4 K: CERNOX
Heaters for flat surfaces: thin film MINCO or OMEGA
Heaters for gas outlets: heater cartridges from VULCANIC
Cable connectors (Burndy, Lemo, etc.)