## Slide 1: FREIA Laboratory Facility for Research Instrumentation and Accelerator Development
Accelerator Development
in Uppsala
Roger Ruber
J-PARC, 6 June 2019

## Slide 2: Uppsala Accelerator History
1477: Uppsala University, oldest in Scandinavia
25'000 students, 7'000 staff
historical profiles: Linné, Rudbeck, Celsius, Ångström, Svedberg
1940's: The(odore) Svedberg builds a cyclotron
Gustaf Werner synchro-cyclotron (1947 - 2016)
  nuclear physics & oncology
CELSIUS ring (1984 - 2005)
  nuclear & particle physics
2000's: External projects
CTF3/CLIC (since 2005)
FLASH/XFEL (since 2006)
ESS (since 2009)
2010's: New ventures
FREIA laboratory (est. 2011)
Skandion clinic (est. 2015)

## Slide 3: KEK & WASA Superconducting Solenoid
1991-2006 WASA Solenoid
study rare π0 and η decays at CELSIUS
  using internal pellet target
KEK contributes ultra-thin solenoid
  1992-1996 construction & test at KEK
2006 move to Jülich (Germany)
2019 move to GSI/FAIR (Germany)
WASA (1999) T. Thörnlund
WSCS (1994)
WSCS (1993)

## Slide 4: FREIA Laboratory
cryogenics
- liquid helium
- liquid nitrogen
control room
- equipment controls
- data acquisition
radio-frequency (RF) power sources
3 bunkers
with test stands
horizontal cryostat
vertical cryostat
State-of-the-art Equipment
Facility for Research Instrumentation and Accelerator Development
Funded by KAWS, Government, Uppsala Univ.
Competent and motivated staff
collaboration of physics (IFA) and engineering (Teknikum).

## Slide 5: Accelerator Research & Development
High Intensity Proton Beams
Ultra Bright Electron Beams
SC Cavities & Magnets
RF Generation & Control
Cryogenics & Test Stands
Accelerator
Physics
Accelerator
Technology

## Slide 6
Overview of Cryogenic Test Stands
cryogenic test stands

## Slide 7: “HNOSS” Horizontal Cryostat
HNOSS = Horizontal Nugget for Operation of Superconducting Systems
Test of superconducting cavities/devices
  3240 x ø1200mm inner volume
  up to two cavities simultaneously,
  each equipped with helium tank,
Low or High power RF testing
  fundamental power coupler (top, bottom, side)
  (cold) tuning system
Operation in the range 1.8 to 4.5K.
Available as ARIES
Trans National Access Facility

## Slide 8: “Gersemi” Vertical Cryostat
Under commissioning
Test of SC cavities & magnets (<350kJ)
  3.2m x ø1.1m total volume
  2.65m x ø1.1m below lambda plate
    design includes joint for lambda plate
Three operation modes
  vacuum; liquid bath; pressurized (bath with 2K heat exchanger)
Operation in the range 1.8 to 4.5K
Available as ARIES
Trans National Access Facility
2 x 2000 A

## Slide 9
Development of High Power RF Technology
RF Generation & Control

## Slide 10: High Power RF Amplifiers
400 kW pulsed (352 MHz)
  2 stations, each 2 tetrodes TH595(A)
  3.5 ms, 14-28 Hz
  ESS prototype development
50 kW CW (352/400 MHz)
  single tetrode TH571b
1.2 MW pulsed (704 MHz)
  HV modulator & klystron test for ESS
CERN 50 kW CW

## Slide 11: Solid State RF Amplifier
Transistor Amplifier Module
single ended RF power amplifier
based on BLF188XR
1250 W and 70% efficiency
Amplifier Demonstrator
8 modules, 10.5 kW
69% efficiency
  pulsed 14 Hz, 3.5 ms (ESS)
L. Haapala et al. Electronics Letters, vol. 52, (2016) p.1552.
D. Dancila et al. IOP Conf. Series, J. Physics Conf. Series vol. 874, 2017 (012093).

## Slide 12: Low-loss Compact Combiners
Compact Cavity Combiner
352 MHz 200 kW
  12 input ports
  0.2% insertion loss
Compact Planar Combiner
352 MHz 10 kW
  8 input ports
  Gysel type
  line coupling compensates parasitic coupling
352 MHz 20 kW
  2 to 1
    2 ext. loads
  combiner/splitter
  insert.loss 0.1 dB
V. A. Goryashko et al. IEEE Microwave and wireless components Letts, vol. 28, 2018.
M. Jobs et al. IEEE Trans. Components, Packaging Manufacturing Tech., vol. 8, 2018.
L. Hoang Duc et al. J. of Engineering, 2017.
Input RF power
Output RF power

## Slide 13: FPGA Based Digital LLRF
Signal Driven
2 ADC inputs at 250 Msps
  (*) analogue bandwidth of 750 MHz
2 DAC outputs at 500 Msps
Digital downconversion to baseband 0 Hz, no analog mixers
  downconverted signal at 10 Msps or 1 Msps, selectable
undersampling to operate at any frequency from 10 to 750 MHz*
Self-excited Loop
CW or
pulsed mode
  switch closes the loop for a duration of 2.86 ms, repetition rate of 14 Hz.
Code in the FPGA

## Slide 14
Development of SRF cavities for ESS
Superconducting cavities

## Slide 15: ESS Cavities & Cryomodules
Double Spoke Cavity, 352 MHz
Prototype cavity
  without and with FPC
  RF conditioning
  Q0, gradient, fill time,
  Lorentz force detuning, microphonics
  test LLRF, SEL,
  tuner operation
  nominal gradient
Cryomodules
  prototype valve box & cryomodule
  13 series cryomodules
    Oct. 2019 – end 2020 (~6 weeks/CM)
Elliptical Cavity, 704 MHz
RF stations
  acceptance test of HV modulator for ESS local test stand
  test RF distribution (circulator, load)
Prototype high beta elliptical
  with power coupler and tuner
  RF conditioning
  Q0, gradient, fill time, heat load
  Lorentz force detuning, microphonics
  test LLRF, SEL, tuner operation

## Slide 16: Spoke Cryomodule Prototype (2019)
Warm RF conditioning
  ~3 days/cavity
  MP bands were consistent with HNOSS test
    strength depends on pulse length,
    1st/2nd conditioning…
Cold RF conditioning
  no coupler activity
  Quench during cavity conditioning at 4 K
    burst disc rupture → thermal cycling
Cavity #2 performance
  multipacting regions similar as prototype
    2-3; 4-5; 7-8 MV/m
  field emission sensitive to tuner motion or position (under investigation)
FREIA CAV2 after tuner test (2019)

## Slide 17: Spoke Cryomodule Prototype (2019)
Fast tuner performance
  Lorenz force detuning compensation (piezo)
w/o correction
w/ correction
fshift
Pfwd
Pref
Ptrans

## Slide 18
Test and Development of SC Magnets for CERN
superconducting magnets

## Slide 19: Orbit Correctors for HL-LHC
Test of nested dipole orbit corrector magnets for the High Luminosity upgrade of LHC
  magnet design and construction by CIEMAT (Spain)
  test at FREIA (20 magnets)
Parameter | Unit | Value
Aperture | mm | 150
Magnetic length | m | 1.2
Nominal integrated field | T m | 2.5
Nominal current inner | A | 1625
Nominal current outer | A | 1474
Short sample current at 1.9 K | A | 
Loadline fraction at 1.9 K |  | 
Strand diameter | mm | 0.480
Cu/no_Cu |  | 1.75
Number of turns per layer inner |  | 140
Number of turns per layer outer |  | 191
Nominal strand current density | A/mm2 | 
Nominal superconductor current density | A/mm2 | 
Nominal differential inductance inner | mH | 58.4
Nominal differential inductance outer | mH | 118.8
Nominal stored energy inner | kJ | 87
Nominal stored energy outer | kJ | 150
Maximum hotspot temp | K | 270
MCBXF

## Slide 20: Magnet Powering & Quench Monitoring
2 x 2000 A
Data acquisition
Computer
PLC Slot
Quench detection system
Patch panel
Data acquisition
slot
Computer
IGBTs based EE system

## Slide 21: CCT Magnet Development
Canted-Cosine-Theta magnet is a dipole based on the superposition of two oppositely skewed solenoids with respect to the bore axis.
  produces a perfect cosθ field,
  is cost effective compared to a conventional SC dipole
    but not the same field strength possibilities
CERN (G. Kirby)
Scanditronix (A. Ahl)

## Slide 22
CLIC, Free Electron Lasers, Ultra-fast Electron Diffraction
high brilliance electron beams
CLIC
FELs
Ultrafast Electron Diffraction

## Slide 23: RF Breakdown Studies
Models for RF conditioning process
  why the achievable gradient increases?
  why an ultimate limit in conditioning?
  strong dependence on temperature
    not many data available
  agree within range of available data
    but diverge significantly outside that range
  include temperature-dependent terms,
    can be distinguished by dedicated experiments
Dark currents
  No indication of single emitting spot inside cavity
  Broad energy spectrum
Breakdown events
  Good correlation with BD position (from RF)
  Electrons with well defined energies
  Discovered H2+ in "Flashbox" at TBTS
42 MW @ 50ns
34 MW @ 50ns

## Slide 24: Cryogenic DC Spark System
Field emission and BDR as a function of temperature
Complement to RF tests
  very high repetition rate, pulsed DC
  simple geometry (large planar electrodes)
  similar high-field behavior in RF and pulsed DC
  allows in depth studies of the fundamental physics of high-fields (e.g. material and surface science)
  possibility to find new and potentially important connections between the high-gradient NC and SC fields.
OFE-Cu electrodes
50 mm diameter
60 μm gap
Field emission at 300K and 30K
starts at higher field at 30 K
Electrodes at 30K reached almost 20% higher field gradient than at 300 K.
PRELIMINARY

## Slide 25: Soft X-ray Laser (SXL) at MAX IV
Collaboration: Uppsala, Stockholm, Lund University, KTH & MAX IV
  funding from Wallenberg foundation and universities
Uppsala is involved in
  accelerator (microbunching instability),
  FEL (short-pulse generation),
  optical beamline design.
A. Mak et al “Compact FEL at MAX IV” J. Synchrotron Rad. (2019) 26.

## Slide 26: Attosecond Pulse Generation
High-Harmonic Generation (HHG) sources are facing saturation
Undulator light source is a promising way to the attosecond region
Application submitted to the EU/H2020 program
  12 partners from Germany, Hungary, Italy, UK. Ukraine, Sweden and Japan
Read more in: A. Mak et al 2019 Rep. Prog. Phys. 82 025901
high-harmonic generation in gas

## Slide 27: CompactLight
EU funded project to design the next generation compact FEL
Consideration of costs and space: reduce linac length
  opening the way to affordable “Regional Facilities”
Uppsala:
  communication with users, specify science requirements
  definition of FEL system & accelerator/undulator requirements
  design of the soft X-ray FEL and potentially the beamline
  breakdown studies in accelerating structures
Preliminary design of the CompactLight FEL. Courtesy of N. Thompson
A. Mak et al “Science Requirements and Performance Specification for the CompactLight”, FREIA Report 2019/01.
Notes: Echo-Enabled Harmonic Generation (EEHG) is a laser assisted electron beam manipulation scheme designed to produce high-harmonics in the e-beam density distribution for the generation of short-wavelength radiation.

## Slide 28
European Spallation Source (ESS) and High Luminosity LHC (CERN)
high brilliance proton beams
ESS Superconducting Linac
HiLumi LHC
ESS Neutrino Super Beam

## Slide 29: ESS Neutrino Super Beam (ESSnuSB)
Doubling the ESS beam power for a second target
  linac duty cycle doubling to 8 % (RF sources, cooling)
    using new H- source
  accumulator ring (~400 m circ.) compress 2.86 ms beam pulse to few µs
    multi-turn injection, stripping H- → H+
  2nd target station with magnetic horn (350 kA)
    to deliver ~300 MeV neutrinos
Injection
Extraction
Collimation
RF

## Slide 30: ESSnuSB Accumulator Ring
p
p
28 Hz
28 Hz
28 Hz
Incoming beam from the linac:
for neutrons
for neutrinos
4 x 640 µs
14 Hz
1.35 kHz
After accumulation:
2.23E14 protons per pulse
4 x 1.2 µs
Switchyard
H-
p
Losses due to Lorentz stripping < 0.1 W/m ⇒
Maximum magnetic field in transfer line 0.15 T
Accumulator ring lattice and optics
384 m circumference
481 injected turns
H- stripping at injection
distributes the compressed beam pulses over four separate targets

## Slide 31: Summary
Uppsala University & FREIA Laboratory actively developing accelerator and instrumentation technology
Technology Development
NC and SC RF cavities
SC magnets
RF power generation
LLRF and controls
Physics Research
high brilliance beams
superconducting RF
RF breakdown
Academic Teaching