## Slide 1: Preparation for Series CM
Hardware:
RF stations
Doorknob
Vacuum pumping cart
Sensors and gauges: arc detector, electron pickup
Necessary cable pulling/ terminal box/cable naming/numbering
Test box
Cryogenic jumper

## Slide 2: Preparation for Series CM
RF station:
ElEctrosy:
  RF power test up to 360 kW (measured externally) in August with two different tubes (HPA1: TH595 and HPA2: TH595A)
  RF power limited by the screen grid current of 400 mA in HPA1
  Observation:
  Significant unbalance between HPA1 and HPA2, higher gain for HPA 2 than HPA1
Unnormal pulse behavior for G1 power supply
Stable maximum output for half day
One RF shunt down by unclear reason
  Maintenance:
      Try two TH595 tubes in Electrosys, the system is more balance but no improvement for the max output
      Check the G1 power supply and send back for factory diagnosis (what the latest state?)

## Slide 3: Preparation for Series CM
RF station:
DB station:
  RF power test up to 400 kW (measured internally) in May (both TH595A tubes)
  Observation:
        No fine-tune of new tube in section 2
        Stable maximum output for half day
  Maintenance:
        Fine-tune of new tube in section 2
        Adjust R8 potentiometer for section 1 to improve Vg1 of section 1 (from -176 V  around -200 V )
        Potential risk of G1 power supply

## Slide 4
Preparation for Series CM
Doorknob
Need to be dismounted before the installation of the coming series CM
When and who will take care of it?
Pumping cart
Two pumping charts are applied in the 1st series CM? Any preparation for the second cart we have? Issue solve for the first cart?
Sensors and gauges: arc detector
Cabling, adaptor, mechanical support and read gauge, PLC
Numbers of diagnostic sensors (arc detector) will be used? Mounting procedure of the arc detector support? Calibration of the pressure sensor/MKS? Second LHe level sensor to be connected to the PLC?
Necessary cable pulling/ terminal box/cable naming/numbering
Cable pulling has been done.
The terminal box is implemented base on the series CM cable logic
Cables are properly named and added into FREIA database
Loop diagram is completed (to be constantly updated) and is added in FREIA drop
PLC channels for heaters installed inside CM is documented
Test box
Will we get an official one from Orsay?
cryogenic jumper
The cryogenic jumper has been replaced before the series CM

## Slide 5: Preparation for Series CM
Software:
LLRF upgrade
LLRF2 has successfully upgraded and tested
LLRF1 upgrade is on going
CS-studio
New version of CSS and new LLRF interface are in place
EPICS
New PVs are defined based on the series CM PID scheme
Labview test interface upgrade
All Labview interface are modified based on the new PVs
Quench detection has been integrated into both test interfaces
Tuner/piezo control program
Need to be tested under the new CS-studio version
Readout of shock sensors
Need to be checked with Orsay

## Slide 6
Central cavity frequency
Loaded Q
Steady heat load
Dynamic heat load for both cavities from 8 to 12 MV/m
Q0 (calorimetric measurement) high than 1.5 e 9 at 9MV/m
Reach gradient of 12 MV/m
Tuning range of the slow step tuner
Frequency shift due to cool down
Stabilization of the cavity field with LLRF using both RF and piezo tuner compensation
Stabilization of the CM for long-term operation
Onset and level of field emission
Multipacting
The list of minimun tests in some order of priority

## Slide 7: To do list
number | item | Person in charge
1 | Get back and install G1 power supply for Electrosys | Rolf, Tord
2 | Test DB and Electrosys station to full power | Rolf, Tord, Han, Micheal
2 | Ask for shock senor reader preparation, test box, documentation | Roger
3 | Tuner control software validation | Kjell
4 | Dismount of doorknob | Lars
5 | Validation of vacuum pumping cart | Lars
6 | Overall check with the LLRF/software | Han, Tor, Kjell
7 | Cryogenic procedure | Lars, Esat
Before CM arrival:

## Slide 8: To do list
number | item | Person in charge
1 | Readout information of shock sensor and vacuum | Akira, Han
2 | Visual checking of CM | Han, Akira
3 | Cavity frequency at room temperature | Han
4 | Sensor/cable continuity (test box) | Akira
5 | FPC and doorknob installation | Lars
6 | Vacuum pumping system installation | Lars
7 | Calibration of the pressure sensors/MKS | Konrad
After CM arrival:
Anything else?