## Slide 1: Preparation for Series CM
Hardware:
RF stations
Doorknob
Vacuum pumping cart
Sensors and gauges: arc detector, electron pickup
Necessary cable pulling/ terminal box/cable naming/numbering
Test box
Cryogenic jumper

## Slide 2: Preparation for Series CM
RF station:
ElEctrosy:
  We got back of the G1 power supply and installed in the HPA1. Also, related modification has been down for HPA2.
  RF power test up to 380 kW (measured internally & at the load)
  Observation:
  RF output limited by the pre-amplifier
  A capacitor installed in the G2 circuit which might be a challenge for PID operation

## Slide 3: Preparation for Series CM
RF station:
DB station:
  RF power test up to 400 kW (measured internally) & about 360 kW (measure at the load)
  Observation:
        Water conductivity issue in section A -> put shielding for the cable
        PLC disconnection

## Slide 4: Preparation for Series CM
Software:
LLRF upgrade
PID mode of LLRF2 is not fully functioning
Problem has been report to ESS

## Slide 5: To do list
number | item | Person in charge | status
1 | Get back and install G1 power supply for Electrosys | Rolf, Tord | close
2 | Test DB and Electrosys station to full power | Rolf, Tord, Han, Michael | On going
2 | Ask for shock senor reader preparation, test box, documentation | Roger | opening
3 | Tuner control software validation | Kjell | opening
4 | Dismount of doorknob | Lars | opening
5 | Validation of vacuum pumping cart | Lars | On going
6 | Overall check with the LLRF/software | Han, Tor, Kjell | opening
7 | Cryogenic procedure | Lars, Esat | opening
8 | Test documentation | Han | close
Before CM arrival:

## Slide 6: To do list
number | item | Person in charge
1 | Readout information of shock sensor and vacuum | Akira, Han
2 | Visual checking of CM | Han, Akira
3 | Cavity frequency at room temperature | Han
4 | Sensor/cable continuity (test box) | Akira
5 | FPC and doorknob installation | Lars
6 | Vacuum pumping system installation | Lars
7 | Calibration of the pressure sensors/MKS | Konrad
After CM arrival: